## Slide 1: HydroShare: Advancing Collaboration through Hydrologic Data and Model Sharing
David Tarboton, Ray Idaszak, Jeffery Horsburgh, Dan Ames, Jon Goodall, Larry Band, Venkatesh Merwade, Alva Couch, Jennifer Arrigo, Rick Hooper, David Valentine, David Maidment, Jeff Heard, Pabitra Dash, Tian Gan, Tony Castronova, Stephen Jackson, Cuyler Frisby, Stephanie Mills, Brian Miles
http://www.hydroshare.org
OCI-1148453
OCI-1148090
2012-2017
USU, RENCI, BYU, UNC, UVA, CUAHSI, Tufts, Texas, Purdue, SDSC

## Slide 2: Research Areas
Hydrologic Information Systems
Digital Elevation Model Terrain Analysis
Hydrology and Geomorphology
Distributed Hydrologic Modeling
Snowmelt Hydrology
Non parametric stochastic hydrology
Streamflow regimes for stream ecology
The Great Salt Lake
Data
Catalog
Desktop
Server
Metadata
Search
ODM, WaterML

## Slide 3: Outline
Hydrologic data and computational challenges
Hydrologic Terrain Analysis (TauDEM -> CyberGIS)
CUAHSI HIS Services-Oriented Architecture
  Standards for hydrologic data storage and exchange
  Catalog for data discovery
  Integration of information from multiple sources
HydroShare
  Collaborative data analysis and publication
  Collaborative integrated modeling
  Architecture (Resource Centric Paradigm)
  Resource Data Model
  Functionality (to be) developed

## Slide 4: Hydrologic Data Challenges
From dispersed federal agencies
From investigators collected for different purposes
Different formats
  Points
  Lines
  Polygons
  Fields
  Time Series
Rainfall and Meteorology
Water quantity
Soil water
Groundwater
Water quality
GIS
Data Heterogeneity

## Slide 5
What proportion of your research time do you spend on preparing or preprocessing data into appropriate forms needed for research purposes?
http://his.cuahsi.org/documents/HISStatusSept15.pdf
Chart: 
| < 10 % | 10-25 % | 25-50 % | 50-75 % | > 75 % None
 | 18.6 | 45.7 | 24.3 | 11.4 | 0
Notes: Surveys of the hydrology community have indicated that data gathering and preprocessing is an inordinate fraction of the time required for modeling and analysis
In hydrology most of the easy single site, single variable, low hanging fruit research problems are solved and advances in understanding and better predictions require
combining information from multiple sources,
sharing and collaboration
Easier access to advanced computational capability
Sustainability and reliability in software

## Slide 6: A digital divide
Big Data and HPC
Researchers
Experimentalists
Modelers
awk
grep
vi
#PBS -l nodes=4:ppn=8
mpiexec
chmod
#!/bin/bash
Do you have the access or know how to take advantage of advanced computing capability?
Gateways, Web Interfaces, Software services

## Slide 7: TauDEM is software for deriving Hydrologically Useful Information from Digital Elevation Models
Raw DEM
Pit Removal
Flow Field
Flow Related Terrain Information
Notes: This slide shows the general model for deriving flow field related derivative surfaces from digital elevation data. The input is a raw digital elevation model, generally elevation values on a grid. This is basic information used to derive further hydrology related spatial fields that enrich the information content of this basic data. The first step is to remove sinks, either by filling, or carving. Then a flow field is defined. This enables the calculation of flow related terrain information.

## Slide 8: The challenge of increasing Digital Elevation Model (DEM) resolution
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2
e.g. 50,000 km2
Watershed
27 MB
240 MB
2 GB
200 GB

## Slide 9: Parallel Pit Filling
Initialize( D,P) Do for all i in P if D(i) > n P(i) ← D(i) Else P(i) ← n endfor Send( topRow, rank-1 ) Send( bottomRow, rank+1 ) Recv( rowBelow, rank+1 ) Recv( rowAbove, rank-1 ) Until P is not modified
D denotes the original elevation.
P denotes the pit filled elevation.
n denotes lowest neighboring elevation
i denotes the cell being evaluated
Communicate
Init.
1st Pass
2nd Pass
Parallel extension of: Planchon, O., and F. Darboux (2001), A fast, simple and versatile algorithm to fill the depressions of digital elevation models, Catena(46), 159-176.

## Slide 10
Can we deliver GIS functionality in general, and TauDEM specifically, as a service over the web
Data Sources
Functions and Tools
Server
Software as a Service
Users
Based on slide from Norm Jones

## Slide 12: Select the products you want
The wizard configures the sequence of functions to run to get the result

## Slide 13: The job progresses through the system
Analysis submitted
Analysis running
Results data created
Results Ready

## Slide 14: Results displayed in browser

## Slide 15
http://www.cuahsi.org
What is CUAHSI?
Support
EAR 0753521
(as of January 2013)
109 US University members
7 affiliate members
20 International affiliate members
3 corporate members
provides community and research support services to advance water research

## Slide 16: CUAHSI HIS
HydroServer – Data Publication
Lake Powell Inflow and Storage
HydroDesktop – Data Access and Analysis
HydroDesktop – Combining multiple data sources
HydroCatalog
Data Discovery
The CUAHSI Hydrologic Information System (HIS) is an internet based system to support the sharing of hydrologic data. It is comprised of hydrologic databases and servers connected through web services as well as software for data publication, discovery and access.

## Slide 17
Data Searching – What we used to have to do
NWIS
NARR
NAWQA
NAM-12
request
request
request
request
request
request
request
request
return
return
return
return
return
return
return
return
Searching each data source separately
Slide: Michael Piasecki, Drexel University
Notes: 17

## Slide 18
What CUAHSI HIS enables
Searching all data sources collectively
NWIS
NAWQA
NARR
generic
request
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
ODM
Slide: Michael Piasecki, Drexel University
Notes: 18

## Slide 19: CUAHSI Hydrologic Information System: A Services-Oriented Architecture Based System for Sharing Hydrologic Data
Data Discovery and Integration
Data Publication
Data Analysis and Synthesis
HydroCatalog
HydroDesktop
HydroServer
Data Services
Metadata Services
Search Services
WaterML, Other OGC Standards

## Slide 20
Set of query functions
Returns data in WaterML
WaterML and WaterOneFlow
WaterML is an XML language for communicating water data
WaterOneFlow is a set of web services based on WaterML
GetSites
WaterOneFlow
Web Service
GetValues
GetSiteInfo
GetVariableInfo
Notes: 20

## Slide 21
http://www.opengeospatial.org/standards/waterml
Open Geospatial Consortium Web Service Standards
This document is an OGC® Encoding Standard for the representation of hydrological observations data with a specific focus on time series structures.
These standards have been developed over the past 10 years …. by 400 companies and agencies ....

## Slide 22: HydroDesktop
Uses EPA WATERS Web, Mapping, and Database Services at http://www.epa.gov/waters/geoservices/index.html to delineate Watersheds
An open source
dotSpatial GIS based desktop client that supports discovery and analysis of hydrologic observations data
Notes: The service URLs that the HD tool uses are seen in http://hydrodesktop.codeplex.com/SourceControl/changeset/view/475b15a84bf4#Source%2fEPADelineation%2fCallWebService.cs The HD tool uses the Point Indexing Service to find the nearest NHD reach to where the user clicked. This returns a location on that reach. This point location is then used as input to the Navigation Delineation Service to get the watershed, and the Upstream/Downstream Service to get the river lines. The delineation service has two limitations: * It only works up to a certain distance upstream. I think we have it set to 100km. So for large watersheds (those with more than 100km of stream length upstream of where the user clicked), we don't get the most upstream portions of the watershed. * It doesn't delineate exactly to where the user clicked. It delineates to the endpoint of the NHD reach. (Can't remember if it is the clicked reach or the upstream reach -- try it and see.)

## Slide 23
Search last 22 years for all data in buffer around watershed

## Slide 24: Download and Plot the Data
Combining information from multiple sources

## Slide 25: Perform an analysis using R
At your fingertips
the full analysis capability of R
data from multiple sources
accessed from distributed (cloud) resources.
importance of interoperability

## Slide 26: CUAHSI HIS: A common window on water observations data for the United States unlike any that has existed before
Storage in a community data model
Publication from a server
Data access through internet-based services using consistent language and format
Tools for access and analysis
Discovery through thematic and geographic search functionality
Integrated modeling and analysis combining information from multiple sources
Server
Desktop
Catalog

## Slide 27: But
Publishing data using CUAHSI HIS requires access to or setting up a HydroServer
Accessing data requires HydroDesktop
Generally limited to time series at a point
Server
Desktop
Catalog

## Slide 28
Enable more rapid advances in hydrologic understanding through collaborative data sharing, analysis and modeling
Data
Analysis
Models
http://www.hydroshare.org
USU, RENCI, BYU, UNC, UVA, CUAHSI, Tufts,, Texas, Purdue, SDSC

## Slide 29: What is (will) HydroShare (be)?
HydroShare will be a community collaboration website that enables users to easily discover and access data and models, retrieve them to a desktop computer or perform analyses in a distributed computing environment that includes grid, cloud, or high performance computing model instances as necessary.
Understanding will be advanced through the ability to integrate information from multiple sources.
Outcomes (data, results, models) can then be published as new resources that can be shared with collaborators.
Data
Analysis
Models
Our goal is to make sharing of hydrologic data and models as easy as sharing videos on YouTube or shopping on Amazon.

## Slide 30: Collaborative data analysis and publication use case
Observers and instruments
Data
Analysis
Models
Collaboration
HydroServer (ODM)
1
2
Observe
Publish and Catalog
3
Discover and Analyze/Model (in Desktop or Cloud)
CUAHSI Water Data Center
Publication, Archival, Curation

## Slide 31
Observers and instruments
Data
Analysis
Models
Collaboration
Share the results (Data and Models)
HydroShare resource
store
4
Collaborative data analysis and publication use case
CUAHSI Water Data Center
Publication, Archival, Curation

## Slide 32: Collaborative data analysis and publication use case
Observers and instruments
Data
Analysis
Models
Collaboration
Group Collaboration using HydroShare
Preparation of a paper
5
6
CUAHSI Water Data Center
Publication, Archival, Curation

## Slide 33: Collaborative data analysis and publication use case
Observers and instruments
Data
Analysis
Models
Collaboration
Submittal of paper, review, archival of electronic paper with data, methods and workflow
7
CUAHSI Water Data Center
Publication, Archival, Curation

## Slide 34: Collaborative Integrated Modeling Use Case
Data: Links to national and global data sets of essential terrestrial variables (e.g. NASA NEX, HydroTerre)
Tools to preprocess and configure inputs (EcoHydroLib, TauDEM, CyberGIS)
Preconfigured models and modeling systems as services (SWATShare)
Standards for information exchange for interoperability (OpenMI, CSDMS BMI)
Tools for visualization and analysis
x
y
t
Flow
Time
Flow
Time
Time
P
Pre-processing and model linking
Modeling Services (e.g. SWATShare)
Notes: Data: Links to national and global data sets of essential terrestrial variables (e.g. NASA NEX, HydroTerre)
Tools to preprocess and configure inputs
Preconfigured models and modeling systems as services
Standards for information exchange for interoperability (OpenMI, CSDMS BMI)
Tools for Visualization and Analysis
Automated reasoning to couple models based on purpose, context, data and resources

## Slide 35: Definition of Data
In OMB Circular A-110 research data is defined as “recorded factual material commonly accepted in the scientific community as necessary to validate research findings, but not any of the following: preliminary analyses, drafts of scientific papers, plans for future research, peer reviews, or communications with colleagues.”
Validating research findings may involve
Observations and measurements
Models, code and scripts
Simulation results
HydroShare resources need to accommodate all these types of “data”

## Slide 36: Resource Repository Centric Paradigm for Modeling and Analysis
Analysis Tools
Visualization Tools
Data Loaders
Data Discovery Tools
Models
Resource Repository
Each model interacts with information in the common data store
The modeler does not need to be concerned with and can take advantage of standardized analysis, visualization loading and discovery tools
Enable multiple models to use common “best practice” tools

## Slide 37: Resource Data Model
Open Archives Initiative – Object Reuse and Exchange (OAI-ORE) - standards for the description and exchange of aggregations of Web resources
BagIt – hierarchical file packaging format designed to support disk-based or network-based storage and transfer of generalized digital content
Compatible with DataOne

## Slide 38: Types of data to support as resources
Resource Types
Generic 
Time Series (CUAHSI HIS)
Geographic feature set
Geographic Raster
Referenced HIS time series
Multidimensional Space Time dataset
River geometry
Sample based observations (ODM2 and CZO)
Documents
Tabular objects
HydroDesktop Project package
Scripts
Models
Model Components
Referenced data sets from other (non HIS) sources.
Tools
Uploaders to facilitate loading of resources
Viewers to visualize the resource
Exporters to download the resource
Best practice tools for hydrologic data preprocessing and analysis
Resource Data Model.
Data and metadata content
Logical relationships
File formats

## Slide 39: Multidimensional Space Time Resource Type
x
y
t
Time Series Resource Type
NetCDF
ODM/WaterML

## Slide 40
Representing River Geometry in HydroShare
Hydraulic Calculations
LiDAR
Cross Sections
Cross Sections Attached to River Network

## Slide 41: Models
Model package
  Bundled components
  references existing resources
Model program
  executable entity
  may consist of submodules and other complex relationships
Model input
  input required by a program
  files, parameters, etc...
Model output
  outputs produced by a program
  files, plots, etc...

## Slide 42: Model Execution in HydroShare
Package
Input and output Hydroshare resources
Link input, output, and program resources to create model packages
Execution of model package within the HydroShare environment to create "new" resources
Program
Input
Program
Input
Package
Output
EXECUTE
Output
CREATE OUTPUT
CREATE PACKAGE

## Slide 43: SWATShare

## Slide 44
RHESSys ecohydrology data preparation workflow
Manual workflows
Workflow framework
Common across many models
Notes: Explain what pieces have been implemented as iRODS rules.
Explain what iRODS is.

## Slide 45: Architecture Outline
Users
Browser
Client
HydroShare
Web Services (REST API)
Web Pages

## Slide 46: Architecture
Users
Browser
Client (HydroDesktop)
iRODS “Network File System”
Content
Resource Files
Resource Science Metadata
User Accounts
Functionality
Authentication and Authorization Infrastructure (AAI) for Access Control
Discovery (using e.g. ElasticSearch via MSVC plugin)
Web Tools
Web Services (HydroShare REST API)
Django web application framework
Web Pages
iRODS Native REST API
3rd party clients, interoperable systems and web tools
Connection point for partners
BiG CZ SSI
CI-WATER
SEAD
CyberGIS
SESYNC GI Venture
Compute Engines (Docker or HPC)

## Slide 49: Sharing and collaboration

## Slide 50: Summary
A new, web-based system for advancing model and data sharing
Sharing features to HydroDesktop
Access more types of hydrologic data using standards compliant data formats and interfaces
Enhance catalog functionality that broadens discovery functionality to different data types
New model sharing and discovery functionality
Facilitate and ease access to use of high performance computing
New social media and collaboration functionality
Links to other data and modeling systems

## Slide 51: Thanks to the HydroShare team!
  USU
  RENCI/UNC
  CUAHSI
  BYU
  Tufts
  UVA
  Texas
  Purdue
  SDSC
http://hydroshare.cuahsi.org
OCI-1148453
OCI-1148090
2012-2017
Notes: The HydroShare project is part of a broad effort in CUAHSI in the area of Hydrologic Information Systems. We have a team of developers and domain scientists from eight universities working on HydroShare. This is part of the even broader focus in NSF on data management, Cyberinfrastructure and sustainable software.