## Slide 1
The figure shows a sample from an unconfined aquifer. L=50 cm, Diameter = 6 cm. The sample is tested for 3 min under constant head difference of 16.3 cm. 45.2 cm3 of water is collected at the outlet.
Determine the hydraulic conductivity of the sample
Determine the average interstitial velocity assuming a porosity of 0.3
Determine the Reynolds number assuming an effective grain size (d10) of 0.037 cm
From Mays, 2011, Ground and Surface Water Hydrology

## Slide 2: Water Viscosity at different temperatures
From http://www.engineeringtoolbox.com/water-dynamic-kinematic-viscosity-d_596.html

## Slide 3
Parallel conduit conceptual model for porous media flow.
vi
Ai
A
Intrinsic Permeability

## Slide 4
Range of values of Hydraulic Conductivity
From Mays, 2011, Ground and Surface Water Hydrology

## Slide 5
Constant Head Permeameter
From Mays, 2011, Ground and Surface Water Hydrology

## Slide 6
Falling Head Permeameter
From Mays, 2011, Ground and Surface Water Hydrology
A 20-cm long sample of silty fine sand with diameter of 10 cm is tested. The falling head tube has a diameter of 3 cm and the initial head is 8 cm. Over a period of 8 hr, the head in the tube falls to 1 cm. Estimate the hydraulic conductivity.