## Slide 1: Terrain Analysis Using Digital Elevation Models (TauDEM)
Learning Objectives
To be able to delineate watersheds as the basic hydrologic model elements from Digital Elevation Models using Geographic Information Systems tools and to use this information in Hydrologic Analyses
  TauDEM
  Raster Calculation

## Slide 2: Topography defines watersheds which are fundamentally the most basic hydrologic landscape elements.

## Slide 3: The starting point: a grid digital elevation model (DEM)
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 4: Deriving hydrologically useful information from Digital Elevation Models
Raw DEM
Pit Removal (Filling)
Flow Field
Flow Related Terrain Information
Notes: This slide shows the general model for deriving flow field related derivative surfaces from digital elevation data. The input is a raw digital elevation model, generally elevation values on a grid. This is basic information used to derive further hydrology related spatial fields that enrich the information content of this basic data. The first step is to remove sinks, either by filling, or carving. Then a flow field is defined. This enables the calculation of flow related terrain information. My focus has been on flow related information working within this framework. I try to leave other GIS functionality, like radiation exposure, line of sight analyses and visualization to others. I have distributed my software in ways that it easily plugs in to mainstream systems, such as ArcGIS to enhance ease of use.

## Slide 5: The Pit Removal Problem
DEM creation results in artificial pits in the landscape
A pit is a set of one or more cells which has no downstream cells around it
Unless these pits are removed they become sinks and isolate portions of the watershed
Pit removal is first thing done with a DEM

## Slide 6: Pit Filling
Increase elevation to the pour point elevation until the pit drains to a neighbor

## Slide 7: Pit Filling
Pits
Pour Points
Original DEM
Pits Filled
Notes: Elevations are filled to that of the pools pour point

## Slide 8
80
74
63
69
67
56
60
52
48
30
4
5
6
3
7
2
1
8
D8 Flow Direction Model
- Direction of steepest descent
Slope = Drop/Distance
Steepest down slope direction

## Slide 9
Grid Network

## Slide 10
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
2
5
15
20
2
The area draining each grid cell includes the grid cell itself.
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
5
2
2
20
15
Contributing Area (Flow Accumulation)

## Slide 11: Stream Definition
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
2
5
15
20
2
Flow Accumulation > 10 Cell Threshold
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
2
1
5
2
2
11
15
20
Stream Network for 10 cell Threshold Drainage Area

## Slide 12
Watershed Draining to Outlet

## Slide 13: Watershed and Stream Grids

## Slide 14: DEM Delineated Catchments and Stream Networks
For every stream segment, there is a corresponding catchment
Catchments are a tessellation of the landscape
Based on the D8 flow direction model

## Slide 15: TauDEM Channel Network and Watershed Delineation Software
Stream and watershed delineation
Multiple flow direction flow field
Calculation of flow based derivative surfaces
Deployed as an ArcGIS Toolbox with tools that drive accompanying command line executables, available from http://hydrology.usu.edu/taudem/

## Slide 16: ArcMap

## Slide 17: Default file name suffixes
For complete list see: http://hydrology.usu.edu/taudem/taudem5.0/TauDEM_Tools.chm

## Slide 18: Illustrative Use Case: Delineation of channels and watersheds using a constant support area threshold
Steps
Pit Remove
D8 Flow Directions
D8 Contributing Area
Stream Definition by Threshold
Stream Reach and Watershed

## Slide 19: Pit Remove

## Slide 20: D8 Contributing Area

## Slide 21: Stream Definition by Threshold

## Slide 22: Stream Reach and Watershed

## Slide 23: D-Infinity multiple flow direction model for representation of flow field in a DEM
D
D8
67
56
52
48
Steepest single direction
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.)
Notes: This slide shows how the terrain flow field is represented. Early DEM work used a single flow direction model, D8. In 1997 I published the Dinfinity method that proportions flow from each grid cell among downslope neighbors. This, at the expense of some dispersion, allows a better approximation of flow across surfaces.

## Slide 24: D-Infinity Slope, Flow Direction and Contributing Area

## Slide 25
D8
Contributing Area
D
<1 ha
1-4 ha
4-8 ha
>8 ha

## Slide 26: Wetness Index
Slope (S)
Specific Catchment Area (a)
Wetness Index ln(a/S)

## Slide 27: Edge contamination
Edge contamination arises due to the possibility that a contributing area value may be underestimated due to grid cells outside of the domain not being counted. This occurs when drainage is inwards from the boundaries or areas with no data values. The algorithm recognizes this and reports "no data" resulting in streaks of "no data" values extending inwards from boundaries along flow paths that enter the domain at a boundary.

## Slide 28: Summary Concepts
The GIS grid based terrain flow data model enables the representation of flow processes at and near the earth surface and derivation of a wide variety of information useful for the study of hydrologic processes.
  Slope
  Flow direction
  Drainage area
  Catchments, watersheds and channel networks
  Multiple other flow related quantities
Edge contamination checking important to ensure that results are not impacted by area outside the domain of the DEM analyzed

## Slide 29: Terrain Analysis Using Digital Elevation Models (TauDEM)
Readings
Tarboton, D. G., R. L. Bras and I. Rodriguez-Iturbe, (1991), "On the Extraction of Channel Networks from Digital Elevation Data," Hydrologic Processes, 5(1): 81-100. http://www.neng.usu.edu/cee/faculty/dtarb/hp91.pdf
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319. http://www.neng.usu.edu/cee/faculty/dtarb/96wr03137.pdf
Tarboton, D. G., K. A. T. Schreuders, D. W. Watson and M. E. Baker, (2009), "Generalized terrain-based flow analysis of digital elevation models," 18th World IMACS Congress and MODSIM09 International Congress on Modelling and Simulation, ed. R. S. Anderssen, R. D. Braddock and L. T. H. Newham, Modelling and Simulation Society of Australia and New Zealand and International Association for Mathematics and Computers in Simulation, July 2009, p.2000-2006, http://www.mssanz.org.au/modsim09/F4/tarboton_F4.pdf.