## Slide 1: TOPMODEL and the role of topography and variable contributing areas in runoff production
Learning objectives
Be able to define and compute the topographic wetness index and describe its role and use in TOPMODEL runoff calculations
Be able to use TOPMODEL principles to calculate the spatial distribution of soil moisture deficit and use this information in the calculation of runoff using appropriate GIS tools

## Slide 2: TOPMODEL
Beven, K., R. Lamb, P. Quinn, R. Romanowicz and J. Freer, (1995), "TOPMODEL," Chapter 18 in Computer Models of Watershed Hydrology, Edited by V. P. Singh, Water Resources Publications, Highlands Ranch, Colorado, p.627-668.
“TOPMODEL is not a hydrological modeling package. It is rather a set of conceptual tools that can be used to reproduce the hydrological behaviour of catchments in a distributed or semi-distributed way, in particular the dynamics of surface or subsurface contributing areas.”

## Slide 3: Hydrological processes within a catchment are complex, involving:
Macropores
Heterogeneity
Fingering flow
Local pockets of saturation
However:
The general tendency of water to flow downhill is however subject to macroscale conceptualization
Hydraulic conductivity tends to decrease with depth

## Slide 4: TOPMODEL Key Ideas
Surface saturation and soil moisture deficits based on topography
  Slope
  Specific Catchment Area
  Topographic Convergence
Partial contributing area concept
Saturation from below (Dunne) runoff generation mechanism
Map of saturated areas showing expansion during a single rainstorm. The solid black shows the saturated area at the beginning of the rain; the lightly shaded area is saturated by the end of the storm and is the area over which the water table had risen to the ground surface. [from Dunne and Leopold, 1978]

## Slide 5: Specific catchment area a is the upslope area per unit contour length [m2/m  m]
Upslope contributing area a
Stream line
Contour line
Topographic Definition

## Slide 6: Topmodel - Assumptions
The soil profile at each point has a finite capacity to transport water laterally downslope.
Hydraulic conductivity decreases exponentially (as a rough macroscale approximation)
Hydraulic gradient approximated by topographic slope
S
zw
z
K
Units
z m T m2/hr f m-1
K m/hr S dimensionless q m2/hr = m3/hr/m

## Slide 7: Topmodel - Assumptions
Drainage of saturated zone supports baseflow
Dynamics of saturated zone approximated by successive steady state representations
Recharge rate spatially homogeneous
The actual lateral discharge is proportional to specific catchment area.
Specific catchment area a [m2/m  m]
(per unit contour length)
S
zw
R is proportionality constant that may be interpreted as “steady state” recharge rate, or “steady state” per unit area contribution to baseflow.
a
R
q

## Slide 8
Soil moisture deficit at a point and depth to water table is determined by equating topographic and profile q and solving for zw
Specific catchment area a [m2/m  m]
(per unit coutour length)
Saturation when zw<0.
i.e.
Topmodel – Local depth to water table
S
zw
q

## Slide 9
Specific catchment area a [m2/m  m]
(per unit coutour length)
D=ezw m= e/f
S
zw
q
D= ezw
Topmodel – Local soil moisture deficit
Points with equivalent topographic wetness index respond similarly in terms of runoff generation
Define

## Slide 10
Specific catchment area a [m2/m  m]
(per unit coutour length)
S
zw
q
D= ezw
Topmodel – Spatial Averages

## Slide 11
Local soil moisture deficit a function of average soil moisture deficit and topographic wetness index
Average soil moisture deficit a function of streamflow (baseflow) and watershed drainage parameters
Enables spatial modeling of runoff generation from topography and aggregate watershed properties
Specific catchment area a [m2/m  m]
(per unit coutour length)
S
zw
q
D= ezw
Topmodel - Summary

## Slide 12
Topographic variability for runoff generation summarized by distribution of wetness index expressed as a histogram
Specific catchment area a [m2/m  m]
(per unit coutour length)
S
zw
q
D= ezw
Topmodel – Wetness Index Histogram
saturated
Increasing D
Drainage
Recharge

## Slide 13: TOPMODEL and GIS
Surface saturation and soil moisture deficits based on topography
  Slope
  Specific Catchment Area
  Topographic Convergence

## Slide 14: Topographic Slope
?
Topographic Definition Drop/Distance
Limitation imposed by 8 grid directions.

## Slide 15
Numerical Evaluation with the D Algorithm
Upslope contributing area a
Stream line
Contour line
Specific catchment area a is the upslope area per unit contour length [m2/m  m]
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.) (http://www.engineering.usu.edu/cee/faculty/dtarb/dinf.pdf)

## Slide 16
Contributing Area using D8
Contributing Area using D

## Slide 17
Slope
Specific Catchment Area
Wetness Index ln(a/S)
from Map Calculator.
Average, l = 6.9

## Slide 18: Numerical Example
Given
Ko=10 m/hr
f=5 m-1
Qb = 0.8 m3/s
A (from GIS)
ne = 0.2
Raster calculator -( [ln(sca/S)] - 6.9)/5+0.46
Compute
R=0.0002 m/h
l=6.9
T=2 m2/hr

## Slide 19: Calculating Runoff from 25 mm Rainstorm
Flat area’s and z <= 0
  Area fraction (81 + 1246)/15893=8.3%
  All rainfall ( 25 mm) is runoff
0 < z  rainfall/effective porosity = 0.025/0.2 = 0.125 m
  Area fraction 546/15893 = 3.4%
  Runoff is P-z*0.2
  (1 / [Sat_during_rain ]) * (0.025 - (0.2 * [z]))
  Mean runoff 0.0113 m =11.3 mm
z > 0.125 m
  Area fraction 14020/15893 = 88.2 %
  All rainfall infiltrates
Area Average runoff
  11.3 * 0.025 + 25 * 0.083 = 2.47 mm
  Volume = 0.00247 * 15893 * 30 * 30 = 35410 m3