## Slide 1: Using Digital Elevation Model Derived Height Above the Nearest Drainage for flood inundation mapping and determining river hydraulic geometry
David Tarboton1, Xing Zheng2, David Maidment2, Yan Liu3, Shaowen Wang3
1. Utah State University, dtarb@usu.edu
2. University of Texas at Austin, 3. University of Illinois

## Slide 2: Outline
Overview
Calculating height above the nearest drainage (HAND) from a Digital Elevation Model
Using HAND to map flood inundation for stream reach catchments
Using HAND to determine stream reach hydraulic properties
Further considerations

## Slide 3: Flooding occurs when Water Depth is greater than Height Above Nearest Drainage (HAND)
Height Above
Nearest Drainage
(HAND)
Address Point
Flood Depth
Normal Depth
Stream Bed
May be used to determine flood risk
Slide from David Maidment

## Slide 4
National Water Model Discharge Forecast Across the Continental US
(Operational by National Weather Service in August 2016)
Slide from David Maidment

## Slide 5
Discharge
Depth
Inundation
Impact
Transform discharge to depth by rating curve or hydraulic model
Create flood inundation map from water depth
Assess impact on people and property
Take discharge forecast from the National Water Model
Flood emergency response depends on assessment of impact
Flood Inundation Mapping
Slide from David Maidment

## Slide 6: Implementation in GIS
Each stream reach has a discharge
Each stream reach has a water depth calculated from discharge, hw
Each stream reach has a unique ID
Each catchment has a unique ID for the reach to which it drains
Each grid cell has the ID of the catchment it is in (reach it drains to) and height above the nearest drainage, hd
Evaluate inundation using
    if(hw(id) > hd(id))
      Inundation depth = hw(id) - hd(id)
    else
      Inundation depth = 0
Streams
Catchments
Height above drainage (relative elevation of land surface cell above cell in stream to which it flows)
Inundation map
Reach Scale Flood Depth
Comid | Depth (ft)
5781365 | 8
5781381 | 9
5781405 | 10
5781401 | 15
5781399 | 14
5781383 | 12
5781933 | 11

## Slide 7
Information Model for Flood Mapping
NHDPlus Flowline and Catchment
Q
t
NWM Forecast
River Segment with unique ID
River Geometry
Q
H
Rating Curve
Lidar-HAND (GeoFlood)
HEC-RAS
NED-HAND
Flood Map Library
Real-time
Inundation Extent
Slide from Xing Zheng

## Slide 8: Reach based height above nearest drainage flood map example
hw=8 ft
hw=9 ft
hw=11 ft
hw=12 ft
hw=14 ft
hw=10 ft
hw=15 ft
This is approximate because it neglects many details of the river hydraulics and flow over flood plains. But more detailed approaches often demand hard to obtain and uncertain inputs so this may be a helpful approach to get screening level and real time flood maps
Premised on good elevation model and consistent stream raster

## Slide 9
Video from Xing Zheng

## Slide 10: Outline
Overview
Calculating height above the nearest drainage (HAND) from a Digital Elevation Model
Using HAND to map flood inundation for stream reach catchments
Using HAND to determine stream reach hydraulic properties
Further considerations

## Slide 11
D
D8
67
56
52
48
Steepest single direction
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.
Calculation of HAND from a Digital Elevation Model (DEM)
D8
D
Notes: This slide shows how the terrain flow field is represented. Early DEM work used a single flow direction model, D8. In 1997 I published the Dinfinity method that proportions flow from each grid cell among downslope neighbors. This, at the expense of some dispersion, allows a better approximation of flow across surfaces.

## Slide 12: HAND evaluated using TauDEM Dinfinity Vertical Distance Down function
D
Tesfa, T. K., D. G. Tarboton, D. W. Watson, K. A. T. Schreuders, M. E. Baker and R. M. Wallace, (2011), "Extraction of hydrological proximity measures from DEMs using parallel processing," Environmental Modelling & Software, 26(12): 1696-1709, http://dx.doi.org/10.1016/j.envsoft.2011.07.018.
hs
hr
Ridge
pr
ps
ss
sr
hs
hr
vr
vs
Stream
pr
ps
ss
sr
Point of interest
TauDEM Vertical Distance Down a special case of a general hydrological proximity measure
Vertical distance to stream evaluated as weighted average over multiple flow paths. This results in a “smooth” height above nearest drainage layer
D

## Slide 13: TauDEM model for vertical drop to stream (aka HAND)
i
Pik
Pik

## Slide 14: HAND Algorithm
0
0
0
0
0
0
0
Set h=0 along streams (target input set)
Mark remaining grid cells as “ready” if all down results are available and “not ready” if down results not yet computed
For a “ready” cell find its flow direction and elevation differences to down cells
Calculate h using weighted average
= 0.99
==0.92
==1.13
0.99

## Slide 15: HAND Algorithm Continued
0
0
0
0
0
0
0
Evaluate up cells when they become “ready”
= 4.88
==2.1
==2.74
0.99
0.95
2.64
1.88
4.88

## Slide 16: Result
Elevation z (m)
HAND h (m)
435.56
436.01
436.44
0
0
0
0.99
0.92
2.64
1.88
436.47
437.49
439.20
437.15
438.65
436.48
438.13
440.22
0.71
2.20
3.31
4.68

## Slide 17: HAND from TauDEM for Onion Creek near Austin Texas
1/3 arc second NED DEM

## Slide 18: Outline
Overview
Calculating height above the nearest drainage (HAND) from a Digital Elevation Model
Using HAND to map flood inundation for stream reach catchments
Using HAND to determine stream reach hydraulic properties
Further considerations

## Slide 19: Mapping Flood Inundation with Height above the Nearest Drainage (HAND)
Each stream reach has a water depth hw (from a hydraulic model)
Each stream reach has an ID
Each grid cell has the ID of the reach it connects to and the height above the nearest stream (drainage) hd
Evaluate inundation using hw-hd
    If(hw(id) > hd(id))
      Inundation depth = hw(id) - hd(id)
    Else
      Inundation depth = 0

## Slide 20
Mapping from height above nearest drainage to flood extent
Reach and Watershed id
Height above nearest drainage raster hHAND
hw(1) = 3.5
hw(2) = 2.5
hw(3) = 1.5
Notes: Elevations are filled to that of the pools pour point

## Slide 21: Deriving Terrain Aligned Flow Network
Grids from the NHD Plus channel head cell to the outlet cell are defined as Stream Cells
Channel Head
NHD Plus Flowline
NHD Plus channel head and flowline
DEM derived stream
NHD HR Stream
D8 Flow direction from each grid cell set in the steepest downslope direction to one of eight adjacent neighbors
Routing across flats away from high terrain and towards low terrain (Garbrecht and Martz, 1997)
67
56
52
48

## Slide 22: DEM derived stream network is consistent with the DEM but at the scale (drainage density) of NHD Plus.

## Slide 23: Height Above Nearest Drainage (HAND) evaluated from 1/3 arc sec NED DEM relative to stream raster derived from NHDPlus medium resolution stream network source grid cells. 2 m contour interval.

## Slide 24: The problem of artificial DEM Barriers

## Slide 25
From NHDHR
Etch (soft burn) in of NHDHR streams
NHDHR vectors are part of a network with direction.
Trace downslope enforcing DEM to not increase along the flow path
Railway Barrier that deflects filled DEM derived streams

## Slide 26: Conditioning the DEM by Obstacle Removal or “etching” using Vector Stream Information used to align and reconcile elevation and hydrography
48 | 48 | 49 | 48 | 47
48 | 46 | 50 | 46 | 45
47 | 45 | 51 | 43 | 39
44 | 40 | 51 | 47 | 47
41 | 45 | 52 | 48 | 48
48 | 48 | 49 | 48 | 47
48 | 46 | 50 | 46 | 45
47 | 45 | 51 | 43 | 39
44 | 40 | 51 | 47 | 47
41 | 45 | 52 | 48 | 48
48 | 48 | 49 | 48 | 47
48 | 46 | 50 | 46 | 45
47 | 45 | 40 | 40 | 39
44 | 40 | 51 | 47 | 47
41 | 45 | 52 | 48 | 48
Digital Elevation Model Conditioning
Obstacles, like this railroad that are present in DEM are removed tracing down NHD HR streams ensuring that elevation never increases along a stream.

## Slide 27: Obstacle Removal “Etch in” Workflow
Rasterize NHDPlus HR flowline;
Lower the elevation of stream cells on DEM by 100m;
Remove pits on the burned DEM;
Derive D8 flow direction on the pit-removed DEM;
Keep D8 flow direction on stream cells only;
Call TauDEM:flowdircond to burn the original DEM
  Identify ‘top cells’ which are on NHDPlus HR streams, have D8 direction, and are not downstream cells. Put them in a queue;
  For each cell in the queue:
    If the elevation is higher than its neighbors, level the elevation with neighbors;
    If above step makes any of the neighboring cell a non-downstream cell, add the neighboring cell to the queue. This step propagates the burn-in until the upstream connects to the downstream.
Motivated development of new TauDEM function “flowdircond”

## Slide 28: Effect of obstacle removal
Before
After
HAND inundation based on raw 10 m NED DEM
Hand inundation for 10 m NED DEM with obstacles removed using NHD HR

## Slide 29: Adjustments at railroad crossing
Original DEM – Flow Direction Conditioned DEM

## Slide 30: Outline
Overview
Calculating height above the nearest drainage (HAND) from a Digital Elevation Model
Using HAND to map flood inundation for stream reach catchments
Using HAND to determine stream reach hydraulic properties
Further considerations

## Slide 31: Evaluating River Hydraulic Properties
Comid | H | A | R | P | T | V | Ab | As
5781175 | 3 |  |  |  |  |  |  | 
5781175 | 4 |  |  |  |  |  |  | 
Wetted Bed Area
L
As
Ab
V
T
P
A
T
P
Cross Section Area
Wetted Perimeter
Top Width
h
Surface Area
Volume
Depth
R
Hydraulic Radius
A table with reach hydraulic parameters keyed to hydrography

## Slide 32
For each Catchment
For each height h
Identify cells where hd < h
Bed Area
Surface area
Single Cell Plan Area =dx * dy
Volume =
T
P
A
Cross Section Area
P
Wetted Perimeter
T
Top Width
Wetted Bed Area
L
As
Ab
V
Surface Area
Volume
R
Hydraulic Radius
Approximates each cell as sloping plane
Based on slide from David Maidment
Note: DEM topography used for HAND should represent river bed elevations
HAND based derivation of “reach scale” hydraulic properties

## Slide 33: Reach Hydraulic Properties Example
1 m inundation
3 m inundation
Height (m) | As (m2) | Vol (m3) | Ab | L (m) | A=V/L (m2) | P=Ab/L (m) | T=As/L (m) | R=A/P (m)
1 | 129878 | 79466 | 129948 | 2975 | 26.7 | 43.7 | 43.7 | 0.612
3 | 319877 | 530378 | 320414 | 2975 | 178.3 | 107.7 | 107.5 | 1.655

## Slide 34: Terrain Approximated Reach Average Hydraulic Properties
Used for input to reach scale hydraulic model
Hydraulic Radius
Wetted Perimeter
Cross-sectional Area
Top Width

## Slide 35: Example - Reach Catchment 5781289
Eanes Creek, Rollingwood, Texas
Drainage area = 3.13 mi2
Reach Length = 4.3 miles
Slide from David Maidment

## Slide 36: Example Discharge Computation for Reach Catchment 5781289 Eanes Creek, Rollingwood, Texas
Hydraulic Radius, R
n = 0.035 Manning roughness of channel
So = 0.0163 Bed slope
Cross section Area, A
Flood Discharge, Q (cfs)
Slide from David Maidment
Chart: Rating Curve for Eanes Creek, ComID = 5781289
| 0 | 607.56406134719509 | 2490.8796015163871 | 5785.1592347077531 | 10565.65567829302 | 16808.943658196447 | 24277.138771673799
Stage Height, h (ft) | 0 | 2.0669 | 3.937 | 5.807 | 7.6443 | 9.4159 | 10.9907
Assumes uniform flow

## Slide 37: Rating Curve for Eanes Creek
Chart: Rating Curve for Eanes Creek, ComID = 5781289
| 0 | 607.56406134719509 | 2490.8796015163871 | 5785.1592347077531 | 10565.65567829302 | 16808.943658196447 | 24277.138771673799
Stage Height, h (ft) | 0 | 2.0669 | 3.937 | 5.807 | 7.6443 | 9.4159 | 10.9907
Chart: Rating Curve for Eanes Creek, ComID = 5781289
| 0 | 607.56406134719509 | 2490.8796015163871 | 5785.1592347077531 | 10565.65567829302 | 16808.943658196447 | 24277.138771673799
Stage Height, h (ft) | 0 | 2.0669 | 3.937 | 5.807 | 7.6443 | 9.4159 | 10.9907
Forecast Discharge, Q, from National Water Model
Flood Depth, y (ft)
Slide from David Maidment

## Slide 38: Outline
Overview
Calculating height above the nearest drainage (HAND) from a Digital Elevation Model
Using HAND to map flood inundation for stream reach catchments
Using HAND to determine stream reach hydraulic properties
Further considerations

## Slide 39: Automated workflow prototyped for Texas Flood Response System by David Maidment and Colleagues
Summary of Impacts for Disaster Districts
Inundation mapping and local impact assessment
National Water Model discharge forecasts
Conversion of discharge to depth using rating curves
ESRI
Slide from David Maidment

## Slide 40: HAND Workflow implemented on ROGER supercomputer at NCSA for Continental US-Scale HAND layer evaluated
USGS 3DEP 10m DEM
NHD HR Flowline
1:24000
NHDPlus Flowline
1:100000
Obstacle Removal
D∞ Flow Direction
D8 Flow Direction
D8 Flow Accumulation
Pit Removal
Stream Definition by Threshold
D∞ Distance Down
(Vertical Average)
Channel Head Extraction
Rasterization
Channel Head Weight Grid
Stream Raster
D∞ Flow Direction
Raster
HAND Raster
Catchment Features
Flood Inundation Mapping
Results at https://web.corral.tacc.utexas.edu/nfiedata/

## Slide 41: Decompose computation by catchments or River Corridor
Parallel computation
High resolution in some areas
Incremental refinement of DEM
Incremental improvement
Can exploit high resolution (e.g. LIDAR) data in areas where accuracy is critical

## Slide 42
Increased Use of Lidar
30m USGS DEM
10m USGS DEM
0.5m Lidar DEM
D-8 Flowline
NHDMR Flowline
Target Flowline
River Direction
Slide from Xing Zheng

## Slide 43: Integration of topography and bathymetry
Wetted Bed Area
L
As
Ab
V
Surface Area
Volume
Reach scale hydraulic property calculations assume the DEM represents channel bed elevations
Image from Xing Zheng

## Slide 44: Improve NWM Routing using Reach Hydraulic Properties
Runoff
Streamflow
RAPID flow routing (for continental US)
Probabilistic flood forecasts
Weather model and forecasts (HRRR)
Land-Atmosphere Model (NOAH-MP)
Precipitation
Weather
Catchment-level forecasts
Based on slide from David Maidment
Routing here may be improved using HAND derived channel hydraulic properties

## Slide 45: Improve Stream Reach Segmentation
The segmentation of the NHD Plus network was not designed with HAND hydraulic property calculation and routing in mind. A more uniform segmentation may be better
Illustration from Xing Zheng

## Slide 46: Conclusions and Further Considerations
HAND is a special case of TauDEM distance down DEM proximity measure
The HAND approach suggested as way to rapidly approximate real time flood inundation
Serves to support flood inundation mapping where the data to support hydraulic calculations is limited
Neglects details of the river hydraulics and flow over flood plains, but more detailed approaches demand hard to obtain and uncertain inputs so this may be a helpful approach to get screening level and real time flood maps
Includes an approach to approximate reach scale hydraulic properties
Consider best reach length
Premised on good elevation model and consistent stream raster
  DEM topography should represent river bed elevations to maximal extent possible
  Research ways to align and reconcile elevation and hydrography (present obstacle removal approach not ideal)
Has been calculated across continental US using 10 m resolution DEM and NHDPlus streams for use in US National Water Model flood inundation mapping
Can exploit high resolution (e.g. LIDAR) data in areas where accuracy is critical

## Slide 47: Reading
Prior Work
Rodda, H. J. E., (2005), "The Development and Application of a Flood Risk Model for the Czech Republic," Natural Hazards, 36(1): 207-220, http://dx.doi.org/10.1007/s11069-004-4549-4.
Rennó, C. D., A. D. Nobre, L. A. Cuartas, J. V. Soares, M. G. Hodnett, J. Tomasella and M. J. Waterloo, (2008), "HAND, a new terrain descriptor using SRTM-DEM: Mapping terra-firme rainforest environments in Amazonia," Remote Sensing of Environment, 112(9): 3469-3481, http://doi.org/10.1016/j.rse.2008.03.018.
Nobre, A. D., L. A. Cuartas, M. Hodnett, C. D. Rennó, G. Rodrigues, A. Silveira, M. Waterloo and S. Saleska, (2011), "Height Above the Nearest Drainage – a hydrologically relevant new terrain model," Journal of Hydrology, 404(1–2): 13-29, http://dx.doi.org/10.1016/j.jhydrol.2011.03.051.
Tesfa, T. K., D. G. Tarboton, D. W. Watson, K. A. T. Schreuders, M. E. Baker and R. M. Wallace, (2011), "Extraction of hydrological proximity measures from DEMs using parallel processing," Environmental Modelling & Software, 26(12): 1696-1709, http://dx.doi.org/10.1016/j.envsoft.2011.07.018.
Nobre, A. D., L. A. Cuartas, M. R. Momo, D. L. Severo, A. Pinheiro and C. A. Nobre, (2016), "HAND contour: a new proxy predictor of inundation extent," Hydrological Processes, 30(2): 320-333, http://dx.doi.org/10.1002/hyp.10581.

## Slide 48: Reading
Papers just out
Zheng, X., D. G. Tarboton, D. R. Maidment, Y. Y. Liu and P. Passalacqua, (2018), "River Channel Geometry and Rating Curve Estimation Using Height above the Nearest Drainage," JAWRA Journal of the American Water Resources Association, 54(4): 785-806, http://doi.org/10.1111/1752-1688.12661.
Liu, Y. Y., D. R. Maidment, D. G. Tarboton, X. Zheng and S. Wang, (2018), "A CyberGIS Integration and Computation Framework for High-Resolution Continental-Scale Flood Inundation Mapping," JAWRA Journal of the American Water Resources Association, 54(4): 770-784, https://doi.org/10.1111/1752-1688.12660.

## Slide 49: Are there any questions?
HAND 10m for CONUS