## Slide 1: Terrain Analysis Using Digital Elevation Models (TauDEM)
David Tarboton1, Dan Watson2, Rob Wallace,3 Kim Schreuders1, Jeremy Neff1
1Utah Water Research Laboratory, Utah State University, Logan, Utah
2Computer Science, Utah State University, Logan, Utah
3US Army Engineer Research and Development Center, Information Technology Lab, Vicksburg, Mississippi
This research was funded by the US Army Research and Development Center under contract number W9124Z-08-P-0420
http://hydrology.usu.edu/taudem dtarb@usu.edu

## Slide 2: Outline
Overview of principles and methods (60 min)
Break (10 min)
Hands on using ArcGIS and R (50 min)
Break (10 min)
TauDEM parallel methods (15 min)
TauDEM on CSDMS Beach (20 min)
Discussion and overrun cushion (15 min)

## Slide 3: http://hydrology.usu.edu/taudem/taudem5.0/documentation.html

## Slide 4: TauDEM - Channel Network and Watershed Delineation Software
Pit removal (standard flooding approach)
Flow directions and slope
  D8 (standard)
  D (Tarboton, 1997, WRR 33(2):309)
  Flat routing (Garbrecht and Martz, 1997, JOH 193:204)
Drainage area (D8 and D)
Network and watershed delineation
  Support area threshold/channel maintenance coefficient (Standard)
  Combined area-slope threshold (Montgomery and Dietrich, 1992, Science, 255:826)
  Local curvature based (using Peuker and Douglas, 1975, Comput. Graphics Image Proc. 4:375)
Threshold/drainage density selection by stream drop analysis (Tarboton et al., 1991, Hyd. Proc. 5(1):81)
Other Functions: Downslope Influence, Upslope Dependence, Wetness index, distance to streams, Transport limited accumulation
Developed as C++ command line executable functions
MPICH2 used for parallelization (single program multiple data)
Relies on other software for visualization (ArcGIS Toolbox GUI)

## Slide 5: Principles and methods
Fundamentals of watershed delineation
Geomorphology based channel delineation (objective support threshold determination)
D-Infinity multiple flow direction model
Generalized accumulation functionality

## Slide 6: Principles and methods
Fundamentals of watershed delineation
Geomorphology based channel delineation (objective support threshold determination)
D-Infinity multiple flow direction model
Generalized accumulation functionality

## Slide 7: Topography defines watersheds which are fundamentally the most basic hydrologic landscape elements.

## Slide 8: The starting point: A Grid Digital Elevation Model
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 9: A grid defines geographic space as a mesh of identically-sized square cells. Each cell holds a numeric value that measures a geographic attribute (like elevation) for that unit of space.
Grid size is defined by extent, spacing and no data value information
  Number of rows, number of column
  Cell sizes (X and Y)
  Top, left , bottom and right coordinates
Grid values
  Real (floating decimal point)
  Integer (may have associated attribute table)

## Slide 10: TauDEM Grid Data Format Assumptions
Input and output grids are uncompressed GeoTIFF
Maximum size 4 GB (~32,000 x 32,000 rows and cols for single file version)
For larger areas use multifile version
GDAL Nodata tag preferred (if not present, a missing value is assumed)
Grids are square (x= y)
Grids have identical extents, cell size and spatial reference
Spatial reference information is not used (no projection on the fly)

## Slide 11: The terrain flow information model for deriving channels, watersheds, and flow related terrain information.
Raw DEM
Pit Removal (Filling)
Flow Field
Channels, Watersheds, Flow Related Terrain Information
Notes: This slide shows the general model for deriving flow field related derivative surfaces from digital elevation data. The input is a raw digital elevation model, generally elevation values on a grid. This is basic information used to derive further hydrology related spatial fields that enrich the information content of this basic data. The first step is to remove sinks, either by filling, or carving. Then a flow field is defined. This enables the calculation of flow related terrain information. My focus has been on flow related information working within this framework. I try to leave other GIS functionality, like radiation exposure, line of sight analyses and visualization to others. I have distributed my software in ways that it easily plugs in to mainstream systems, such as ArcGIS to enhance ease of use.

## Slide 12: The Pit Removal Problem
DEM creation results in artificial pits in the landscape
A pit is a set of one or more cells which has no downstream cells around it
Unless these pits are removed they become sinks and isolate portions of the watershed
Pit removal is first thing done with a DEM

## Slide 13: Pit Filling
Increase elevation to the pour point elevation until the pit drains to a neighbor

## Slide 14: Pit Filling
Pits
Pour Points
Original DEM
Pits Filled
Notes: Elevations are filled to that of the pools pour point

## Slide 15
80
74
63
69
67
56
60
52
48
30
4
5
6
3
7
2
1
8
D8 Flow Direction Model
- Direction of steepest descent
Slope = Drop/Distance
Steepest down slope direction

## Slide 16
Grid Network

## Slide 17
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
2
5
15
20
2
The area draining each grid cell includes the grid cell itself.
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
5
2
2
20
15
Contributing Area (Flow Accumulation)

## Slide 18: Stream Definition
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
2
5
15
20
2
Flow Accumulation > 10 Cell Threshold
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
2
1
5
2
2
11
15
20
Stream Network for 10 cell Threshold Drainage Area

## Slide 19
Watershed Draining to Outlet

## Slide 20: Watershed and Stream Grids

## Slide 21: DEM Delineated Catchments and Stream Networks
For every stream segment, there is a corresponding catchment
Catchments are a tessellation of the landscape
Based on the D8 flow direction model

## Slide 22: Edge contamination
Edge contamination arises due to the possibility that a contributing area value may be underestimated due to grid cells outside of the domain not being counted. This occurs when drainage is inwards from the boundaries or areas with no data values. The algorithm recognizes this and reports "no data" resulting in streaks of "no data" values extending inwards from boundaries along flow paths that enter the domain at a boundary.

## Slide 23: Principles and methods
Fundamentals of watershed delineation
Geomorphology based channel delineation (objective support threshold determination)
D-Infinity multiple flow direction model
Generalized accumulation functionality

## Slide 24: How to decide on stream delineation threshold ?
AREA 1
AREA 2
3
12
Why is it important?

## Slide 25: Delineation of Channel Networks and Catchments
500 cell theshold
1000 cell theshold

## Slide 26
Hydrologic processes are different on hillslopes and in channels. It is important to recognize this and account for this in models.
Drainage area can be concentrated or dispersed (specific catchment area) representing concentrated or dispersed flow.

## Slide 27: Examples of differently textured topography
From W. E. Dietrich
From W. E. Dietrich

## Slide 28
Lets look at some geomorphology.
    Drainage Density
    Horton’s Laws
    Slope – Area scaling
    Stream Drops
“landscape dissection into distinct valleys is limited by a threshold of channelization that sets a finite scale to the landscape.” (Montgomery and Dietrich, 1992, Science, vol. 255 p. 826.)
Suggestion: One contributing area threshold does not fit all watersheds.

## Slide 29: Drainage Density for Different Contributing Area Thresholds
EPA Reach Files
100 grid cell threshold
1000 grid cell threshold
Dd = L/A
Hillslope length  1/2Dd

## Slide 30: Drainage Density Versus Contributing Area Threshold

## Slide 31: Hortons Laws: Strahler system for stream ordering
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
2
3

## Slide 32: Constant Stream Drops Law
Broscoe, A. J., (1959), "Quantitative analysis of longitudinal stream profiles of small watersheds," Office of Naval Research, Project NR 389-042, Technical Report No. 18, Department of Geology, Columbia University, New York.
Average elevation difference between ends of Strahler streams

## Slide 33: Suggestion: Map channel networks from the DEM at the finest resolution consistent with observed channel network geomorphology ‘laws’.
Look for statistically significant break in constant stream drop property as stream delineation threshold is reduced
Break in slope versus contributing area relationship
Physical basis in the form instability theory of Smith and Bretherton (1972), see Tarboton et al. 1992

## Slide 34: Statistical Analysis of Stream Drops

## Slide 35: T-Test for Difference in Mean Values
72
130
0
T-test checks whether difference in means is large (> 2)
when compared to the spread of the data around the mean values

## Slide 36: Optimal Contributing Area Threshold

## Slide 37
100 grid cell contributing area threshold stream delineation

## Slide 38
200 grid cell contributing area threshold stream delineation

## Slide 39: Peuker Douglas “Valley” Computation (Peuker and Douglas, 1975, Comput. Graphics Image Proc. 4:375)
43
41
48
47
48
47
54
51
54
51
56
58

## Slide 40: Flow accumulation of “valley” grid cells only

## Slide 41: “Valley” Flow accumulation Threshold

## Slide 42
Peuker Douglas “Valley” based stream delineation

## Slide 43: Channel network delineation, other options
1
1
1
1
1
1
1
1
1
1
1
1
1
1
4
3
3
12
2
2
2
3
16
25
6
Contributing Area
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
3
1
1
1
2
3
3
2
Grid Order
4
5
6
3
7
2
1
8

## Slide 44
Grid network pruned to order 4 stream delineation

## Slide 45: Principles and methods
Fundamentals of watershed delineation
Geomorphology based channel delineation (objective support threshold determination)
D-Infinity multiple flow direction model
Generalized accumulation functionality

## Slide 46: Representation of Flow Field
D
D8
67
56
52
48
Steepest single direction
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.)
Notes: This slide shows how the terrain flow field is represented. Early DEM work used a single flow direction model, D8. In 1997 I published the Dinfinity method that proportions flow from each grid cell among downslope neighbors. This, at the expense of some dispersion, allows a better approximation of flow across surfaces.

## Slide 47: D-Infinity Slope, Flow Direction and Contributing Area

## Slide 48
D8
Contributing Area
D
<1 ha
1-4 ha
4-8 ha
>8 ha

## Slide 49: Principles and methods
Fundamentals of watershed delineation
Geomorphology based channel delineation (objective support threshold determination)
D-Infinity multiple flow direction model
Generalized accumulation functionality

## Slide 50
Contributing area – General accumulation function
x
w(x)

## Slide 51: Pseudocode for Recursive Flow Accumulation
Global P, w, A,  FlowAccumulation(i) for all k neighbors of i if Pki>0 FlowAccumulation(k) next k return
Pki

## Slide 52: General Pseudocode Upstream Flow Algebra Evaluation
Pki
Global P, ,  FlowAlgebra(i) for all k neighbors of i if Pki>0 FlowAlgebra(k) next k i = FA(i, Pki, k, k) return

## Slide 53: Example: Retention limited runoff generation with run-on
Global P, (r,c), q FlowAlgebra(i) for all k neighbors of i if Pki>0 FlowAlgebra(k) next k return
r
c
qi
qk

## Slide 54: Retention limited runoff with run-on
0.6
0.4
1
A
B
C
D
r=7
c=4
q=3
r=5
c=6
qin=1.8
q=0.8
r=4
c=6
q=0
1
r=4
c=5
qin=2
q=1
Retention Capacity
Runoff from uniform input of 0.25
Notes: Figure 2 illustrates the evaluation of infiltration capacity limited runoff generation with run on according to (5). Inputs are the r and c values indicated, with the proportional flow directions indicated by the arrows. Grid cells A and B on the left have no dependencies so may be immediately evaluated and using min(r-c,0) result in q=3 and 0 for grid cells A and B respectively. With these evaluated, the unevaluated dependencies of grid cell C become 0, so equation (5) can be evaluated for grid cell C. The inflow is qin=0.6 x 3 = 1.8 from grid cell B. Then q=min(5-6+1.8,0)=0.8. Now all dependencies of D have been evaluated. Inflows from cells A, B, and C, accounting for the proportions are 3 x 0.4 + 0.8 = 2, so the runoff from D is q=min(4-5+2,0)=2.

## Slide 55
Useful for a tracking contaminant or compound subject to decay or attenuation

## Slide 56: Transport limited accumulation
Supply
Capacity
Transport
Deposition
2
2
)
tan(
b
T
cap
ca
=
å
+
=
}
,
min{
cap
in
out
T
T
S
T
å
-
+
=
out
in
T
T
S
D
Useful for modeling erosion and sediment delivery, the spatial dependence of sediment delivery ratio and contaminant that adheres to sediment
S

## Slide 57: General Pseudocode Downstream Flow Algebra Evaluation
Pki
Global P, ,  FlowAlgebra(i) for all k neighbors of i if Pik>0 FlowAlgebra(k) next k i = FA(i, Pik, k, k) return

## Slide 58
Dependence function of grid cells y
0
1
0
0
1
0
0
0.6
0
0.3
0.3
0
0.6
0
0
Grid cells y
Useful for example to track where a contaminant may come from

## Slide 59: Weighted distance to target set
38.2
7.5+42.4*
(0.7+0.5)/2
32.9
7.5
30*0.5/2
0
0
0
0
0
38.2
38.2
38.2
38.2
30
To quantify effectiveness of riparian zone sediment capture based on buffer potential

## Slide 60: Buffer potential weighted distance to stream

## Slide 61: Distance Down and Distance Up
Types of distance measurements possible in distance down and distance up functions.
hs
hr
vr
vs
Point of interest
Stream
Ridge
pr
ps
ss
sr
hs
hr
vr
vs
Point of interest
Stream
Ridge
pr
ps
ss
sr

## Slide 62: Avalanche Runout

Upslope recursion to determine elevation and distance to point in trigger zone that has the highest alpha angle

## Slide 63: Summary Concepts
The GIS grid based terrain flow data model enables the representation of flow processes at and near the earth surface and derivation of a wide variety of information useful for the study of hydrologic processes.
  Slope
  Flow direction
  Drainage area
  Catchments, watersheds and channel networks
  Multiple other flow related quantities

## Slide 64: Summary Concepts (2)
Hydrologic processes are different between hillslopes and channels
Drainage density defines the average spacing between streams and the representative length of hillslopes
The constant drop property provides a basis for selecting channel delineation criteria to preserve the natural drainage density of the topography
Generalized channel delineation criteria can represent spatial variability in the topographic texture and drainage density

## Slide 65: Summary Concepts (3)
Flow algebra generalizes the recursive flow accumulation methodology
Downslope and upslope logic
Several new flow algebra functions
Edge contamination checking is important to ensure that results are not impacted by area outside the domain of the DEM analyzed

## Slide 66: Outline
Overview of principles and methods (60 min)
Break (10 min)
Hands on using ArcGIS and R (50 min)
Break (10 min)
TauDEM parallel methods (15 min)
TauDEM on CSDMS Beach (20 min)
Discussion and overrun cushion (15 min)

## Slide 67: Outline
Overview of principles and methods (60 min)
Break (10 min)
Hands on using ArcGIS and R (50 min)
Break (10 min)
TauDEM parallel methods (15 min)
TauDEM on CSDMS Beach (20 min)
Discussion and overrun cushion (15 min)

## Slide 68: Digital Elevation Model data
Obtained from http://seamless.usgs.gov
Should be projected (need to use a GIS for this)
TauDEM needs GeoTIFF
  If larger than 4 GB use multiple files that cover the domain and MF version (on Beach)
GDAL useful to translate to TIFF format
  http://www.gdal.org/
  http://trac.osgeo.org/gdal/wiki/DownloadingGdalBinaries

## Slide 69: ArcMap

## Slide 70: Default file name suffixes
For complete list see: http://hydrology.usu.edu/taudem/taudem5.0/TauDEM_Tools.chm

## Slide 71: R
z=raster("logan.tif")
plot(z)

## Slide 72: Illustrative Use Case: Delineation of channels and watersheds using a constant support area threshold
Steps
Pit Remove
D8 Flow Directions
D8 Contributing Area
Stream Definition by Threshold
Stream Reach and Watershed

## Slide 73: Pit Remove

## Slide 74: D8 Flow Direction (and Slope)

## Slide 75: D8 Contributing Area

## Slide 76: Stream Definition by Threshold

## Slide 77: Stream Reach and Watershed

## Slide 78: Topographic wetness index from the Dinfinity method
Steps
Pit Remove
D-Infinity Flow Directions (and Slopes)
D-Infinity Contributing Area
Slope Over Area Ratio

## Slide 79: D-Infinity Contributing Area

## Slide 80: Wetness Index
Slope (S)
Specific Catchment Area (a)
Wetness Index ln(a/S)

## Slide 81: Peuker Douglas
Local Valley Form Computation (Peuker and Douglas, 1975, Comput. Graphics Image Proc. 4:375)
43
41
48
47
48
47
54
51
54
51
56
58

## Slide 82: Weighted D8 Contributing Area
Contributing area only of valley form grid cells upstream of outlet

## Slide 83: Stream Drop Analysis

## Slide 84: Outline
Overview of principles and methods (60 min)
Break (10 min)
Hands on using ArcGIS and R (50 min)
Break (10 min)
TauDEM parallel methods (15 min)
TauDEM on CSDMS Beach (20 min)
Discussion and overrun cushion (15 min)

## Slide 85: The challenge of increasing Digital Elevation Model (DEM) resolution
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10-30 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2

## Slide 86: TauDEM Parallel Approach
MPI, distributed memory paradigm
Row oriented slices
Each process includes one buffer row on either side
Each process does not change buffer row

## Slide 87: Some Algorithm Details Pit Removal: Planchon Fill Algorithm
Initialization
1st Pass
2nd Pass
Planchon, O., and F. Darboux (2001), A fast, simple and versatile algorithm to fill the depressions of digital elevation models, Catena(46), 159-176.

## Slide 88: Parallel Scheme
Communicate
Initialize( Z,F) Do for all grid cells i if Z(i) > n F(i) ← Z(i) Else F(i) ← n i on stack for next pass endfor Send( topRow, rank-1 ) Send( bottomRow, rank+1 ) Recv( rowBelow, rank+1 ) Recv( rowAbove, rank-1 ) Until F is not modified
Z denotes the original elevation.
F denotes the pit filled elevation.
n denotes lowest neighboring elevation
i denotes the cell being evaluated
Iterate only over stack of changeable cells

## Slide 89: Parallelization of Contributing Area/Flow Algebra
A=1
A=1
A=1
A=1.5
A=3
A=1.5
A=1
D=2
D=1
A=1
D=1
D=1
B=-2
Queue’s empty so exchange border info.
B=-1
A=1
A=1
A=1
D=0
A=3
A=1.5
A=1
D=2
D=1
A=1
D=1
D=1
B=-2
A=1
A=1
A=1
A=1.5
A=3
A=1.5
A=1
D=0
D=0
A=1
D=1
D=1
resulting in new D=0 cells on queue
A=1
A=1
A=1
A=1.5
A=3
A=1.5
A=1
A=5.5
A=2.5
A=1
A=6
A=3.5
and so on until completion
A=1
A=1
A=1
D=0
D=0
D=0
A=1
D=2
D=1
A=1
D=1
D=1
D=0
D=0
D=0
D=1
D=3
D=1
D=0
D=2
D=1
D=0
D=3
D=1
A=1
D=0
D=0
D=1
D=2
D=0
A=1
D=2
D=1
D=0
D=2
D=1
A=1
A=1
D=0
D=1
D=1
D=0
A=1
D=2
D=1
A=1
D=1
D=1
A=1
A=1
A=1
D=1
D=0
A=1.5
A=1
D=2
D=1
A=1
D=1
D=1
B=-1
Decrease cross partition dependency
Executed by every process with grid flow field P, grid dependencies D initialized to 0 and an empty queue Q. FindDependencies(P,Q,D) for all i for all k neighbors of i if Pki>0 D(i)=D(i)+1 if D(i)=0 add i to Q next
Executed by every process with D and Q initialized from FindDependencies. FlowAlgebra(P,Q,D,,) while Q isn’t empty get i from Q i = FA(i, Pki, k, k) for each downslope neighbor n of i if Pin>0 D(n)=D(n)-1 if D(n)=0 add n to Q next n end while swap process buffers and repeat
1. Dependency grid
2. Flow algebra function

## Slide 90: Capabilities Summary
Capability to run larger problems |  |  |  | 
 |  | Processors used | Grid size | 
 |  |  | Theoretcal limit | Largest run
2008 | TauDEM 4 | 1 | 0.22 GB | 0.22 GB
Sept 2009 | Partial implement-ation | 8 | 4 GB | 1.6 GB
June 2010 | TauDEM 5 | 8 | 4 GB | 4 GB
Sept 2010 | Multifile on 48 GB RAM PC | 4 | Hardware limits | 6 GB
Sept 2010 | Multifile on cluster with 128 GB RAM | 128 | Hardware limits | 11 GB
1.6 GB
0.22 GB
4 GB
6 GB
11 GB
At 10 m grid cell size
Single file size limit 4GB

## Slide 91: Improved runtime efficiency
Parallel Pit Remove timing for NEDB test dataset (14849 x 27174 cells  1.6 GB).
128 processor cluster
16 diskless Dell SC1435 compute nodes, each with 2.0GHz dual quad-core AMD Opteron 2350 processors with 8GB RAM
8 processor PC
Dual quad-core Xeon E5405 2.0GHz PC with 16GB RAM

## Slide 92: Improved runtime efficiency
Parallel D-Infinity Contributing Area Timing for Boise River dataset (24856 x 24000 cells ~ 2.4 GB)
128 processor cluster
16 diskless Dell SC1435 compute nodes, each with 2.0GHz dual quad-core AMD Opteron 2350 processors with 8GB RAM
8 processor PC
Dual quad-core Xeon E5405 2.0GHz PC with 16GB RAM

## Slide 93: Scaling of run times to large grids
Dataset | Size | Hardware | Number of Processors | PitRemove (run time seconds) |  | D8FlowDir (run time seconds) | 
 | (GB) |  |  | Compute | Total | Compute | Total
GSL100 | 0.12 | Owl (PC) | 8 | 10 | 12 | 356 | 358
GSL100 | 0.12 | Rex (Cluster) | 8 | 28 | 360 | 1075 | 1323
GSL100 | 0.12 | Rex (Cluster) | 64 | 10 | 256 | 198 | 430
GSL100 | 0.12 | Mac | 8 | 20 | 20 | 803 | 806
YellowStone | 2.14 | Owl (PC) | 8 | 529 | 681 | 4363 | 4571
YellowStone | 2.14 | Rex (Cluster) | 64 | 140 | 3759 | 2855 | 11385
Boise River | 4 | Owl (PC) | 8 | 4818 | 6225 | 10558 | 11599
Boise River | 4 | Virtual (PC) | 4 | 1502 | 2120 | 10658 | 11191
Bear/Jordan/Weber | 6 | Virtual (PC) | 4 | 4780 | 5695 | 36569 | 37098
Chesapeake | 11.3 | Rex (Cluster) | 64 | 702 | 24045 |  | 
Owl is an 8 core PC (Dual quad-core Xeon E5405 2.0GHz) with 16GB RAM
Rex is a 128 core cluster of 16 diskless Dell SC1435 compute nodes, each with 2.0GHz dual quad-core AMD Opteron 2350 processors with 8GB RAM
Virtual is a virtual PC resourced with 48 GB RAM and 4 Intel Xeon E5450 3 GHz processors
Mac is an 8 core (Dual quad-core Intel Xeon E5620 2.26 GHz) with 16GB RAM

## Slide 94: Scaling of run times to large grids
Chart: PitRemove run times
| 0.12000000000000002 | 2.14 | 4
Compute (OWL 8) | 9.5315 | 529.3877 | 4817.6293
Total (OWL 8) | 12.0132 | 680.5546 | 6224.5029
Compute (VPC 4) | 1502.2881 | 4779.8761
Total (VPC 4) | 2120.0307 | 5695.2647
Compute (Rex 64) | 10.3477 | 139.9145 | 701.7363
Total (Rex 64) | 255.8499 | 3758.8385 | 24045.0594
Owl is an 8 core PC (Dual quad-core Xeon E5405 2.0GHz) with 16GB RAM
Rex is a 128 core cluster of 16 diskless Dell SC1435 compute nodes, each with 2.0GHz dual quad-core AMD Opteron 2350 processors with 8GB RAM
Virtual is a virtual PC resourced with 48 GB RAM and 4 Intel Xeon E5450 3 GHz processors
Chart: D8FlowDir run times
| 0.12000000000000002 | 2.14 | 4
Compute (OWL 8) | 355.6897 | 4363.094 | 10558.4924
Total (OWL 8) | 357.8926 | 4570.5555 | 11599.0188
Compute (VPC 4) | 10658.033 | 36568.8896
Total (VPC 4) | 11191.1583 | 37098.2448
Compute (Rex 64) | 198.0345 | 2854.9228
Total (Rex 64) | 429.8418 | 11384.6786

## Slide 95: Limitations and Dependencies
Uses MPICH2 library from Argonne National Laboratory http://www.mcs.anl.gov/research/projects/mpich2/
TIFF (GeoTIFF) 4 GB file size. Extended using multiple files
Processor memory
Grid data needs to be projected (same x, y and z units) and all grids have to be exactly aligned (rows, columns, cell size, position in space)

## Slide 96: Outline
Overview of principles and methods (60 min)
Break (10 min)
Hands on using ArcGIS and R (50 min)
Break (10 min)
TauDEM parallel methods (15 min)
TauDEM on CSDMS Beach (20 min)
Discussion and overrun cushion (15 min)

## Slide 97: Multi-File approach
To overcome 4 GB file size limit
To avoid bottleneck of parallel reads to network files
What was a file input to TauDEM is now a folder input
All files in the folder tiled together to form large logical grid

## Slide 98: Processor Specific Multi-File Strategy
Core 1
Core 2
Shared file store
Node 2 local disk
Node 1 local disk
Core 1
Core 2
Node 2 local disk
Node 1 local disk
Output
Shared file store
Input
Scatter all input files to all nodes
Gather partial output from each node to form complete output on shared store

## Slide 99: Beach Specifics
TauDEM is in /home/csdms/models/taudem/5.1
Scripts are in /home/csdms/models/taudem/scripts
  run_taudem.sh. Submits to debug queue. Edit to change queue
  taudem_submit.sh. Called by above script. Performs scatter – gather. Edit to adjust number of nodes and number of processes per node
Assemble input data in a directory tddata
Run Taudem commands using
    run_taudem.sh <command> <arguments>

## Slide 100: Beach job sequence to delineate Logan watershed
run_taudem.sh pitremove -z logan -fel loganfel
run_taudem.sh d8flowdir -fel loganfel -p loganp -sd8 logansd8
run_taudem.sh aread8 -p loganp -ad8 loganad8
run_taudem.sh threshold -ssa loganad8 -src logansrc1 -thresh 1000
run_taudem.sh moveoutletstostrm -p loganp -src logansrc1 -o LoganOutlet.shp -om outletsmoved.shp
run_taudem.sh peukerdouglas -fel loganfel -ss loganss
run_taudem.sh aread8 -p loganp -o outletsmoved.shp -ad8 loganssa -wg loganss
run_taudem.sh dropanalysis -p loganp -fel loganfel -ad8 loganad8 -ssa loganssa -drp logandrp.txt -o outletsmoved.shp -par 5 500 10 0
run_taudem.sh threshold -ssa loganssa -src logansrc -thresh 300
run_taudem.sh streamnet -fel loganfel -p loganp -ad8 loganad8 -src logansrc -ord loganord -tree logantree.dat -coord logancoord.dat -net logannet.shp -w loganw -o outletsmoved.shp