## Slide 1: HydroShare: Advancing Hydrology through Collaborative Data and Model Sharing
David Tarboton, Ray Idaszak, Jeffery Horsburgh, Dan Ames, Jon Goodall, Larry Band, Venkatesh Merwade, Alva Couch, Jennifer Arrigo, Rick Hooper, David Valentine, David Maidment, Jeff Heard, Pabitra Dash, Tian Gan, Tony Castronova, Stephen Jackson, Cuyler Frisby, Stephanie Mills, Brian Miles
http://www.hydroshare.org
OCI-1148453
OCI-1148090
2012-2017
USU, RENCI, BYU, UNC, UVA, CUAHSI, Tufts, Texas, Purdue, SDSC

## Slide 2: Research Areas
Hydrologic Information Systems
Digital Elevation Model Terrain Analysis
Hydrology and Geomorphology
Distributed Hydrologic Modeling
Snow and glacier melt
Non parametric stochastic hydrology
Streamflow regimes for stream ecology
The Great Salt Lake
Data
Catalog
Desktop
Server
Metadata
Search
ODM, WaterML
Production
Consumption
Discovery

## Slide 3: Outline
Data and computational challenges
CUAHSI HIS
HydroShare
  Goals
  Use cases
  Resource data model
  Architecture
Web based data, modeling and analysis services
Summary
Data
Analysis
Models

## Slide 4: The challenge of increasing Digital Elevation Model (DEM) resolution
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2
e.g. 50,000 km2
Watershed
27 MB
240 MB
2 GB
200 GB

## Slide 5: Data Heterogeneity
From dispersed federal agencies
From investigators collected for different purposes
Different formats
  Points
  Lines
  Polygons
  Fields
  Time Series
Rainfall and Meteorology
Water quantity
Soil water
Groundwater
Water quality
GIS
The way that data is stored can enhance or inhibit the analysis that can be done
We need ways to organize the data we work with
Data models

## Slide 6
Data intensive models to understand and examine consequences, impacts and effects
From Larry Band
Notes: Strata can be redefined any time

## Slide 7: A Digital Divide
Data Intensive High Performance Computing
Hydrologic Experimentation and Modeling
awk
grep
vi
#PBS -l nodes=4:ppn=8
mpiexec
chmod
#!/bin/bash
Do you have the access or know how to take advantage of advanced computing capability?
Gateways, Web Interfaces, Software services

## Slide 8: HydroShare Goals
Enable more rapid advances in hydrologic understanding through collaborative data sharing, analysis and modeling
To become a foundational cyberinfrastructure platform for hydrologic research that blends
  Software as a service
  Data as a service
  Models as a service
  Visualization and analysis services
To solve problems of size and scope not otherwise solvable using desktop computing
Address community needs

## Slide 9: CUAHSI HIS
HydroServer – Data Publication
Lake Powell Inflow and Storage
HydroDesktop – Data Access and Analysis
HydroDesktop – Combining multiple data sources
HydroCatalog
Data Discovery
The CUAHSI Hydrologic Information System (HIS) is an internet based system to support the sharing of hydrologic data. It is comprised of hydrologic databases and servers connected through web services as well as software for data publication, discovery and access.

## Slide 10
http://www.opengeospatial.org/standards/waterml
Open Geospatial Consortium Web Service Standards
This document is an OGC® Encoding Standard for the representation of hydrological observations data with a specific focus on time series structures.
These standards have been developed over the past 10 years …. by 400 companies and agencies ....

## Slide 11: HydroDesktop
Uses EPA WATERS Web, Mapping, and Database Services at http://www.epa.gov/waters/geoservices/index.html to delineate Watersheds
An open source
dotSpatial GIS based desktop client that supports discovery and analysis of hydrologic observations data
Notes: The service URLs that the HD tool uses are seen in http://hydrodesktop.codeplex.com/SourceControl/changeset/view/475b15a84bf4#Source%2fEPADelineation%2fCallWebService.cs The HD tool uses the Point Indexing Service to find the nearest NHD reach to where the user clicked. This returns a location on that reach. This point location is then used as input to the Navigation Delineation Service to get the watershed, and the Upstream/Downstream Service to get the river lines. The delineation service has two limitations: * It only works up to a certain distance upstream. I think we have it set to 100km. So for large watersheds (those with more than 100km of stream length upstream of where the user clicked), we don't get the most upstream portions of the watershed. * It doesn't delineate exactly to where the user clicked. It delineates to the endpoint of the NHD reach. (Can't remember if it is the clicked reach or the upstream reach -- try it and see.)

## Slide 12
Search last 22 years for all data in buffer around watershed

## Slide 13: Download and Plot the Data
Combining information from multiple sources

## Slide 14: Perform an analysis using R
At your fingertips
the full analysis capability of R
data from multiple sources
accessed from distributed (cloud) resources.
importance of interoperability

## Slide 15: But
Publishing data using CUAHSI HIS requires access to or setting up a HydroServer
Accessing data requires HydroDesktop
Generally limited to time series at a point
Server
Desktop
Catalog

## Slide 16: HydroShare is a collaborative environment (being developed) for data sharing, analysis and modeling
Web based data and software services to overcome
Simplify working with large datasets and HPC
Overcome platform dependency limitations
Avoid software installation limitations
Users
Browser
Client
Django web framework
Web Services (REST API)
Web Pages
iRODS “Network File System”
Resource Files
User accounts
Access control
Our goal is to make sharing of hydrologic data and models as easy as sharing videos on YouTube or shopping on Amazon.

## Slide 17
Collaborative data analysis and publication use case
Observe
Store
Discover and access
Analyze
Model
Collaborate
Publish (DOI)
1
Observers and instruments
Analysis
Models
2
3
4
5
6
7
Data
Publication, Archival, Curation
Collaboration
Digital Library

## Slide 18: Collaborative Integrated Modeling
Data: Links to national and global data sets of essential terrestrial variables (e.g. NASA NEX, HydroTerre)
Tools to preprocess and configure inputs (EcoHydroLib, TauDEM, CyberGIS)
Preconfigured models and modeling systems as services (SWATShare)
Standards for information exchange for interoperability (OpenMI, CSDMS BMI)
Tools for visualization and analysis
x
y
t
Flow
Time
Flow
Time
Time
P
Pre-processing and model linking
Modeling Services (e.g. SWATShare)
Notes: Data: Links to national and global data sets of essential terrestrial variables (e.g. NASA NEX, HydroTerre)
Tools to preprocess and configure inputs
Preconfigured models and modeling systems as services
Standards for information exchange for interoperability (OpenMI, CSDMS BMI)
Tools for Visualization and Analysis
Automated reasoning to couple models based on purpose, context, data and resources

## Slide 19: At its heart, HydroShare is a system for sharing Resources and Collaborating
Files and sets of files structured to represent a hydrologic process, model, or element in the hydrologic environment
Standard data models enhance interoperability and support functionality “hydro value added”
Tools that act on resources to visualize, modify and create new resources
  Encode standard/best practices
Access control and sharing model

## Slide 20: Resource Data Model
Open Archives Initiative – Object Reuse and Exchange (OAI-ORE) - standards for the description and exchange of aggregations of Web resources
BagIt – hierarchical file packaging format designed to support disk-based or network-based storage and transfer of generalized digital content
Compatible with DataOne

## Slide 21: Types of data to support as resources
Resource Types
Generic 
Geographic Raster 
Referenced Time Series (CUAHSI HIS web service link) 
Geographic Feature set
Multidimensional Space Time dataset
River Geometry
Sample based observations (ODM2 and CZO)
HydroDesktop Project package
Scripts
Model program
Model component
Model instance
Composite resources
x
y
t

## Slide 22: River Channel
http://dx.doi.org/10.1016/j.envsoft.2014.12.002

## Slide 23: Models
Model package
  Bundled components
  references existing resources
Model program
  executable entity
  may consist of submodules and other complex relationships
Model input
  input required by a program
  files, parameters, etc...
Model output
  outputs produced by a program
  files, plots, etc...

## Slide 24: Model Execution in HydroShare
Package
Input and output Hydroshare resources
Link input, output, and program resources to create model packages
Execution of model package within the HydroShare environment to create "new" resources
Program
Input
Program
Input
Package
Output
EXECUTE
Output
CREATE OUTPUT
CREATE PACKAGE

## Slide 25: SWATShare
SWAT Models (.zip file)
Metadata
Model and Output (.zip, .xls or .txt file)
Location

## Slide 26
Demo

## Slide 27: Collaborative functionality

## Slide 28
Clearing your desk. The trend towards network (cloud) computing.
Data Sources
Functions and Tools
Server
Software as a Service
Users
Based on slide from Norm Jones
Can we deliver Hydrologic Analysis functionality as a service over the web?

## Slide 29: Terrain Analysis
Raw DEM
Pit Removal
Flow Field
Flow Related Terrain Information
Watersheds are the most basic hydrologic landscape elements
Notes: This slide shows the general model for deriving flow field related derivative surfaces from digital elevation data. The input is a raw digital elevation model, generally elevation values on a grid. This is basic information used to derive further hydrology related spatial fields that enrich the information content of this basic data. The first step is to remove sinks, either by filling, or carving. Then a flow field is defined. This enables the calculation of flow related terrain information.

## Slide 30: TauDEM
Stream and watershed delineation
Multiple flow direction flow field
Calculation of flow based derivative surfaces
MPI Parallel Implementation for speed up and large problems
Open source platform independent C++ command line executables for each function
Deployed as an ArcGIS Toolbox with python scripts that drive command line executables
CSDMS Cluster Implementation
Open Topography and XSEDE implementation
http://hydrology.usu.edu/taudem/

## Slide 31: Using TauDEM today requires
Expertise in Hydrologic DEM analysis
The software
  ArcGIS licenses (for ArcGIS plugin)
  The ability to install software
  TauDEM command functions with MPI installation
  Compilation for other platforms
Sufficient Hardware (RAM and Disk)
The data (uncompressed GeoTIFF, projected, consistent grid size and spatial reference)

## Slide 32: Moving TauDEM to the cloud
CyberGIS
http://gateway.cigi.illinois.edu/
Open Topography
www.opentopography.org

## Slide 33: Parallel TauDEM Functions
MPI, distributed memory paradigm
Row oriented slices
Each process includes one buffer row on either side
Each process does not change buffer row
Improved runtime efficiency
Capability to run larger problems

## Slide 34: XSEDE Extended Collaboration Support Services (ECSS) improvements
Reconfiguration of multiple file header reads to be broadcast from single node
Reconfiguration of output files to avoid spanning processors
Execution time of the three most costly TauDEM functions on a 36GB DEM dataset.
#cores | Compute | Header Read | Data Read | Data Write
32 | 42.7 / 42.8 | 193.5 / 3.8 | 0.4 / 0.4 | 153.5 / 3.5
64 | 35.3 / 34.8 | 605.5 / 3.9 | 1.5 / 1.1 | 160.2 / 2.3
128 | 33.7 / 33.0 | 615.2 / 2.6 | 0.9 / 1.0 | 173.2 / 2.3
256 | 37.5 / 38.0 | 831.7 / 2.3 | 0.5 / 0.9 | 391.3 / 1.6
I/O Time Comparison (before / after; in seconds) for 2 GB DEM
StreamNet
DinfFlowdir
D8Flowdir

## Slide 35: TauDEM Wetness index from Open Topography
Eel River ln(a/S)
a in meters

## Slide 36: TauDEM in CyberGIS
http://gateway.cigi.illinois.edu/

## Slide 37: Select the products you want
The wizard configures the sequence of functions to run to get the result

## Slide 38: Results displayed in browser

## Slide 39: Computation via Python Client calling API
Input
Result
Python session on desktop but data and analysis on server
Assumptions
Research hydrologic modelers should be comfortable using a scientific programming language like Python or R.
Hydrologic modelers are not expert in HPC systems and learning this is a barrier to the use of HPC.
Hydrologic modeling is data intensive (large datasets from a range of sources)

## Slide 40: Architecture
iRODS “Network File System”
iCAT Zone
User Accounts
Authentication and Authorization Infrastructure (AAI) for Access Control
Web Services (REST API)
Django web application framework (Python)
Web Pages
iRODS Native REST API
Clients (3rd party), interoperable systems and web tools
HydroDesktop
Tethys
BiG CZ SSI
CI-WATER
SEAD
CyberGIS
SESYNC GI Venture
RENCI
Utah
www.hydroshare.org
tools.hydroshare.org
Distributed Resource Servers
Files
Science Metadata
Discovery (using e.g. ElasticSearch via MSVC plugin)
Others

## Slide 41: Summary
A new, web-based system for advancing model and data sharing
Sharing features to HydroDesktop
Access multiple types of hydrologic data using standards compliant data formats and interfaces
Flexible discovery functionality
Model sharing and execution
Facilitate and ease access to use of high performance computing
Social media and collaboration functionality
Links to other data and modeling systems

## Slide 42: Thanks to the HydroShare team!
  USU
  RENCI/UNC
  CUAHSI
  BYU
  Tufts
  UVA
  Texas
  Purdue
  SDSC
http://hydroshare.cuahsi.org
OCI-1148453
OCI-1148090
2012-2017
Notes: The HydroShare project is part of a broad effort in CUAHSI in the area of Hydrologic Information Systems. We have a team of developers and domain scientists from eight universities working on HydroShare. This is part of the even broader focus in NSF on data management, Cyberinfrastructure and sustainable software.