## Slide 1
Manned Boat ADCP Deployment

## Slide 2
ADCP Transducer Deployed Through Hole in Bottom of Kayak

## Slide 3
ADCP Tethered to Stand-Up Cableway

## Slide 4
ADCP Deployed From Bank Operated Cableway

## Slide 5
View of complete measurement transect in WinRiver II ADCP measurement program

## Slide 6
WinRiver II Measurement Summary Sheet

## Slide 7
Using extrap program to view a 0.1667 power curve velocity profile found in a ‘typical’ natural river channel. No adjustment would be necessary for this measurement.
ADCP does is not capable of measuring a portion of the top and bottom of the river. WinRiver II would estimate the top and bottom discharge for the measurement based on these segments of the power curve.

## Slide 8
Here the velocity profile has changed due to water backing up against bridge piers downstream of the measuring section. Power curve exponent can be adjusted manually or optimized by extrap and a 0.0802 power curve might be applied to the measurement in WinRiver II to adjust the top and bottom discharge estimates. An adjustment like this sometimes changes the total computed discharge by 2-3 %.
Top and bottom discharge may need to be adjusted based on these segments of the curve.

## Slide 9
A loop moving bed test where no moving bed was found and no adjustment was required
Out and back segments are close together, indicating no moving bed.

## Slide 10
If a moving bed is present and the ADCP uses bottom tracking the instrument will ‘think’ it’s moving upstream during the measurement and measured discharge may be artificially high. A correction can be applied based on a moving bed loop test.
Out and back segments are separated indicating that a moving bed may be present

## Slide 11
http://hydroacoustics.usgs.gov/index.shtml