## CEE6110 Probabilistic and Statistical Methods in Engineering

Homework 7.  Bootstrap Methods	Fall 2006, Solution

- Reevaluating Kottegoda 5.2.

Use t distribution given on page 249.

Confidence limits are   (KR page 250)

data = [2437  2437 2425	2427	2428	2448	2456	2436	2435	2446	2441	2456	2444	2447	2433	2429	2435	2471	2472	2445	2436	2450	2454	2449	2441	2457	2447	2436 	2458	2415	2448	2445	2436	2469	2455	2473	2488	2454	2427	2411];

x=data(1:20);

xbar=mean(x)

sdev=std(x)

n=length(x)

v=n-1  % Degrees of freedom

t1=tinv(0.025,v)

t2=tinv(0.975,v)

xbar =

2.4424e+003

sdev =

13.3077

n =

20

v =

19

t1 =

-2.0930

t2 =

2.0930

Limits

llimit=xbar+t1*sdev/sqrt(n)

ulimit=xbar+t2*sdev/sqrt(n)

llimit =

2.4362e+003

ulimit =

2.4486e+003

T-statistic confidence interval is 2436 <µ < 2448.

(a) Bootstrap method to estimate 95% confidence limits on the mean using the first 20 concrete densities in table E.1.2.

B=1000;

n=length(x);

for ib=1:B;

rind=ceil(rand(n,1)*n);

xbs=x(rind);

bsmean(ib)=mean(xbs);

end

bsmean=sort(bsmean);

llimitboot =bsmean(25)

ulimitboot =bsmean(975)

hist(bsmean)

llimitboot =

2.4373e+003

ulimitboot =

2.4482e+003

Bootstrap confidence limits for the mean calculated using the first 20 concrete densities 2437 <µ < 2448.

(b) Bootstrap method to estiamte 95% confidence limits on the mean using all 40 concrete densities in table E.1.2.

B=1000;

n=length(data);%Note this uses all the data. The first

for ib=1:B;%  20 values are stored in the variable x.

rind=ceil(rand(n,1)*n);

xbs=data(rind);

bsmean(ib)=mean(xbs);

end

bsmean=sort(bsmean);

llimitboot= bsmean(25)

ulimitboot =bsmean(975)

hist(bsmean)

llimitboot =

2.4400e+003

ulimitboot =

2.4502e+003

Bootstrap confidence limits for the mean using all the data:  2440 <µ < 2450.

2.  Reevaluating Kottegoda 5.5 using the correct data

ch1=chi2inv(0.975,v)   % v, the degrees of freedom were calculated above in problem 1

ch2=chi2inv(0.025,v)

ch1 =

32.8523

ch2 =

8.9065

Limits

(n-1)*sdev^2/ch1

(n-1)*sdev^2/ch2

ans =

102.4220

ans =

377.7908

The confidence limits on the variance are 102< σ2< 378. Note that this range includes 162 unlike what was mentioned in the solution to assignment 5.

a) Bootstrap simulation for estimating 95% confidence limits  for variance and standard devaition with first 20 density values from Table E.1.2.

B=1000;

n=length(x);

for ib=1:B;

rind=ceil(rand(n,1)*n);

xbs=x(rind);

bsvar(ib)=var(xbs);

bsstd(ib)=std(xbs);

end

bsvar=sort(bsvar);

bsstd=sort(bsstd);

bsLvar= bsvar(25)

bsUvar=bsvar(975)

bsLstd= bsstd(25)

bsUstd=bsstd(975)

subplot(2,1,1)

hist(bsvar)

xlabel('variance');

ylabel('Frequency');

subplot(2,1,2)

hist(bsstd)

xlabel('standard deviation');

ylabel('Frequency');

bsLvar =

64.7237

bsUvar =

275.1474

bsLstd =

8.0451

bsUstd =

16.5876

The confidence limits for variance and standard deviation with the first 20 concrete densitites are 65 <σ2 < 275 and 8<σ <17.

b) Bootstrap simulation for estimating 95% confidence limits for variance and standard deviation with 40 density values from Table E.1.2.

B=1000;

n=length(data);

for ib=1:B;

rind=ceil(rand(n,1)*n);

xbs=data(rind);

bsvar(ib)=var(xbs);

bsstd(ib)=std(xbs);

end

bsvar=sort(bsvar);

bsstd=sort(bsstd);

bsLvar= bsvar(25)

bsUvar=bsvar(975)

bsLstd= bsstd(25)

bsUstd=bsstd(975)

subplot(2,1,1)

hist(bsvar)

xlabel('variance');

ylabel('Frequency');

subplot(2,1,2)

hist(bsstd)

xlabel('standard deviation');

ylabel('Frequency');

bsLvar =

146.8692

bsUvar =

385.3846

bsLstd =

12.1190

bsUstd =

19.6312

The confidence limits for variance and standard deviation with all the concrete density data:  147 <σ2 < 385 and 12<σ <20.

3.

i) Parametric bootstrap with the first 20 concrete density data.

B=1000;

n=length(x)

xbar=mean(x);

xstd=std(x);

for ib=1:B;

rnorm=randn(n,1);

xbs=rnorm*xstd+xbar;

bsmean(ib)=mean(xbs);

bsvar(ib)=var(xbs);

bsstd(ib)=std(xbs);

end

bsmean=sort(bsmean);

bsvar=sort(bsvar);

bsstd=sort(bsstd);

bsLmean= bsmean(25)

bsUmean=bsmean(975)

bsLvar= bsvar(25)

bsUvar=bsvar(975)

bsLstd= bsstd(25)

bsUstd=bsstd(975)

n =

20

bsLmean =

2.4365e+003

bsUmean =

2.4485e+003

bsLvar =

82.5161

bsUvar =

304.9485

bsLstd =

9.0838

bsUstd =

17.4628

Confidence limits with parametric bootstraping using the first 20 concrete densities

2437 <µ < 2449 , 82.5 <σ2 < 305 and 9 <σ <17.

3.ii) Parametric bootstrap with 40 concrete density data.

B=1000;

n=length(data);

xbar=mean(data);

xstd=std(data);

for ib=1:B;

rnorm=randn(n,1);

xbs=rnorm*xstd+xbar;

bsmean(ib)=mean(xbs);

bsvar(ib)=var(xbs);

bsstd(ib)=std(xbs);

end

bsmean=sort(bsmean);

bsvar=sort(bsvar);

bsstd=sort(bsstd);

bsLmean= bsmean(25)

bsUmean=bsmean(975)

bsLvar= bsvar(25)

bsUvar=bsvar(975)

bsLstd= bsstd(25)

bsUstd=bsstd(975)

bsLmean =

2.4399e+003

bsUmean =

2.4496e+003

bsLvar =

159.9685

bsUvar =

382.1098

bsLstd =

12.6479

bsUstd =

19.5476

Confidence limits with parametric bootstraping using all the concrete densities

2440 <µ < 2450 , 156 <σ2 < 382 and 13 <σ <20.

4. Summary

|  | Statitic | Lower limit | Upper limit | Range |
| --- | --- | --- | --- | --- |
| Mean | Parametric, assignment 6 | 2436.2 | 2448.6 | 12.4 |
|  | Bootstrap 20 points | 2437.3 | 2448.2 | 10.9 |
|  | Bootstrap 40 points | 2440 | 2450.2 | 10.2 |
|  | Parametric bootstrap 20 points | 2436.5 | 2448.5 | 12 |
|  | Parametric bootstrap 40 points | 2439.9 | 2449.6 | 9.7 |
| Variance | Parametric, assignment 6 | 102.4 | 377.8 | 275.4 |
|  | Bootstrap 20 points | 64.72 | 275.14 | 210.42 |
|  | Bootstrap 40 points | 146.86 | 385.38 | 238.52 |
|  | Parametric bootstrap 20 points | 82.5 | 304.94 | 222.44 |
|  | Parametric bootstrap 40 points | 159.9 | 382 | 222.1 |
| Std Deviation | Parametric, assignment 6 | 10.12 | 19.44 | 9.32 |
|  | Bootstrap 20 points | 8 | 16.6 | 8.6 |
|  | Bootstrap 40 points | 12.1 | 19.6 | 7.5 |
|  | Parametric bootstrap 20 points | 9.1 | 17.5 | 8.4 |
|  | Parametric bootstrap 40 points | 12 | 19.6 | 7.6 |

The uncertainty ranges in the means are consistent across all the methods.  The uncertainty ranges of variance and standard deviation appear to be less for bootstraping methods than for parametric methods.  This may be because the bootstrap approach of sampling with repalcement ends up drawing a subset of the sample at each bootstrap trial.  On average the variance of a subset of data is less than the variance of the sample data, due to being based on fewer independent data values since data values are sampled with replacement and hence repeated in the bootstrap samples.  This appears to be a shortcoming of the bootstrap approach.  This sampling effect only applies to the non-parametric bootstrap.  The parametric bootstrap bootstrap results were generated by taking σ2 = Ŝ2 = 13.3077 evaluated in problem 5.2, and then drawing bootstrap samples from the resulting distribution.  The true distribution for the bootstrap samples has variance Ŝ2.  The sample distribution for the bootstrap samples has variance (Ŝ*)2 which has confidence intervals given by 5.3.14.a, that has χ2 in the numerator, different from 5.3.14 b that had χ2 in the denominator.  Evaluating the interval in 5.3.14 a we get,

χ2n-1, 1-α/2  Ŝ2/(n-1)  ≤ (Ŝ*)2 ≤ χ2n-1, α/2  Ŝ2/(n-1)

= 8.91*13.30772/19 ≤ (Ŝ*)2 ≤ 32.85*13.30772/19

= 83 ≤ (Ŝ*)2 ≤ 306

This matches with the parametric boostrap simualtions.

5. a) 95% confidence limits on pre 1947 and post 1947 means.

flow= [ 1092	1099	1440	1083	1621	1132	935	1540	1966	775	1166	843	1508	1876	1696	1690	2730	1440	985	1346	1553	1370	743	1340	896	1600	2190	1600	714	794	1460	1240	1230	1270	861	1355	612	822	1370	1380	510	810	735	259	1290	1325	528	622	355	468	472	664	717	950];

time=[1921	1922	1923	1924	1925	1926	1927	1928	1929	1930	1931	1932	1933	1934	1935	1936	1937	1938	1939	1940	1941	1942	1943	1944	1945	1946	1947	1948	1949	1950	1951	1952	1953	1954	1955	1956	1957	1958	1959	1960	1961	1962	1963	1964	1965	1966	1967	1968	1969	1970	1971	1972	1973	1974];

pre=flow(1:27);% pre 1947 data. This includes 1947 data

post=flow(28:54);% post 1947 data.

B=1000;

n1=length(pre);

n2=length(post);

for ib=1:B;

rind1=ceil(rand(n1,1)*n1);

rind2=ceil(rand(n2,1)*n2);

xbspre=pre(rind1);

xbspost=post(rind2);

bsmeanpre(ib)=mean(xbspre);

bsmeanpost(ib)=mean(xbspost);

end

bsmeanpre=sort(bsmeanpre);

llimitbootpre= bsmeanpre(25)

ulimitbootpre =bsmeanpre(975)

bsmeanpost=sort(bsmeanpost);

llimitbootpost= bsmeanpost(25)

ulimitbootpost =bsmeanpost(975)

subplot(2,1,1);

hist(bsmeanpre);

xlabel('Pre 1947 mean');

ylabel('Frequency');

subplot(2,1,2);

hist(bsmeanpost);

xlabel('Post 1947 mean');

ylabel('Frequency');

llimitbootpre =

1.2320e+003

ulimitbootpre =

1.5614e+003

llimitbootpost =

751.0370

ulimitbootpost =

1.0434e+003

The 95% confidence limits for pre and post 1947 means,

1232 <µpre < 1561  and 751 <µpost < 1043  There is no overlap between the pre and post means; therefore based on confidence intervals we would deduce that the difference is statistically significant.

5.b)  Using bootstrap samples estimate 95% confidence limits on the difference between pre 1947 and post 1947 means.

Significance of difference

B=1000;

n1=length(pre);

n2=length(post);

for ib=1:B;

rind1=ceil(rand(n1,1)*n1);

rind2=ceil(rand(n2,1)*n2);

xbs1=pre(rind1);

xbs2=post(rind2);

bsdiff(ib)=mean(xbs1)-mean(xbs2);

end

bsdiff=sort(bsdiff);

ldiff=bsdiff(25)

udiff=bsdiff(975)

hist(bsdiff)

xlabel('Difference between \mu1 and \mu2');

find(bsdiff < 0);

ldiff =

275.6296

udiff =

704.0000

The 95% confidence limits from the bootstrap method on the difference between means is 275 < (µpre -µpost) < 704.

Since the range does not include zero, difference between the means is significant in this two sided test.

c) The null hypothesis is, Ho: T=µ1 –µ2=0.

alternate hypothesis is, H1: T > 0.

Where µ1-is pre 1947 mean and µ2 is the post 1947 mean.

p=length(find(bsdiff < 0))/B

p1=[1:length(bsdiff)]/B; %Empirical cumulative probabilities

tc=bsdiff(find(p1>= 0.05, 1))

% 'tc' gives the first value of the sorted difference between means, where the cumulative probabiity is greater than or equal to 0.05.

% tc is the critical value of the statistic T that defines the region of %rejection to its left at 0.05 level of significane.  Note that this is %a one sided test and hence 0.05 is not divided by two.

p =

0

tc =

304.7407

The test statistic T=0 (i.e µ1 = µ2) falls in the rejection region at 0.05 level of significance (left of the value tc=304.7).  The probability that the difference between means is ≤305 is 0.05 or there is .95 probability that the difference is greater than 305, i.e the difference between the means is statistically significant. Hence we reject the null hypothesis that the two means are similar and accpet the alternate hypothesis that µ1 > µ2.  We are saying µ1 > µ2, because we have defined our statistic as µ1-µ2 and differences are all positive.  Because no bootstrap sample resulted in a difference between means less than 0, the bootstrap estimate of the p value is zero, implying that we reject the hypothesis at all levels of significance.  This could be refined using a larger sample set, but is going to be a small number.

5.d)

B=1000;

n1=length(pre);

n2=length(post);

for ib=1:B;

rind1=ceil(rand(n1,1)*n1);

rind2=ceil(rand(n2,1)*n2);

xbspre=pre(rind1);

xbspost=post(rind2);

bsvarpre(ib)=var(xbspre);

bsvarpost(ib)=var(xbspost);

end

bsvarpre=sort(bsvarpre);

llimitbootpre= bsvarpre(25)

ulimitbootpre =bsvarpre(975)

bsvarpost=sort(bsvarpost);

llimitbootpost= bsvarpost(25)

ulimitbootpost =bsvarpost(975)

subplot(2,1,1);

hist(bsvarpre);

xlabel('Pre 1947 variance');

ylabel('Frequency');

subplot(2,1,2);

hist(bsvarpost);

xlabel('Post 1947 variance');

ylabel('Frequency');

llimitbootpre =

8.9182e+004

ulimitbootpre =

3.5126e+005

llimitbootpost =

9.5973e+004

ulimitbootpost =

1.9436e+005

The confidence limits on pre and post varainces are;

89182<σ2pre < 351260  and 95973 <σ2post < 194360.

There is considerable overlap between the variances, suggesting that variance has not changed.

5.e)

The null hypothesis is, Ho: T=σ1 –σ2=0.

alternate hypothesis is, H1:T ≠ 0.

Where σ1-is pre 1947 variance and σ2 is the post 1947 variance.  Unlike in the previous problem where we tested if one mean is greater than the other, here we are merely testing if the variances are different, hence it is a two sided test.

B=1000;

n1=length(pre);

n2=length(post);

for ib=1:B;

rind1=ceil(rand(n1,1)*n1);

rind2=ceil(rand(n2,1)*n2);

xbs1=pre(rind1);

xbs2=post(rind2);

bsdiff(ib)=var(xbs1)-var(xbs2);

end

bsdiff=sort(bsdiff);

ldiff=bsdiff(25)

udiff=bsdiff(975)

hist(bsdiff)

xlabel('Difference between  \sigma1 and  \sigma2');

p1=[1:length(bsdiff)]/B;%Empirical cumulative probabilities

F0=p1(find(bsdiff < 0,1,'last'))%F(0),see Note 1 below

if(F0 < 0.5)

p=2*F0

else

p=2*(1-F0)

end

tc1=bsdiff(find(p1>= 0.01/2, 1)) %see Note 2

tc2=bsdiff(find(p1>= (1-0.01/2), 1))

Note 1: F0 is the empirical probability that the differnce between variances is less than or equal to zero.

Note 2:  tc1 is the critical value of the statistic T, on one side of the distribution at which the p1 value is equal to 0.01/2.  Note that the level of significance 0.01 is divided by 2 to accommodate the two sided distribution. tc2 is the critical value on the other side of the distribution.

ldiff =

-6.4354e+004

udiff =

2.0985e+005

F0 =

0.2380

p =

0.4760

tc1 =

-1.0328e+005

tc2 =

2.4315e+005

Note that tc2 is not exactly equal to –tc1, because the distribution is empirical and not exactly symmetrical.

In this case, T=0 does not fall in the rejection region at 0.01 level of significance (Note that this is a two tailed test).   Hence we accept the hypothesis that the pre 1947 variance is same as the post 1947 variance.

Compare results from assignment 6, problem 5.10

In testing the difference between the means, both the methods (parametric approach in assignment 6 and bootstrap) gave similar p values and the hypothesis that the two means are similar was rejected.  The advantage of bootstrap is that it did not make any assumptions about the variability of the variance nor was it required to estimate the variance.

While testing variances, the p value got from bootstraping is rather high that supports accepting the hypothesis that the variances are similar.  This p valuse is not comparable with the one we got in the parametric approach in assignment 5, because the test statistic used here (T=σ1 –σ2) is different from the F-statitic used in assignement 5 that is a ratio of variances.