## Slide 1: Evapotranspiration
Be able to calculate evaporation from open water surfaces and transpiration from vegetation, using a method appropriate for the information available

## Slide 2: Standard Evaporation Rates
Potential Evaporation Eo [mm/day] is the quantity of water evaporated per unit area, per unit time from an idealized, extensive free water surface under existing atmospheric conditions.
Reference Crop Evaporation Erc [mm/day] is the rate of evaporation from an idealized grass crop with a fixed crop height of 0.12 m, an albedo of 0.23, and a surface resistance of 69 s/m
These assume
No shortage of water
Ignore influence of evaporation on meteorological parameters
Actual Evaporation E [mm/day]

## Slide 3: ET involves
Energy exchanges and energy balance
Turbulent diffusion into the atmosphere
Adjustment and balance
Rn
G
+
+
+
-
-
-

## Slide 4: Evaporative Energy Flux
MJ/kg
Evaporation rate E mm/day or m/s L/T
Mass evaporation rate wE kg/m2/day M L-2 T-1
Latent heat transfer rate
LE = v wE kJ/m2/hr or W/m2 E L-2 T-1

## Slide 5: Energy Budget for a Unit Area
Ad – loss of energy associated with horizontal air movement. Significant in an “oasis” situation, generally neglected.
P – energy absorbed by biochemical processes in the plants, typically 2% of net radiation
A = LE + H [MJ m-2 day-1]
A = Rn – G – S – P – Ad
Often
A = Rn – G
Rn – net incoming radiation
LE – outgoing energy as evaporation
S – energy temporarily stored within the volume
G – outgoing heat conduction into the soil

## Slide 6: Turbulent transfer near the ground
From Chow et al., 1988
=0.4 von Karman

## Slide 7
Ta
Ts
ea
es
Turbulent convection transports heat, vapor and momentum

## Slide 8: Vapor Transport
Td
ea
Ta
es(Ta)
The vapor pressure at the surface is es(Ts); the vapor pressure of the overlying air is relative humidity times es(Ta). The rate of evaporation is proportional to es – ea.

## Slide 9: Mass Transfer / Aerodynamic Method

## Slide 10: Bowen Ratio
- psychrometric constant
Using standard values for P and v the value is 0.066 [kPa/K]

## Slide 11: Bowen Ratio Energy Balance Method
A = Rn – G = LE + H = LE(1+)

## Slide 13: Combination Method Concepts
Rn – G = LE + H
Ta
es(Ta)
Ts
es(Ts)

## Slide 14: Combination or Penman Method

## Slide 15: Priestley Taylor Method
This is also sometimes taken as an estimate of equilibrium potential evapotranspiration for well watered surface

## Slide 16
From Brutsaert, 2005

## Slide 17
From Brutsaert, 2005

## Slide 18: Summary of ET Equations
Bowen Ratio
Mass Transfer
Combination
Priestly Taylor
What happens in these equations if the wind speed doubles?

## Slide 19: Evapotranspiration Feedbacks
Conditions adjust to varying inputs. Calculations can interpret adjustments, but should not be used to predict the effect of changing one variable without considering the adjustments of connected variables
Rn
G
+
+
+
-
-
-

## Slide 20: Water Balance Evaporation
Errors in quantifying the water balance terms all accumulate in the evaporation estimate

## Slide 21: Eddy Correlation Approach
is vertical wind velocity component fluctuation
is specific humidity fluctuation

## Slide 22: Evaporation Pan
1.21 m
255 mm
150 mm
U.S. Class A pan

## Slide 23: Method Information Requirements
RN
Mass Transfer
Bowen Ratio / Energy Balance
Combination