## Slide 1: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map

## Slide 2: Six Basic Course Elements
Lectures
  Powerpoint slides
  Video streaming
Readings
  Handouts and lecture synopses
Homework
  Computer exercises
  Hand exercises
Term Project
  Oral presentation
  HTML report
Class Interaction
  Email
  Discussion
Examinations
  Midterm, final

## Slide 3: Our Classroom
Dr David Tarboton
Students at Utah State University
Dr David Maidment Students at University of Texas at Austin
Dr Ayse Irmak Students at University of Nebraska - Lincoln

## Slide 4
B.E. in Agricultural Engineering (with First Class Honors) from University of Canterbury, Christchurch, New Zealand, 1972
MS, PhD in Civil Engineering from University of Illinois, 1974 and 1976, respectively
1981 – joined University of Texas at Austin as an Assistant Professor, and have been on the faculty ever since. Now Hussein M. AlHarthy Centennial Chair in Civil Engineering
Initiated the GIS in Water Resources course in 1991 – this is the 20th anniversary!
Worked with ESRI since 1994 on a GIS Hydro Preconference seminar for the ESRI Users Conference
Leader of the CUAHSI Hydrologic Information System project since 2004
David R. Maidment

## Slide 5: David Tarboton
Sc.D MIT 1990, Thesis: “The Analysis of River Basins and Channel Networks Using Digital Elevation Models”
  4 papers
  Fractal (space filling) River Networks
  Slope Scaling with Contributing Area
  On the Extraction of Channel Networks from Digital Elevation Data
  A Physical Basis for Drainage Density
  Relied on Fortran and C Codes. Largest grid analyzed 1719 x 1169 took days on MicroVAX and output results directly to tape due to insufficient disk space to hold results. Visualized using primitive XY and array plotting code.
1996 - Developed D-Infinity to have a better contributing area for study of landscape evolution – published 1997.
1997 - Contract to develop user friendly slope-stability tool based on D-infinity contributing area. Led to SINMAP developed for ArcView 3, the first GIS software I used.
Gradually adapted the set of Fortran and C codes that had accumulated from above research to use ESRI grid format and be distributable as TARDEM/TauDEM
Participated in GISWR since 1999 (this year is the 12th time – I skipped 2007 while working on WATERS Network conceptual design)

## Slide 6
M.E. (1998) & Ph.D (2002). Agricultural and Biological Engineering. University of Florida. Gainesville, FL. Dissertation: “Linking multiple layers of information to explain soybean yield variability” . 5 papers
  Linking multi-variables for diagnosing causes of spatial yield variability
  Analysis of spatial yield variability using a combined crop model-empirical approach
  Estimating spatially variable soil properties for crop model use
  Relationship between plant available soil water and yield
  Artificial neural network as a data analysis tool in precision farming
2004- Joined to UNL and continued to work on computer simulation of crop production for another year and gradually moved to Remote Sensing field with applications in Natural Resources Systems.
2006 - Remote Sensing-based Estimation of Evapotranspiration and other Surface Energy Fluxes
2008- Working on development of the Nebraska Hydrologic Information System (HIS), which is designed to provide improved access to evapotranspiration and other hydrologic data for end users.
Participated in GISWR since 2006 (this year is the 5th time – I skipped 2007 due to position change at UNL)
Ayse Irmak

## Slide 7: University Without Walls
Traditional Classroom
Community
Inside and Outside
The Classroom

## Slide 8: Learning Styles
Instructor-Centered Presentation
Community-Centered Presentation
Student
Instructor
We learn from the instructors and each other

## Slide 9: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map

## Slide 10: Geographic Data Model
Conceptual Model – a set of concepts that describe a subject and allow reasoning about it
Mathematical Model – a conceptual model expressed in symbols and equations
Data Model – a conceptual model expressed in a data structure (e.g. ascii files, Excel tables, …..)
Geographic Data Model – a conceptual model for describing and reasoning about the world expressed in a GIS database

## Slide 11
Data Model based on Inventory of data layers

## Slide 12: Spatial Data: Vector format
Point - a pair of x and y coordinates
(x1,y1)
Line - a sequence of points
Polygon - a closed set of lines
Node
vertex
Vector data are defined spatially:
Notes: DRM

## Slide 13: Themes or Data Layers
Vector data: point, line or polygon features

## Slide 14: Kissimmee watershed, Florida
Themes

## Slide 15: Attributes of a Selected Feature

## Slide 16: Raster and Vector Data
Point
Line
Polygon
Vector
Raster
Raster data are described by a cell grid, one value per cell
Zone of cells
Notes: DRM

## Slide 17
http://srtm.usgs.gov/srtmimagegallery/index.html
Santa Barbara, California

## Slide 18: The challenge of increasing Digital Elevation Model (DEM) resolution (Dr Tarboton’s research)
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10-30 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2

## Slide 19: How do we combine these data?
Digital Elevation
Models
Watersheds
Streams
Waterbodies

## Slide 20: An integrated raster-vector database

## Slide 21: Remote Sensing Coverage of Nebraska
P33R30
10
P32R30
9
P31R30
10
P30R30
9
P29R30
10
P33R31
11
P32R31
10
P31R31
12
P30R31
9
P29R31
11
P28R31
8
P33R32
15
P32R32
8
P31R32
12
P30R32
10
P29R32
12
P28R32
10
P27R32
8

## Slide 22: Evaporation from Remote Sensing (Dr Irmak)

## Slide 23: Data intensive science synthesizes large quantities of information (Hey et al., 2009).
exploiting advanced computational capability for the analysis and integration of large new datasets to elucidate complex and emergent behavior
In hydrology, the image at left (Ralph et al., 2006) illustrates connection between extreme floods recorded in USGS stream gages and atmospheric water vapor from space based sensors
Satellite remote sensing and massive datasets enhance understanding of multi-scale complexity in processes such as rainfall and river networks

## Slide 24: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map

## Slide 25: Linking Geographic Information Systems and Water Resources
GIS
Water
Resources

## Slide 26: A Key Challenge
GIS
Water Environment
(Watersheds, streams, gages, sampling points)
How to connect water environment with water observations
Time Series Data
Water Observations
(Flow, water level concentration)

## Slide 27
CUAHSI is a consortium representing 125 US universities
Supported by the National Science Foundation Earth Science Division
Advances hydrologic science in nation’s universities
Includes a Hydrologic Information System project
http://www.cuahsi.org

## Slide 28: How the web works
Catalog (Google)
Web Server
(CNN.com)
Browser
(Firefox)
Access
Catalog harvest
Search
HTML – web language for text and pictures

## Slide 29
Rainfall
Water quantity
Meteorology
Soil water
Groundwater
We Collect Lots of Water Data
Water quality

## Slide 30: The Data have a Common Structure
A point location in space
A series of values in time
Gaging – regular time series
Sampling – irregular time series
Notes: These data are recorded over time to monitor a hydrologic process or property.

## Slide 31: Services-Oriented Architecture for Water Data
Catalog
Server
User
Data access
Service registration
Search
Catalog harvest
WaterML – web language for water data

## Slide 32: What is a “services-oriented architecture”? Networks of computers connected through the web …….
Everything is a service
  Data, models, visualization, ……
A service receives requests and provides responses using web standards (WSDL)
It uses customized web languages
  HTML (HyperText Markup Language) for text and pictures
  WaterML for water time series (CUAHSI/OGC)
  GML for geospatial coverages (OGC)
….. supporting a wide range of users

## Slide 33: WaterML as a Web Language for Colorado River at Austin
http://waterservices.usgs.gov/nwis/iv?sites=08158000&period=P7D&parameterCd=00060
I accessed this WaterML service from USGS at 11:22AM
and got back these flow data from USGS which are up to 10:45AM
USGS has real-time WaterML services for about 22,000 sites available 24/7/365
http://waterservices.usgs.gov/nwis/iv?sites=08158000&period=P7D&parameterCd=00060

## Slide 34: CUAHSI Water Data Services Catalog
69 public services
18,000 variables
1.9 million sites
23 million series
5.1 billion data values
And growing
The largest water data catalog in the world
maintained at the San Diego Supercomputer Center
All the data comes out in WaterML

## Slide 35: CUAHSI HIS
HydroServer – Data Publication
Lake Powell Inflow and Storage
HydroDesktop – Data Access and Analysis
HydroDesktop – Combining multiple data sources
HydroCatalog
Data Discovery
The CUAHSI Hydrologic Information System (HIS) is an internet based system to support the sharing of hydrologic data. It is comprised of hydrologic databases and servers connected through web services as well as software for data publication, discovery and access.

## Slide 36: Organize Water Data Into “Themes”
Integrating Water Data Services From Multiple Agencies
. . . Across Groups of Organizations

## Slide 37
Bringing Water Into GIS Thematic Maps of Water Observations as GIS Layers
Groundwater
Salinity
Streamflow
Unified access to water data in Texas ….

## Slide 38: Geospatial Data Services
ArcGIS Online
ArcGIS Server
ArcGIS Desktop
Data access
Service registration
Search
Catalog harvest
Map services – web language for geospatial data

## Slide 39: ArcGIS Online
GIS on the web – online map services
http://www.arcgis.com

## Slide 40: Topographic Base Map in ArcGIS Online
World
United States
Texas
Austin
Home

## Slide 41
Arc Hydro: GIS for Water Resources
Arc Hydro
  An ArcGIS data model for water resources
  Arc Hydro toolset for implementation
  Framework for linking hydrologic simulation models
The most comprehensive terrain analysis and watershed toolset available
Work of Dean Djokic and his team at ESRI Water Resources Applications
Published in 2002

## Slide 42
Arc Hydro Groundwater: GIS For Hydrogeology
Describes the data model – public domain
Toolset and data model available now from Aquaveo
Book from ESRI Press, published in Spring 2011
Adapted for a National Groundwater Information System for Australia

## Slide 46
Hydrologic Information System
Analysis, Modeling,
Decision Making
Arc Hydro
Geodatabase
A synthesis of geospatial and temporal data supporting hydrologic analysis and modeling

## Slide 47: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map

## Slide 48: Origin of Geographic Coordinates
(0,0)
Equator
Prime Meridian

## Slide 49: Latitude and Longitude
Longitude line (Meridian)
N
S
W
E
Range: 180ºW - 0º - 180ºE
Latitude line (Parallel)
N
S
W
E
Range: 90ºS - 0º - 90ºN
(0ºN, 0ºE)
Equator, Prime Meridian

## Slide 50: Latitude and Longitude in North America
90 W
120 W
60 W
30 N
0 N
60 N
Austin:
Logan:
Lincoln:
(30°18' 22" N, 97°45' 3" W)
(41°44' 24" N, 111°50' 9" W)
40 50 59 96 45 0
(40°50' 59" N, 96°45' 0" W)

## Slide 51: Map Projection
Curved Earth
Geographic coordinates: f, l
(Latitude & Longitude)
Flat Map
Cartesian coordinates: x,y
(Easting & Northing)
Notes: DRM

## Slide 52: Earth to Globe to Map
Representative Fraction
Globe distance Earth distance
=
Map Scale:
Map Projection:
Scale Factor
Map distance Globe distance
=
(e.g. 1:24,000)
(e.g. 0.9996)

## Slide 53: Coordinate Systems
(fo,lo)
(xo,yo)
X
Y
Origin
A planar coordinate system is defined by a pair
of orthogonal (x,y) axes drawn through an origin

## Slide 54: Summary (1)
GIS in Water Resources is about empowerment through use of information technology – helping you to understand the world around you and to investigate problems of interest to you
This is an “open class” in every sense where we learn from one another as well as from the instructors

## Slide 55: Summary (2)
GIS offers a structured information model for working with geospatial data that describe the “water environment” (watersheds, streams, lakes, land use, ….)
Water resources also needs observations and modeling to describe “the water” (discharge, water quality, water level, precipitation)

## Slide 56: Summary (3)
A Hydrologic Information System depends on water web services and integrates spatial and temporal water resources data
Geography “brings things together” through georeferencing on the earth’s surface
Understanding geolocation on the earth and working with geospatial coordinate systems is fundamental to this field