## Slide 1: Key Spatial Analysis Concepts from Exercise 3
Contours and Hillshade to visualize topography

## Slide 2: Zonal Average of Raster over Subwatershed
Join

## Slide 3: Subwatershed Precipitation by Thiessen Polygons
Thiessen Polygons
Intersect with Subwatersheds
Evaluate A*P Product
Summarize by subwatershed

## Slide 4: Subwatershed Precipitation by Interpolation
Kriging (on Precip field)
Zonal Statistics (Mean)
Join
Export

## Slide 5: Runoff Coefficients
Interpolated precip for each subwatershed
Convert to volume, P
Sum over upstream subwatersheds in Excel
Runoff volume, Q
Ratio of Q/P
Watershed | HydroID's
Plum Ck at Lockhart, TX | 330
Blanco Rv nr Kyle, TX | 331, 332
San Marcos Rv at Luling, TX | 331,332,333,336

## Slide 6: Digital Elevation Model Based Watershed and Stream Network Delineation
Readings
At http://resources.arcgis.com, in the Desktop | Geoprocessing | Tool Reference | Spatial Analyst Toolbox Hydrology Toolset start from “An overview of the Hydrology tools” http://resources.arcgis.com/en/help/main/10.1/index.html#//009z0000004w000000 and read to end of Hydrologic analysis sample applications in the Hydrology toolset concepts section
Understanding
How to use

## Slide 7: The Terrain Flow Information Model
Pit removal
Flow direction field derivation
Flow Accumulation
Channels and Watersheds
Raster to Vector Connection

## Slide 8: The terrain flow information model for deriving channels, watersheds, and flow related terrain information.
Raw DEM
Pit Removal (Filling)
Flow Field
Channels, Watersheds, Flow Related Terrain Information
Watersheds are the most basic hydrologic landscape elements
Notes: This slide shows the general model for deriving flow field related derivative surfaces from digital elevation data. The input is a raw digital elevation model, generally elevation values on a grid. This is basic information used to derive further hydrology related spatial fields that enrich the information content of this basic data. The first step is to remove sinks, either by filling, or carving. Then a flow field is defined. This enables the calculation of flow related terrain information. My focus has been on flow related information working within this framework. I try to leave other GIS functionality, like radiation exposure, line of sight analyses and visualization to others. I have distributed my software in ways that it easily plugs in to mainstream systems, such as ArcGIS to enhance ease of use.

## Slide 9: DEM Elevations
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 10: The Pit Removal Problem
DEM creation results in artificial pits in the landscape
A pit is a set of one or more cells which has no downstream cells around it
Unless these pits are removed they become sinks and isolate portions of the watershed
Pit removal is first thing done with a DEM

## Slide 11: Pit Filling
Increase elevation to the pour point elevation until the pit drains to a neighbor

## Slide 12: Pit Filling
Pits
Pour Points
Original DEM
Pits Filled
Notes: Elevations are filled to that of the pools pour point

## Slide 14
80
74
63
69
67
56
60
52
48
80
74
63
69
67
56
60
52
48
30
Slope:
Hydrologic Slope
- Direction of Steepest Descent
30

## Slide 15
2
2
4
4
8
1
4
16
1
2
4
8
4
4
1
2
4
8
2
4
4
4
4
2
1
Eight Direction (D8) Flow Model
32
16
8
64
4
128
1
2

## Slide 16: Flow Direction Grid
32
16
8
64
4
128
1
2

## Slide 17
Grid Network

## Slide 18
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
14
4
1
19
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
Flow Accumulation Grid.
Area draining in to a grid cell
Link to Grid calculator
ArcHydro Page 72

## Slide 19
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
Flow Accumulation > 10 Cell Threshold
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
1
0
4
1
1
10
14
19
Stream Network for 10 cell Threshold Drainage Area

## Slide 20
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
2
5
15
20
2
The area draining each grid cell includes the grid cell itself.
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
5
2
2
25
15
TauDEM contributing area convention.

## Slide 21: Streams with 200 cell Threshold (>18 hectares or 13.5 acres drainage area)

## Slide 22
Watershed Draining to Outlet

## Slide 23: Watershed and Drainage Paths Delineated from 30m DEM
Automated method is more consistent than hand delineation

## Slide 24
ArcHydro Page 74
172
201
204
202
206
203
209
Each link has a unique identifying number
Stream Segments

## Slide 25
Vectorized Streams Linked Using Grid Code to Cell Equivalents
Vector
Streams
Grid
Streams
ArcHydro Page 75

## Slide 26
DrainageLines are drawn through the centers of cells on the stream links. DrainagePoints are located at the centers of the outlet cells of the catchments
ArcHydro Page 75

## Slide 27: Catchments
For every stream segment, there is a corresponding catchment
Catchments are a tessellation of the landscape through a set of physical rules

## Slide 28: Raster Zones and Vector Polygons
Catchment GridID
Vector Polygons
DEM GridCode
Raster Zones
3
4
5
One to one connection

## Slide 29
Catchments, DrainageLines and DrainagePoints of the San Marcos basin
ArcHydro Page 75

## Slide 30
Catchment, Watershed, Subwatershed.
ArcHydro Page 76
Watershed outlet points may lie within the interior of a catchment, e.g. at a USGS stream-gaging site.
Catchments
Subwatersheds
Watershed

## Slide 31: Advanced Considerations
Using vector stream information (DEM reconditioning)
Enhanced pit removal
Channelization threshold selection
Computational considerations

## Slide 32
+
=
 Take a mapped stream network and a DEM
 Make a grid of the streams
 Raise the off-stream DEM cells by an arbitrary elevation
increment
 Produces "burned in" DEM streams = mapped streams
“Burning In” the Streams

## Slide 33
AGREE Elevation Grid Modification Methodology – DEM Reconditioning

## Slide 34: Carving
Lower elevation of neighbor along a predefined drainage path until the pit drains to the outlet point

## Slide 35: Carving
Pits
Carve outlets
Original DEM
Carved DEM
Notes: Elevations are filled to that of the pools pour point

## Slide 36
Filling
Carving
Minimizing Alterations

## Slide 37: Minimizing DEM Alterations
Optimally adjusted
Pits
Original DEM
Carved
Filled
Notes: Elevations are filled to that of the pools pour point

## Slide 38: How to decide on stream delineation threshold ?
AREA 1
AREA 2
3
12
Why is it important?

## Slide 39: Delineation of Channel Networks and Catchments
500 cell theshold
1000 cell theshold

## Slide 40
Hydrologic processes are different on hillslopes and in channels. It is important to recognize this and account for this in models.
Drainage area can be concentrated or dispersed (specific catchment area) representing concentrated or dispersed flow.

## Slide 41: Examples of differently textured topography
Badlands in Death Valley. from Easterbrook, 1993, p 140.
Coos Bay, Oregon Coast Range.
from W. E. Dietrich

## Slide 42: Gently Sloping Convex Landscape
From W. E. Dietrich

## Slide 43: Topographic Texture and Drainage Density
Same scale, 20 m contour interval
Sunland, CA
Driftwood, PA

## Slide 44
Lets look at some geomorphology.
    Drainage Density
    Horton’s Laws
    Slope – Area scaling
    Stream Drops
“landscape dissection into distinct valleys is limited by a threshold of channelization that sets a finite scale to the landscape.” (Montgomery and Dietrich, 1992, Science, vol. 255 p. 826.)
Suggestion: One contributing area threshold does not fit all watersheds.

## Slide 45: Drainage Density
Dd = L/A
Hillslope length  1/2Dd
L
B
B
Hillslope length = B
A = 2B L
Dd = L/A = 1/2B
 B= 1/2Dd

## Slide 46: Drainage Density for Different Support Area Thresholds
EPA Reach Files
100 grid cell threshold
1000 grid cell threshold

## Slide 47: Drainage Density Versus Contributing Area Threshold

## Slide 48: Hortons Laws: Strahler system for stream ordering
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
2
3

## Slide 49: Length Ratio

## Slide 50: Slope Ratio

## Slide 51: Constant Stream Drops Law
Broscoe, A. J., (1959), "Quantitative analysis of longitudinal stream profiles of small watersheds," Office of Naval Research, Project NR 389-042, Technical Report No. 18, Department of Geology, Columbia University, New York.

## Slide 52: Stream Drop Elevation difference between ends of stream
Note that a “Strahler stream” comprises a sequence of links (reaches or segments) of the same order
Nodes
Links
Single Stream

## Slide 53: Suggestion: Map channel networks from the DEM at the finest resolution consistent with observed channel network geomorphology ‘laws’.
Look for statistically significant break in constant stream drop property as stream delineation threshold is reduced
Break in slope versus contributing area relationship
Physical basis in the form instability theory of Smith and Bretherton (1972), see Tarboton et al. 1992

## Slide 54: Statistical Analysis of Stream Drops

## Slide 55: T-Test for Difference in Mean Values
72
130
0
T-test checks whether difference in means is large (> 2)
when compared to the spread of the data around the mean values

## Slide 56: Constant Support Area Threshold

## Slide 57
100 grid cell constant support area threshold stream delineation

## Slide 58
200 grid cell constant support area based stream delineation

## Slide 59: Local Curvature Computation (Peuker and Douglas, 1975, Comput. Graphics Image Proc. 4:375)
43
41
48
47
48
47
54
51
54
51
56
58

## Slide 60: Contributing area of upwards curved grid cells only

## Slide 61: Upward Curved Contributing Area Threshold

## Slide 62
Curvature based stream delineation

## Slide 63: Channel network delineation, other options
1
1
1
1
1
1
1
1
1
1
1
1
1
1
4
3
3
12
2
2
2
3
16
25
6
Contributing Area
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
3
1
1
1
2
3
3
2
Grid Order
4
5
6
3
7
2
1
8

## Slide 64
Grid network pruned to order 4 stream delineation

## Slide 65: The challenge of increasing Digital Elevation Model (DEM) resolution
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10-30 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2

## Slide 66: Computational Considerations – A Parallel Programming Approach
Improved runtime efficiency
Capability to run larger problems
Row oriented slices
Each process includes one buffer row on either side
Each process does not change buffer row

## Slide 67: Pit Removal: Planchon Fill Algorithm
Initialization
1st Pass
2nd Pass
Planchon, O., and F. Darboux (2001), A fast, simple and versatile algorithm to fill the depressions of digital elevation models, Catena(46), 159-176.

## Slide 68: Parallel Scheme
Communicate
Initialize( D,P) Do for all i in P if D(i) > n P(i) ← D(i) Else P(i) ← n endfor Send( topRow, rank-1 ) Send( bottomRow, rank+1 ) Recv( rowBelow, rank+1 ) Recv( rowAbove, rank-1 ) Until P is not modified
D denotes the original elevation.
P denotes the pit filled elevation.
n denotes lowest neighboring elevation
i denotes the cell being evaluated

## Slide 69: Improved runtime efficiency
Parallel Pit Remove timing for NEDB test dataset (14849 x 27174 cells  1.6 GB).
128 processor cluster
16 diskless Dell SC1435 compute nodes, each with 2.0GHz dual quad-core AMD Opteron 2350 processors with 8GB RAM
8 processor PC
Dual quad-core Xeon E5405 2.0GHz PC with 16GB RAM

## Slide 70: Capabilities Summary
Capability to run larger problems |  |  |  | 
 |  | Processors used | Grid size | 
 |  |  | Theoretcal limit | Largest run
2008 | TauDEM 4 | 1 | 0.22 GB | 0.22 GB
Sept 2009 | Partial implement-ation | 8 | 4 GB | 1.6 GB
June 2010 | TauDEM 5 | 8 | 4 GB | 4 GB
Sept 2010 | Multifile on 48 GB RAM PC | 4 | Hardware limits | 6 GB
Sept 2010 | Multifile on cluster with 128 GB RAM | 128 | Hardware limits | 11 GB
1.6 GB
0.22 GB
4 GB
6 GB
11 GB
At 10 m grid cell size
Single GeoTIFF file size limit 4GB

## Slide 71: Summary of Key Processing Steps
[DEM Reconditioning]
Pit Removal (Fill Sinks)
Flow Direction
Flow Accumulation
Stream Definition
Stream Segmentation
Catchment Grid Delineation
Raster to Vector Conversion (Catchment Polygon, Drainage Line, Catchment Outlet Points)

## Slide 72: Summary Concepts
The eight direction pour point model approximates the surface flow using eight discrete grid directions
The elevation surface represented by a grid digital elevation model is used to derive surfaces representing other hydrologic variables of interest such as
  Slope
  Flow direction
  Drainage area
  Catchments, watersheds and channel networks

## Slide 73: Summary Concepts (2)
Hydrologic processes are different between hillslopes and channels
Drainage density defines the average spacing between streams and the representative length of hillslopes
The constant drop property provides a basis for selecting channel delineation criteria to preserve the natural drainage density of the topography
Generalized channel delineation criteria can represent spatial variability in the topographic texture and drainage density

## Slide 74: Are there any questions ?
AREA 1
AREA 2
3
12