## Slide 1: Data Sources for GIS in Water Resources by David R. Maidment, and David G. Tarboton GIS in Water Resources Fall 2014

## Slide 2: Outline
The hierarchical system of watersheds and basins
Where to obtain data and maps
  National/State/Global Data repositories
  Hydrography
  USGS National Water Information System
  Land Cover
  Elevation
  Soil (Statsgo/Surgo)
  Weather
Ideas for term projects

## Slide 3: Water Resources Regions of the US
Region 01 New England Region 02 Mid-Atlantic Region 03 South Atlantic-Gulf Region 04 Great Lakes Region 05 Ohio Region 06 Tennessee Region 07 Upper Mississippi Region 08 Lower Mississippi Region 09 Souris-Red-Rainy Region 10 Missouri Region 11 Arkansas-White-Red Region 12 Texas-Gulf Region 13 Rio Grande Region 14 Upper Colorado Region 15 Lower Colorado Region 16 Great Basin Region 17 Pacific Northwest Region 18 California Region 19 Alaska (Old numbering system) Region 20 Hawaii Region 21 Caribbean
There are 21 water resources regions in the United States
Eighteen 2-digit water resource regions in the Contiguous US

## Slide 4: Watershed Hierarchy
8 HUC
4
2
6
NHDPlus
10
12
Digit #
Each hydrologic unit is identified by a unique hydrologic unit code (HUC) consisting of two to or more digits based on the levels of classification in the hydrologic unit system.
HAW HUC 8 03030002
Little Creek HUC 12 030300020603

## Slide 5: Hydrologic Unit Code Watersheds
~ 2000 HUC 8 for US, about the size of counties

## Slide 6: Watershed Boundary Dataset
National Program by USGS and USDA (NRCS)
Boundaries for 10- and 12- digit watersheds
First cut is by automated delineation from NED
Hand checked and edited
10-digit watersheds
http://nhd.usgs.gov/wbd.html

## Slide 7: The National Map
http://nationalmap.gov/
A central source for US Government data

## Slide 8
River networks
for 8-digit HUC
watersheds
http://nhd.usgs.gov/

## Slide 10
Slope
Elevation
Mean annual flow
  Corresponding velocity
Drainage area
% of upstream drainage area in different land uses
Stream order
http://www.horizon-systems.com/nhdplus/

## Slide 11: River Reach Codes Used for river address locations
ReachCode =
12030102000151
ReachCode = 12030102000005
HUC#
Segment#
Location 0.392
on Reach
12030102000005

## Slide 12: National Elevation Dataset
Digital Elevation Model with 1 arc-second (30m), 1/3 arc-second (10m) and some 1/9 arc second (3m) cells
Distributed as part of the National Map
10 billion data
Derived from USGS 1:24,000 quadrangle sheets and at higher resolution from LIDAR
Get the data:
http://ned.usgs.gov/
http://nationalmap.gov/viewer.html

## Slide 13: National Elevation Dataset Availability
From http://nationalmap.gov/viewer.html

## Slide 14: Digital Elevation Model (DEM)
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 15
Digital Elevation Model (DEM)-30 meter

## Slide 16: Austin West 30 Meter DEM

## Slide 17
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
Water in a given cell flows one or more of eight adjacent cells in the direction of steepest descent (ArcGIS)
ArcGIS raster operations involved in watershed delineation are derived from the premise that “water flows downhill, in doing so, will follow the steepest descent

## Slide 18: Flow Direction Grid
32
16
8
64
4
128
1
2

## Slide 19: Delineation of Streams and Watersheds on a DEM

## Slide 20
http://srtm.usgs.gov/

## Slide 21: HydroSheds derived from SRTM
http://hydrosheds.cr.usgs.gov/

## Slide 23: GTOPO30 - 1 km Digital Elevation Model of the Earth
https://lta.cr.usgs.gov/GTOPO30

## Slide 24: Drainage in North America
Hydro1K is
derived from
GTOPO30
using raster
GIS analysis
https://lta.cr.usgs.gov/HYDRO1K

## Slide 25: Soil Data
Natural Resources Conservation Service (NRCS)
State Soil Geographic Database-STATSGO
Soil Survey Geographic Database- SSURGO
http://www.nrcs.usda.gov/wps/portal/nrcs/site/soils/home/
http://websoilsurvey.sc.egov.usda.gov/App/WebSoilSurvey.aspx
http://datagateway.nrcs.usda.gov/

## Slide 26
1:250,000 Scale Soil Information
http://datagateway.nrcs.usda.gov/

## Slide 27
1:24,000 scale
soil information
SSURGO:
County Level
Digital Soil Maps
http://websoilsurvey.nrcs.usda.gov/DataAvailability/SoilDataAvailabilityMap.pdf

## Slide 28: Ssurgo for Travis County
103 soil map units described by 7530 polygons of average area 35.37 ha (87 acres)

## Slide 29
http://landcover.usgs.gov/

## Slide 30: National Land Cover Dataset
Get the data:
http://www.mrlc.gov/
1992, 2001, 2006 and 2011

## Slide 32
http://www.nationalatlas.gov/atlasftp.html

## Slide 33: www.climate.gov

## Slide 34
http://www.ncdc.noaa.gov/oa/ncdc.html

## Slide 35: PRISM Mean Annual Precipitation (Oregon State U.)
http://www.wcc.nrcs.usda.gov/climate/prism.html

## Slide 36: National Water Information System
Web access to USGS water
resources data in real time
http://waterdata.usgs.gov/usa/nwis/

## Slide 37: USGS Water Watch
Web access to USGS water resources data in real time
http://waterdata.usgs.gov/nwis/rt

## Slide 38: USGS National Water Information System.
Real-time and Historic Data
  Streamflow and stage
  Groundwater levels
  Water Quality
  Site information
Tabular or Graphical Format

## Slide 39: http://water.weather.gov/ahps/

## Slide 40: http://water.weather.gov/ahps/

## Slide 41: http://enviroatlas.epa.gov/enviroatlas/

## Slide 42: EnviroAtlas
All data is available for download
Some data is available for download as web service

## Slide 43
http://www.wcc.nrcs.usda.gov/snotel/

## Slide 44
SNOTEL System for Measuring Snow and Supporting Spring Runoff and Water Supply Forecasts

## Slide 45: USU Doc Daniels SNOTEL Site

## Slide 46: Measuring SWE

## Slide 47: http://www.cbrfc.noaa.gov

## Slide 48: CBRFC SNOTEL Ensemble
http://www.cbrfc.noaa.gov/station/sweplot/sweplot.cgi?tglu1

## Slide 49
Texas Natural Resource Information System http://www.tnris.org/

## Slide 50: TWDB http://www.twdb.state.tx.us/mapping/gisdata.asp

## Slide 51: http://gis.utah.gov

## Slide 52: Utah Terrain Basemap
To use as a basemap in ArcGIS see instructions at
http://gis.utah.gov/map-services/new-utah-terrain-base-map-and-cached-tile-service-available

## Slide 53
Utah GIS Portal Download GIS Data
http://gis.utah.gov/data/

## Slide 54
http://geology.utah.gov/maps/gis/index.htm

## Slide 55
http://www.wrcc.dri.edu/

## Slide 56: Bear River Watershed
http://www.bearriverinfo.org/

## Slide 57: Great Salt Lake Info System
http://greatsaltlakeinfo.org/

## Slide 58: http://www.nconemap.com/

## Slide 59: http://www.ncfloodmaps.com/

## Slide 60: What is Cloud Computing? Following Slides are from Dr Kristin Tolle, Microsoft Research Connections
Notes: Slide Objectives:
Main points you want to make
Transition:
Transition statement(s) to setup the slide
Speaking Points:
Speaking Point #1
Speaking Point #2
Notes:

## Slide 61: Global Footprint
Where is the Cloud?
Notes: Speaking Points:
Windows Azure itself is deployed around the world
With Windows Azure, we have a concept of regions, which is where you choose to place your code and run.
In each of the regions, we have a Microsoft datacenter.
These datacenters are massive facilities that host 10s or in some cases hundreds of thousands of servers
We have currently four regions in North America, two regions in Europe, and two in Asia
As you can see on this slide we also have a number of CDN edge points, which we can use to cache your content and deliver it even faster for customers. %
What you’re going to see in the next couple months and years is that we will rapidly expand our datacenter footprint around the world, so you will have more options for running your applications.
Once you build an application, you can choose where you want to run in the world and you can move your workloads from region to region.
You can also run your application in multiple regions simultaneously and just direct traffic and customers to whichever version of the app is closest to them.
That gives you a global footprint and a chance to reach a bigger customer base or audience in new markets
Notes:
Windows Azure services such as compute and storage are now available in 8 worldwide datacenters with an additional 24 Content Delivery Network endpoints.
You can’t have a real cloud without a data center.

## Slide 62: Microsoft’s Data Center Evolution
  Chicago and Dublin Generation 3
  Data Center Co-Location Generation 1
  Modular Data Center Generation 4
  Quincy and San Antonio Generation 2
Time to Market
Lower TCO
Scalability & Sustainability
Rack
Density & Deployment
Server
Capacity
Containers
IT PAC
  Deployment Scale Unit
Notes: Slide Objectives:
Main points you want to make
Transition:
Transition statement(s) to setup the slide
Speaking Points:
Speaking Point #1
Speaking Point #2
Notes:

## Slide 63: ArcGIS Online: Maps about the Earth
http://www.arcgis.com/features/maps/earth.html
Land Cover
Soils
Elevation

## Slide 64: ArcGIS Online Services
http://landscape1.arcgis.com/arcgis/services/
http://landscape2.arcgis.com/arcgis/services/
http://landscape3.arcgis.com/arcgis/services/
http://elevation.arcgis.com/arcgis/services/
http://hydro.arcgis.com/arcgis/services

## Slide 65: ArcGIS Services are Accessed through Catalog

## Slide 66: Elevation Services

## Slide 67: Dynamic Map Services

## Slide 68: Extract the NHDPlus Flowlines

## Slide 69: Elevation Profile of the Blanco River
Chart: Blanco River Elevation Profile
Slope = 0.2%

## Slide 70: Summary
There are a plethora of data sources available
Knowing what is available is important to scope GIS analyses and projects
GIS is about creating knowledge, telling stories, making decisions – all involve integrating information from multiple sources
The way that data is organized can enhance or inhibit the analyses that can be done
Data dissemination is increasingly becoming service based

## Slide 71: Term paper suggestions
Your own research
An integration of information from multiple sources to address a problem or question of interest
A tool for doing something in GIS (python programming)
A map or dataset in ArcGIS online

## Slide 72: Term paper suggestions continued
An examination of land cover change
  Deforestation
  Urban reforestation
  Impact of change on the water system
Flood plain mapping
  Examination of alternatives and changes to reduce flooding (impervious areas, obstructions) (NC Flood Maps)
Prioritize watershed restoration (river restoration and upland changes) (EnviroAtlas and NC specific sources)
  NC DENR project to prioritize HUC 12s within each HUC8 for mitigation
  Mitigation bankers, conservation organizations
  Based on length of degraded streams
  Impervious surface area
  Other ecosystem services (heat island, carbon sequestration)
  Composite weight
  Examine sensitivity to change using models (SWAT, RHESSys)
Riparian buffers
  An examination of land use and land cover in riparian buffer and mapping the quality of buffer and length of flow through buffer. TauDEM has some buffer flow length functions that could be used.
Terrain stability analysis
  Based on DEM Slope, contributing area – e.g. SINMAP
Stream bank stability analysis
  Based on flow, slope and channel conditions (NC Flood maps)