## Slide 1: Digital Elevation Model Based Watershed and Stream Network Delineation
Understanding
How to use
Reading
http://resources.arcgis.com/en/help/main/10.2/index.html#//009z0000004w000000

## Slide 2: Outline
Key Concepts from Exercise 3
Work the 2nd half of Exercise 3
DEM Pit removal
Flow direction field derivation
Flow Accumulation
Channels and Watersheds
Raster to Vector Connection
Using vector stream information (DEM reconditioning)
Enhanced pit removal

## Slide 3: Key Spatial Analysis Concepts from Exercise 3
Contours and Hillshade to visualize topography

## Slide 4: Zonal Average of Raster over Subwatershed
Join

## Slide 5: Subwatershed Precipitation by Thiessen Polygons
Thiessen Polygons
Intersect with Subwatersheds
Evaluate A*P Product
Summarize by subwatershed

## Slide 6: What Is Involved?
Add Field

## Slide 7: Field Calculator to Multiply A and P

## Slide 8: Summarize (Sum) for unique subwatersheds (by HydroID)

## Slide 9: Now use field calculator to take the ratio

## Slide 10: Subwatershed Precipitation by Interpolation
Kriging (on Precip field)
Zonal Statistics (Mean)
Join
Export

## Slide 11: Runoff Coefficients
Interpolated precip for each subwatershed
Convert to volume, P
Sum over upstream subwatersheds in Excel
Runoff volume, Q
Ratio of Q/P
Watershed | HydroID's
Plum Ck at Lockhart, TX | 330
Blanco Rv nr Kyle, TX | 331, 332
San Marcos Rv at Luling, TX | 331,332,333,336

## Slide 12: The terrain flow information model for deriving channels, watersheds, and flow related terrain information.
Raw DEM
Pit Removal (Filling)
Flow Field
Channels, Watersheds, Flow Related Terrain Information
Watersheds are the most basic hydrologic landscape elements
Notes: This slide shows the general model for deriving flow field related derivative surfaces from digital elevation data. The input is a raw digital elevation model, generally elevation values on a grid. This is basic information used to derive further hydrology related spatial fields that enrich the information content of this basic data. The first step is to remove sinks, either by filling, or carving. Then a flow field is defined. This enables the calculation of flow related terrain information. My focus has been on flow related information working within this framework. I try to leave other GIS functionality, like radiation exposure, line of sight analyses and visualization to others. I have distributed my software in ways that it easily plugs in to mainstream systems, such as ArcGIS to enhance ease of use.

## Slide 13: DEM Elevations
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 14: The Pit Removal Problem
DEM creation results in artificial pits in the landscape
A pit is a set of one or more cells which has no downstream cells around it
Unless these pits are removed they become sinks and isolate portions of the watershed
Pit removal is first thing done with a DEM

## Slide 15: Pit Filling
Increase elevation to the pour point elevation until the pit drains to a neighbor

## Slide 16: Pit Filling
Pits
Pour Points
Original DEM
Pits Filled
Grid cells or zones completely surrounded by higher terrain
The lowest grid cell adjacent to a pit
Notes: Elevations are filled to that of the pools pour point

## Slide 18
80
74
63
69
67
56
60
52
48
80
74
63
69
67
56
60
52
48
30
Slope:
Hydrologic Slope
- Direction of Steepest Descent
30

## Slide 19
2
2
4
4
8
1
4
16
1
2
4
8
4
4
1
2
4
8
2
4
4
4
4
2
1
Eight Direction (D8) Flow Model
32
16
8
64
4
128
1
2

## Slide 20: Flow Direction Grid
32
16
8
64
4
128
1
2

## Slide 21
Grid Network

## Slide 22
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
14
4
1
19
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
Flow Accumulation Grid.
Area draining in to a grid cell
Link to Grid calculator
ArcHydro Page 72

## Slide 23
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
Flow Accumulation > 10 Cell Threshold
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
1
0
4
1
1
10
14
19
Stream Network for 10 cell Threshold Drainage Area

## Slide 24
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
2
5
15
20
2
The area draining each grid cell includes the grid cell itself.
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
5
2
2
25
15
TauDEM contributing area convention.

## Slide 25: Streams with 200 cell Threshold (>18 hectares or 13.5 acres drainage area)

## Slide 26
Watershed Draining to Outlet

## Slide 27: Watershed and Drainage Paths Delineated from 30m DEM
Automated method is more consistent than hand delineation

## Slide 28
ArcHydro Page 74
172
201
204
202
206
203
209
Each link has a unique identifying number
Stream Segments

## Slide 29
Vectorized Streams Linked Using Grid Code to Cell Equivalents
Vector
Streams
Grid
Streams
ArcHydro Page 75

## Slide 30
DrainageLines are drawn through the centers of cells on the stream links. DrainagePoints are located at the centers of the outlet cells of the catchments
ArcHydro Page 75

## Slide 31: Catchments
For every stream segment, there is a corresponding catchment
Catchments are a tessellation of the landscape through a set of physical rules

## Slide 32: Raster Zones and Vector Polygons
Catchment GridID
Vector Polygons
DEM GridCode
Raster Zones
3
4
5
One to one connection

## Slide 33
Catchments, DrainageLines and DrainagePoints of the San Marcos basin
ArcHydro Page 75

## Slide 34
Catchment, Watershed, Subwatershed.
ArcHydro Page 76
Watershed outlet points may lie within the interior of a catchment, e.g. at a USGS stream-gaging site.
Catchments
Subwatersheds
Watershed

## Slide 35
+
=
 Take a mapped stream network and a DEM
 Make a grid of the streams
 Raise the off-stream DEM cells by an arbitrary elevation
increment
 Produces "burned in" DEM streams = mapped streams
“Burning In” the Streams

## Slide 36
AGREE Elevation Grid Modification Methodology – DEM Reconditioning

## Slide 37: Carving
Lower elevation of neighbor along a predefined drainage path until the pit drains to the outlet point

## Slide 38: Carving
Pits
Carve outlets
Original DEM
Carved DEM
Notes: Elevations are filled to that of the pools pour point

## Slide 39
Filling
Carving
Minimizing Alterations

## Slide 40: Minimizing DEM Alterations
Optimally adjusted
Pits
Original DEM
Carved
Filled
Notes: Elevations are filled to that of the pools pour point

## Slide 41: Summary of Key Processing Steps
[DEM Reconditioning]
Pit Removal (Fill Sinks)
Flow Direction
Flow Accumulation
Stream Definition
Stream Segmentation
Catchment Grid Delineation
Raster to Vector Conversion (Catchment Polygon, Drainage Line, Catchment Outlet Points)

## Slide 42: Summary Concepts
The eight direction pour point model approximates the surface flow using eight discrete grid directions
The elevation surface represented by a grid digital elevation model is used to derive surfaces representing other hydrologic variables of interest such as
  Slope
  Flow direction
  Drainage area
  Catchments, watersheds and channel networks

## Slide 43: Are there any questions ?
AREA 1
AREA 2
3
12