## Slide 1: Bug in Flow Direction in Ex3 data
45.4 | 46.1 | 47 | 48.6 | 47.7
45 | 46.1 | 46.4 B | 47.9 | 47.4
45.1 | 45.8 | 46.8 A | 48.6 | 47.6
47.5 | 48 | 47.7 | 50.6 | 48.3
Grid cell size 10m
For D8 slope at B the percentage drop in direction 8 (indicated with arrow) should be
(46.4-45.8)/(SQRT(2)*10)=0.0424 = 4.24%
The fact that the ArcGIS function is reporting 3.33% is a bug
Important to know what is going on under the hood and check. As a software user you (not the manufacturer) are responsible for the results.

## Slide 2: Confirmation
Nawajish Noman <nnoman@esri.com>
Hi Dave,
Thank you very much finding this bug for us. Yes you are right, our result is different. Source of the problem is not the formula. We are doing it the same way you are doing... but we implemented it differently to increase the efficiency - which led to some approximation.
I apologize for the inconvenience.
We are taking necessary steps to fix this problem. I will keep you posted.
Thanks
Noman

## Slide 3: Term projects
Related to Land Use, Land Cover and Flooding (Ditmore, Gaffey, Kirkwood, Yaniero)
SWAT Hydrologic Modeling (Gold)
Natural Flows (Lutton)
Mortality of trees related to wetness (Jones)
Watershed restoration prioritization (Lovette)
Landslides (Martin)
Foodshed (Stanton)

## Slide 4: Enhanced Terrain Analysis Using TauDEM
Learning Objectives
Describe some of the enhanced terrain analysis functionality provided by TauDEM
Encourage the use of TauDEM in term projects where appropriate
Motivate the need for GIS based programming

## Slide 5: TauDEM
http://hydrology.usu.edu/taudem/
Stream and watershed delineation
Multiple flow direction flow field
Calculation of flow based derivative surfaces
MPI Parallel Implementation for speed up and large problems
Open source platform independent C++ command line executables for each function
Deployed as an ArcGIS Toolbox with python scripts that drive command line executables

## Slide 6: ArcMap

## Slide 7: Pit Remove

## Slide 8: Default file name suffixes
For complete list see: http://hydrology.usu.edu/taudem/taudem5/help/GridDefinitionsAndNamingConventions.htm

## Slide 9: TauDEM Grid Data Format Assumptions
Input and output grids are uncompressed GeoTIFF
Maximum size 4 GB (~32,000 x 32,000 rows and cols for single file version)
For larger areas use multifile version
GDAL Nodata tag preferred (if not present, a missing value is assumed)
Grids are square (x= y)
Grids have identical extents, cell size and spatial reference
Spatial reference information is not used (no projection on the fly)

## Slide 10: Illustrative Use Case: Delineation of channels and watersheds using a constant support area threshold
Steps
Pit Remove
D8 Flow Directions
D8 Contributing Area
Stream Definition by Threshold
Stream Reach and Watershed

## Slide 11: D8 Contributing Area

## Slide 12: Stream Definition by Threshold

## Slide 13: Stream Reach and Watershed

## Slide 14
80
74
63
69
67
56
60
52
48
30
4
5
6
3
7
2
1
8
D8 Flow Direction Model
- Direction of steepest descent
Slope = Drop/Distance
Steepest down slope direction

## Slide 15
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
2
5
15
20
2
The area draining each grid cell includes the grid cell itself.
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
5
2
2
20
15
Contributing Area (Flow Accumulation)

## Slide 16: Stream Definition
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
2
5
15
20
2
Flow Accumulation > 10 Cell Threshold
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
2
1
5
2
2
11
15
20
Stream Network for 10 cell Threshold Drainage Area

## Slide 17: Edge contamination
Edge contamination arises due to the possibility that a contributing area value may be underestimated due to grid cells outside of the domain not being counted. This occurs when drainage is inwards from the boundaries or areas with no data values. The algorithm recognizes this and reports "no data" resulting in streaks of "no data" values extending inwards from boundaries along flow paths that enter the domain at a boundary.

## Slide 18: Peuker Douglas Watershed Delineation using TauDEM tools

## Slide 19: Catchments linked to Stream Network

## Slide 20: D-Infinity Contributing Area
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.)
D
D8
Notes: This slide shows how the terrain flow field is represented. Early DEM work used a single flow direction model, D8. In 1997 I published the Dinfinity method that proportions flow from each grid cell among downslope neighbors. This, at the expense of some dispersion, allows a better approximation of flow across surfaces.

## Slide 21: Wetness Index
Slope (S)
Specific Catchment Area (a)
Wetness Index ln(a/S)

## Slide 22: Why Programming
Automation of repetitive tasks (workflows)
Implementation of functionality not available (programming new behavior)

## Slide 23: Three Views of GIS
Geodatabase view: Structured data sets that represent geographic information in terms of a generic GIS data model.
Geovisualization view: A GIS is a set of intelligent maps and other views that shows features and feature relationships on the earth's surface. "Windows into the database" to support queries, analysis, and editing of the information.
Geoprocessing view: Information transformation tools that derive new geographic data sets from existing data sets.
adapted from www.esri.com

## Slide 24: ArcGIS programming entry points
Model builder
Python scripting environment
ArcObjects library (for system language like C++, .Net)
Open standard data formats that anyone can use in programs (e.g. shapefiles, geoTIFF, netCDF)

## Slide 25
http://resources.arcgis.com/en/help/main/10.2/#/What_is_ModelBuilder/002w00000001000000/

## Slide 26: Generalization to Flow Algebra
Pki
Pki
Pki
i
Replace
by general function

## Slide 27: Example: Retention limited runoff generation with run-on
Global P, (r,c), q FlowAlgebra(i) for all k neighbors of i if Pki>0 FlowAlgebra(k) next k return
r
c
qi
qk

## Slide 28: Retention limited runoff with run-on
0.6
0.4
1
A
B
C
D
r=7
c=4
q=3
r=5
c=6
qin=1.8
q=0.8
r=4
c=6
q=0
1
r=4
c=5
qin=2
q=1
Retention Capacity
Runoff from uniform input of 0.25
Notes: Figure 2 illustrates the evaluation of infiltration capacity limited runoff generation with run on according to (5). Inputs are the r and c values indicated, with the proportional flow directions indicated by the arrows. Grid cells A and B on the left have no dependencies so may be immediately evaluated and using min(r-c,0) result in q=3 and 0 for grid cells A and B respectively. With these evaluated, the unevaluated dependencies of grid cell C become 0, so equation (5) can be evaluated for grid cell C. The inflow is qin=0.6 x 3 = 1.8 from grid cell B. Then q=min(5-6+1.8,0)=0.8. Now all dependencies of D have been evaluated. Inflows from cells A, B, and C, accounting for the proportions are 3 x 0.4 + 0.8 = 2, so the runoff from D is q=min(4-5+2,0)=2.

## Slide 29: General Pseudocode Downstream Flow Algebra Evaluation
Pki
Global P, ,  FlowAlgebra(i) for all k neighbors of i if Pik>0 FlowAlgebra(k) next k i = FA(i, Pik, k, k) return

## Slide 30
Dependence function of grid cells y
0
1
0
0
1
0
0
0.6
0
0.3
0.3
0
0.6
0
0
Grid cells y
Useful for example to track where a contaminant may come from

## Slide 31: Weighted distance to target set
38.2
7.5+42.4*
(0.7+0.5)/2
32.9
7.5
30*0.5/2
0
0
0
0
0
38.2
38.2
38.2
38.2
30
To quantify effectiveness of riparian zone sediment capture based on buffer potential

## Slide 32: Buffer potential weighted distance to stream

## Slide 33: Distance Down and Distance Up
Types of distance measurements possible in distance down and distance up functions.
hs
hr
vr
vs
Point of interest
Stream
Ridge
pr
ps
ss
sr
hs
hr
vr
vs
Point of interest
Stream
Ridge
pr
ps
ss
sr

## Slide 34: Terrain Stability Mapping
With Bob Pack. http://www.engineering.usu.edu/dtarb/sinmap.htm

## Slide 35: SINMAP Theoretical Basis
q = slope
Infinite Plane Slope Stability Model
FS=Factor of Safety
where
R
D
Dw
D
h
Density Ratio
Relative Wetness
Dimensionless Cohesion
= DEM source

## Slide 36: DEM Governs Slope & Flow Accumulation
Flow Accumulation (a)
Slope (θ)
DTM Quality
Digital Terrain Model (DTM)

## Slide 37: Probabilistic Formulation
MODEL
P(FS>1)
Flow Accumulation
Slope
Shear Strength
Wetness
Soil/Root Cohesion
SI=FS &

## Slide 38: Stability Class Definitions
1.0

## Slide 39: Interactive Calibration
Selection of ranges of Φ, R/T & c moves position of stability class breaks
Selection of range of R/T moves position of wetness class breaks

## Slide 40
SLOPE
DRAINAGE AREA UPSLOPE
SATURATED
STABLE
UNSTABLE
UNSATURATED
Example Result – Foster Ck
Class 1
2
3
4
5
6

## Slide 41
Foster Creek SI Map

## Slide 42
LANDSLIDE DENSITIES & AREAS FOR SI CLASSES

## Slide 43: Parallelization of Flow Algebra
Executed by every process with grid flow field P, grid dependencies D initialized to 0 and an empty queue Q. FindDependencies(P,Q,D) for all i for all k neighbors of i if Pki>0 D(i)=D(i)+1 if D(i)=0 add i to Q next
Executed by every process with D and Q initialized from FindDependencies. FlowAlgebra(P,Q,D,,) while Q isn’t empty get i from Q i = FA(i, Pki, k, k) for each downslope neighbor n of i if Pin>0 D(n)=D(n)-1 if D(n)=0 add n to Q next n end while swap process buffers and repeat
1. Dependency grid
2. Flow algebra function

## Slide 44: Programming
C++ Command Line Executables that use MPI
ArcGIS Python Script Tools
Python validation code to provide file name defaults
Shared as ArcGIS Toolbox

## Slide 45: Q based block of code to evaluate any “flow algebra expression”
while(!que.empty())
{
//Takes next node with no contributing neighbors
temp = que.front(); que.pop();
i = temp.x; j = temp.y;
// FLOW ALGEBRA EXPRESSION EVALUATION
if(flowData->isInPartition(i,j)){
float areares=0.; // initialize the result
for(k=1; k<=8; k++) { // For each neighbor
in = i+d1[k]; jn = j+d2[k]; flowData->getData(in,jn, angle);
p = prop(angle, (k+4)%8);
if(p>0.){
if(areadinf->isNodata(in,jn))con=true;
else{
areares=areares+p*areadinf->getData(in,jn,tempFloat);
}
}
}
}
// Local inputs
areares=areares+dx;
if(con && contcheck==1)
areadinf->setToNodata(i,j);
else
areadinf->setData(i,j,areares);
// END FLOW ALGEBRA EXPRESSION EVALUATION
}
C++

## Slide 46: Maintaining to do Q and partition sharing
while(!finished) { //Loop within partition
while(!que.empty())
{ .... // FLOW ALGEBRA EXPRESSION EVALUATION
}
// Decrement neighbor dependence of downslope cell
flowData->getData(i, j, angle);
for(k=1; k<=8; k++) {
p = prop(angle, k);
if(p>0.0) {
in = i+d1[k]; jn = j+d2[k];
//Decrement the number of contributing neighbors in neighbor
neighbor->addToData(in,jn,(short)-1);
//Check if neighbor needs to be added to que
if(flowData->isInPartition(in,jn) && neighbor->getData(in, jn, tempShort) == 0 ){
temp.x=in; temp.y=jn;
que.push(temp);
}
}
}
}
//Pass information across partitions
areadinf->share();
neighbor->addBorders();
C++

## Slide 47: Python Script to Call Command Line
mpiexec –n 8 pitremove –z Logan.tif –fel Loganfel.tif

## Slide 48: PitRemove
Python

## Slide 49: Validation code to add default file names
Python

## Slide 50: Terrain Analysis Using Digital Elevation Models (TauDEM)
Readings
Tarboton, D. G., R. L. Bras and I. Rodriguez-Iturbe, (1991), "On the Extraction of Channel Networks from Digital Elevation Data," Hydrologic Processes, 5(1): 81-100. http://www.neng.usu.edu/cee/faculty/dtarb/hp91.pdf
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319. http://www.neng.usu.edu/cee/faculty/dtarb/96wr03137.pdf
Tarboton, D. G., K. A. T. Schreuders, D. W. Watson and M. E. Baker, (2009), "Generalized terrain-based flow analysis of digital elevation models," 18th World IMACS Congress and MODSIM09 International Congress on Modelling and Simulation, ed. R. S. Anderssen, R. D. Braddock and L. T. H. Newham, Modelling and Simulation Society of Australia and New Zealand and International Association for Mathematics and Computers in Simulation, July 2009, p.2000-2006, http://www.mssanz.org.au/modsim09/F4/tarboton_F4.pdf.