## Slide 1: An Overview of Integrated Modeling for Water Resources
Tony Castronova
Utah State University
11/6/2014

## Slide 2: Learning Objectives
Understand that many different modeling activities are going on within the water resources domain
Conceptual understanding of coupled modeling approaches, applications, and benefits
Understand the difference between loose and tight model integration.
Identify the ontological differences in how observed and modeled data are represented
Introduction into the model sharing efforts of HydroShare.

## Slide 3: What is Modeling

## Slide 4: Hydrologists View
nasa.gov
Water Cycle
  Focus of hydrology
  Flow of water through the environment
Complicated
  Many physical processes
  Complex interactions
Interdisciplinary
  Atmospheric, Hydrologic, Geologic, Environmental, etc…

## Slide 5: Lets Look at Some Common Models
hec.usace.army.mil
pubs.usgs.gov
hec.usace.army.mil

## Slide 6: Model Coupling

## Slide 7: Tight vs Loose Integration

## Slide 8: How do these Systems Compare?
Tight Integration
Advantages
Disadvantages
Loose Integration
Advantages
Disadvantages
Complete control over system
Can be optimized for performance
Requires a great deal of expertise
Source code must be available
Requires customized integration for every model system
Learning curve
Rewriting legacy code that has been tightly integrated
Performance?
Improves ease of collaboration
Modular development
Model substitution
Code reuse
Notes: Tight Integration
Advantages
Enables complete control over integrated modeling system
Can be optimized for performance
Disadvantages
Requires a great deal of expertise
Source code must be available
Requires customized integration for every model system
Loose Integration
Advantages
Improves the ease of collaboration, e.g. cross -disciplinary model studies
  large problems that can not be explored by stand alone models.
  predict the wider implications of policies and projects
Modular development
  Simplifies model substitution
  Helpful when changing spatial scales, and performing uncertainty or sensitivity analyses.
Simplify the construction of Decision Support Systems (DSS)
  Develop models in isolation that can be guaranteed to connect to other models
  reducing the time involved by standardizing data transfer
Models can be reused in future projects.
Disadvantages
Learning Curve
Need to redevelop legacy code that has been tightly integrated
Performance?

## Slide 9: A Closer look at Loose Integration
Standard modeling interface defines the methods required by routines
Input and Output data is passed between routines.
Routines are discovered at runtime
Model compositions require more communication
Encourages model reuse

## Slide 10: Existing Software Architectures

## Slide 11: Data Communitcation
(Moore and Tindall, 2005)
Rainfall
Runoff
River
Ground
Water

## Slide 12: Linking Data With Coupled Models
How can we feed forcing data into coupled models?
Establish a method for mapping data between the OpenMI and HIS
  Map observation and model metadata
Create a integrated modeling application that uses this mapping
  An OpenMI component to read data from the HIS
  An OpenMI component to write data to the HIS
Demonstrate how these components can be used in a model simulation
  Calculate evapotranspiration

## Slide 13: How can we feed data into coupled models?
Consortium of Universities for the Advancement of Hydrologic Science, Inc. Hydrologic Information System
Collaborative effort
  University of Texas, Austin
  Utah State University
  San Diego Super Computing Center
  Idaho State University
  City College of New York
  University of South Carolina
NSF Funded ($4.7 Million 2007-2011)
Goals
  Make the nation's water information universally accessible and useful
  Provide access to data sources, tools and models
  Enable the synthesis, visualization and evaluation of the behavior of hydrologic systems.

## Slide 14: CUAHSI HydroDesktop
Web service network of hydrologic resources
Enables users to publish data
Searching across distributed HIS data
hydrodesktop.codeplex.com
Open-source GIS
Entry point to the HIS observation data
Extendable through plugin development

## Slide 15: Observations Data Model (ODM)
Soil
moisture
data
Streamflow
Flux tower data
Groundwater
levels
Water Quality
Precipitation
& Climate
Horsburgh, J. S., D. G. Tarboton, D. R. Maidment, and I. Zaslavsky (2008), A relational model for environmental and water resources data, Water Resources Research, 44, W05406, doi:10.1029/2007WR006392.
Provides a common persistence model for data storage
Notes: A relational database at the single observation level
Metadata for unambiguous interpretation
Traceable heritage from raw measurements to usable information
Promote syntactic and semantic consistency
Cross dimension retrieval and analysis

## Slide 16: Mapping Model Data to HIS
HIS provides a standard for describing and accessing data repositories
OpenMI provides a standard for describing and executing models

## Slide 17: HydroModeler
Component modeling plugin for the HydroDesktop
Extends the original OpenMI configuration editor (OmiED)
Provides an extensible modeling environment

## Slide 18: Example 1: Nitrogen Loading
Streamflow and nitrogen collected using HydroDesktop
Simplified nitrogen loading calculation averaged over time
Notes: Loading = Flow_rate * Nitrogen Measurement * 86400

## Slide 19: Building the Model

## Slide 20: Linking Model Components

## Slide 21: Data Visualization

## Slide 22: Example 2: Modeling ET

## Slide 23
Data Visualization

## Slide 24: Example 3: Service Oriented TOPMODEL
Castronova, Anthony M., Jonathan L. Goodall, and Mostafa M. Elag. "Models as web services using the Open Geospatial Consortium (OGC) Web Processing Service (WPS) standard." Environmental Modelling & Software 41 (2013): 72-83.
Coweeta Watershed
Located in western NC
Long Term Ecological Research
Watershed 18, 0.12 km2
Readily available observations

## Slide 25: Service Oriented Model Design
DbReader
  Supplies CUAHSI HIS observation data
Hargreaves
  Calculates PET using temperature data.
Wps:Topmodel
  Wraps the web TOPMODEL web resource into an OpenMI-compliant form
GET

## Slide 26: Example 4: Flood Modeling in Columbia, SC
Downtown Columbia floods often
  Property damage
  Infrastructure damage
Short, high intensity storms
  2.26 in 1 hour
  River depth from 10in to 10.74ft in 1 hour

## Slide 27: Urban Infrastructure Model Design
Web services are developed independently
RESTful
Use the OGC WPS to encapsulate data
Interaction between models is provided by a client-side script

## Slide 28: Structures Component
Estimates probability of bridge failure
  Structure reliability
  Strength decreases due to age
Finite element model
Designed to investigate
  Failure of bridges due to scour of their foundation

## Slide 29: Transportation Component
Predicts the travel time of vehicles during rush hour in downtown Columbia, SC
Modifies input files, executes DTALite, and returns parsed output data.
Dynamic Traffic Assignment model (agent-based)
  network algorithms
  trip-maker behavior models
Captures the effects of
  road closures
  dynamic message signs
  Advanced traveler information systems

## Slide 30: Water Resources Component
Estimate streamflow based on river stage observations
Streamflow is approximated using Manning’s equation
River stage and streamflow measurements are returned by the model.

## Slide 31: GIS River Overtopping
Geoprocessing routines are used to identify roads that may flood.
Common GIS tools and DEMs are used to determine if a roadway should be closed
Ignores the complicated hydraulic and hydrologic conditions that occur during floods
Provides a likelihood that the river will inundate roadways

## Slide 32: Application: Study Area
Rocky Branch watershed
  11 km2
  Consists of commercial districts, university property, and residential neighborhoods
High intensity storms often cause flooding
  Roads at low lying areas must be closed
  City of Columbia has been attempting to alleviate this problem

## Slide 33: Results

## Slide 34
Analysis Tools
Visualization Tools
Data Loaders
Data Discovery Tools
Models
Interaction with common data store
Can take advantage of visualization loading and discovery tools
HydroShare
User accounts and data storage
Water related data are represneted as resources
social functionality (i.e. discovering resources and people)
Data publishing and documentation

## Slide 35: Design Considerations
Make publishing, sharing, and discovering hydrologic data and models easy.
Support many different types of data
Web service API to interact with HydroShare remotely
waterdata.usgs.gov
epa.gov
Notes: These are some of the resources that are currently under develeopment.
Web service Api is designed to provide interaction with HydroShare from 3rd party applications. Enable easy resource creation and publication

## Slide 36: Representing Models In HydroShare
Model package
  Bundled components
  references existing resources
Model program
  executable entity
  may consist of submodules and other complex relationships
Model input
  input required by a program
  files, parameters, etc...
Model output
  outputs produced by a program
  files, plots, etc...

## Slide 37: Describing Resources using Metadata
Collect metadata during resource creation
  many possible fields
  optional metadata added later
Use DublinCore standard
  set of vocabulary terms
  describes physical and web resources
  our implementation is called the HydroShare Science Metadata
Expand DublinCore
  many different types of resources
  may require specialized terms
Resource Type
Generic Resource
Logan River Streamflow at USGS 10109000
Title
Creators
Contributors
Abstract
Subject Keywords
Url
Rights
Tony Castronova
Streamflow measurements for the Logan river UT recorded by the USGS that have been processed by ...
streamflow
USGS
gap filled
http://waterdata.usgs.gov/ut/nwis/uv/?site_no=10109000&
Create Resource
Notes: Who else uses dublin core? Why should we use it?

## Slide 38: What else do we need?
What Model Specific Metadata is missing?
Software Version
Software Language
Operating System
Release Date
Release Notes
Web Page
Repository
User Manual
Theoretical Manual
Source Code
Executable Code

## Slide 39: Expanding a model program
Uses HS science metadata
  creator, contributor, date, org...
Model program specific terms
  expands Morsy et al. (2014)
  software and requirements
Expand HS science metadata definition when necessary
  does not describe every possible hydro-related entity
Morsy, M. M., Goodall, J.L., Bandaragoda, C., Castronova, A.M., Greenberg, J. (2014). Metadata for Describing Water Models. International Environmental Modelling and Software Society (iEMSs) 7th International Congress on Environmental Modelling and Software San Diego, California, USA, D.P. Ames, N. Quinn (Eds.). (Accepted)

## Slide 40: Example Implementation

## Slide 41: Creating Model Resources in HydroShare
Manual metadata entry may become cumbersome
  creators/contributors aren't users so additional information is needed
  address, phone, name, affiliation, etc...
Specialized resources need more data!
  metadata list will continue to grow
  not all of this info is known during resource creation
Populating metadata the smart way
  file recognition
  resource file parsing
  Metadata description file
continuous
Resource Type
Model Program
Storm Water Management Model
Title
Creators
Contributors
Abstract
Subject Keywords
Url
Rights
The EPA Storm Water Management Model (SWMM) is a dynamic rainfall-runoff simulation model used for single event or long-term (continuous) simulation of runoff quantity and quality from primarily urban areas.
quantity
quality
http://www.epa.gov/athens/wwqtsc/html/swmm.html
Choose File
SWMM_Model.zip
Lewis Rossman
Carl Chan
Robert Dickinson
Trent Schade
http://creativecommons.org/licenses/by/4.0/
Version
5.1.004
Release Date
04-14-2014
Source Code
http://www2.epa.gov/sites/production/files/2014-10/swmm51007_engine_0.zip/
Software
General

## Slide 42: Model Execution in HydroShare
Instance
Input and output Hydroshare resources
Link input, output, and program resources to create model packages
Execution of model package within the HydroShare environment to create "new" resources
Program
Input
Program
Input
Instance
Output
EXECUTE
Output
CREATE OUTPUT
CREATE PACKAGE

## Slide 43: Summary
While many models already exist that can be used to simulate water resources systems, none can represent the water cycle holistically
Tight and Loose integration techniques can be used to expand the scope of a software model to represent cross-domain studies.
The HydroModeler is a coupled modeling environment built as a HydroDesktop plugin. This allows data to be supplied from HIS into models and from models into a local ODM-like database.
Web services can be used along with loosely integrated modeling techniques to remotely execute model routines.
HydroShare can be used to discover, archive, and share Water Resources models, as well as simulation instance inputs and outputs.

## Slide 44: A Relational Data Model for Simulations