## Slide 1: Welcome to GIS in Water Resources 2015
David Maidment, David Tarboton,

## Slide 2: Our Classroom
Dr David Tarboton
Students at Utah State University
Dr David Maidment Students at University of Texas at Austin

## Slide 3
B.E. in Agricultural Engineering (with First Class Honors) from University of Canterbury, Christchurch, New Zealand, 1972
MS, PhD in Civil Engineering from University of Illinois, 1974 and 1976, respectively
1981 – joined University of Texas at Austin as an Assistant Professor, and have been on the faculty ever since. Now Hussein M. Alharthy Centennial Chair in Civil Engineering
Initiated the GIS in Water Resources course in 1991.
Worked with ESRI since 1994 on a GIS Hydro Preconference seminar for the ESRI Users Conference
Leader of the CUAHSI Hydrologic Information System project from 2004-2011
Developing World Water Online with ESRI and Kisters
Leader of the National Flood Interoperability Experiment
David R. Maidment

## Slide 4: David Tarboton
B.Sc Eng in Civil Engineering from the University of Natal, Durban, South Africa 1981
M.S. and Sc.D from MIT, Cambridge, Massachusetts, 1987 and 1990 respectively
1990 - Joined Faculty at Utah State University in Civil and Environmental Engineering
1996 - Developed D-Infinity and gradually adapted research terrain analysis codes (Fortran and C) into TauDEM
Participated in GISWR since 1999 (this year is the 17th time)
Research includes snow energy balance, stochastic streamflow and physically based hydrologic modeling
Leader of HydroShare project to extend the capability of CUAHSI HIS to collaborative data sharing, additional data types and models

## Slide 5: Six Basic Course Elements
Lectures
  Powerpoint slides
  Video streaming
Readings
  Assigned web materials
Homework
  Computer exercises
  Hand exercises
Term Project
  Oral presentation
  pdf report
Class Interaction
  Email
  Discussion
Examinations
  Midterm, final

## Slide 6: Learning Objectives
Prepare maps using GIS
Use web mapping
Interpolate measured data to form raster surfaces
Perform hydrologic calculations using GIS layers
Build a geometric network for streams and rivers
Analyze a digital elevation model to derive watersheds and stream networks
Prepare a HEC-HMS hydrologic simulation model

## Slide 7: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map
Reading Assignment: Introduction to Map Projections http://desktop.arcgis.com/en/desktop/latest/guide-books/map-projections/what-are-map-projections.htm

## Slide 8: University Without Walls
Traditional Classroom
Community
Inside and Outside
The Classroom

## Slide 9: Learning Styles
Instructor-Centered Presentation
Community-Centered Presentation
Student
Instructor
We learn from the instructors and each other

## Slide 10: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map

## Slide 11: What is GIS
A geographic information system (GIS) is a system designed to capture, store, manipulate, analyze, manage, and present all types of geographical data. -- Wikipedia
maps
data
tools
computers

## Slide 12: Geography is visualized in maps
www.arcgis.com
map

## Slide 13: Maps are built from data
map
data
Road
Name: E. Dean Keeton St
Type: Div Highway
Speed: 35 mph
Shape: [Geometry]
Building
Name: Ernest Cockrell Jr Hall
Address: 301 E. Dean Keeton St
Shape: [Geometry]
Shape includes the geometry of the feature and where it is located on earth

## Slide 14: Vector data represent discrete features
map
data
polygons
lines
points

## Slide 15: Raster data form a grid of cells or pixels
map
data

## Slide 16: More Raster Examples
map
data
rainfall
elevation
land use

## Slide 17: There are many more data types
map
data
triangulated
irregular network
multipatch
annotation
Martin Luther King Dr W

## Slide 18: Connected Map, Chart and Animation
Tropical Storm Fernand
http://www.msnbc.msn.com/id/26295161/ns/weather/

## Slide 19: Geographic Data Model
Conceptual Model – a set of concepts that describe a subject and allow reasoning about it
Mathematical Model – a conceptual model expressed in symbols and equations
Data Model – a conceptual model expressed in a data structure (e.g. ascii files, Excel tables, …..)
Geographic Data Model – a conceptual model for describing and reasoning about the world expressed in a GIS database

## Slide 20: So what is a data model anyway?

## Slide 21: The way that data is organized can enhance or inhibit the analysis that can be done
I have your information right here …
Picture from: http://initsspace.com/

## Slide 22: Geographic Data Model
“All geographic information systems are built using formal models that describe how things are located in space. A formal model is an abstract and well-defined system of concepts. A geographic data model defines the vocabulary for describing and reasoning about the things that are located on the earth. Geographic data models serve as the foundation on which all geographic information systems are built.”
Scott Morehouse, Preface to “Modeling our World”, First Edition. He is the chief software engineer at ESRI

## Slide 23
Data Model based on a collection of data themes

## Slide 24: Spatial Data: Vector format
Point - a pair of x and y coordinates
(x1,y1)
Line - a sequence of points
Polygon - a closed set of lines
Node
vertex
Vector data are defined spatially:
Notes: DRM

## Slide 25: Kissimmee watershed, Florida
Themes

## Slide 26: Attributes of a Selected Feature

## Slide 27: Raster and Vector Data
Point
Line
Polygon
Vector
Raster
Raster data are described by a cell grid, one value per cell
Zone of cells
Notes: DRM

## Slide 28
http://srtm.usgs.gov/srtmimagegallery/index.html
Santa Barbara, California

## Slide 29: The challenge of increasing Digital Elevation Model (DEM) resolution
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10-30 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2

## Slide 30: How do we combine these data?
Digital Elevation
Models
Watersheds
Streams
Waterbodies

## Slide 31: An integrated raster-vector database

## Slide 32: Three Views of GIS
Geodatabase view: Structured data sets that represent geographic information in terms of a generic GIS data model.
Geovisualization view: A GIS is a set of intelligent maps and other views that shows features and feature relationships on the earth's surface. "Windows into the database" to support queries, analysis, and editing of the information.
Geoprocessing view: Information transformation tools that derive new geographic data sets from existing data sets.
adapted from www.esri.com

## Slide 33: Programming
Automation of repetitive tasks (workflows)
Implementation of functionality not available (programming new behavior)

## Slide 34: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map

## Slide 35: Linking Geographic Information Systems and Water Resources
GIS
Water
Resources

## Slide 36: Major Transitions in Geospatial Info
Paper maps to digital data
  National Spatial Data Infrastructure development
  Started in 1990’s
  Took more than a decade to complete
Digital data to web services
  Started several years ago
  Will take years to complete
Maps
Data
Services

## Slide 37: National Spatial Data Infrastructure (NSDI)
Desired Future State of NSDI
Create network of resources and services
Facilitate discovery, access and application of resources
Leverage shared standard-based services
Develop core set of information layers that interface with nonspatial data
Use real-time data feeds and sensor webs

## Slide 38: Open Water Data Initiative
Subcommittee on Spatial Water Data will lead this effort
This reports to both FGDC and ACWI
Chair
Anne Castle, Asst Secretary for Water and Science, Dept of Interior

## Slide 39
Temporal information
Geospatial information
National Water Center – Tuscaloosa Alabama

## Slide 40: NHDPlus Geospatial base for National Water Data Infrastructure
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
3 million catchments average area 3 km2,
reach length 2 km
(built 2004-2014)

## Slide 41: A Key Challenge
GIS
Water Environment
(Watersheds, streams, gages, sampling points)
How to connect water environment with water observations
Time Series Data
Water Observations
(Flow, water level concentration)

## Slide 42: We collect lots of water data
From dispersed federal agencies
From investigators collected for different purposes
Different formats
  Points
  Lines
  Polygons
  Fields
  Time Series
Rainfall and Meteorology
Water quantity
Soil water
Groundwater
Water quality
GIS
The way that data is stored can enhance or inhibit the analysis that can be done
We need ways to organize the data we work with

## Slide 43
CUAHSI is a consortium representing 125 US universities
Supported by the National Science Foundation Earth Science Division
Advances hydrologic science in nation’s universities
Includes a Hydrologic Information Systems
http://www.cuahsi.org

## Slide 44: How the web works
Catalog (Google)
Web Server
(CNN.com)
Browser
(Firefox)
Access
Catalog harvest
Search
HTML – web language for text and pictures

## Slide 45: CUAHSI Hydrologic Information System: A Services-Oriented Architecture Based System for Sharing Hydrologic Data
Data Discovery and Integration
Data Publication
Data Analysis and Synthesis
HydroCatalog
HydroDesktop
HydroServer
Data Services
Metadata Services
Search Services
WaterML, Other OGC Standards

## Slide 46: CUAHSI HIS
HydroServer – Data Publication
Lake Powell Inflow and Storage
HydroDesktop – Data Access and Analysis
HydroDesktop – Combining multiple data sources
HydroCatalog
Data Discovery
The CUAHSI Hydrologic Information System (HIS) is an internet based system to support the sharing of hydrologic data. It is comprised of hydrologic databases and servers connected through web services as well as software for data publication, discovery and access.

## Slide 47: GIS on the web
ArcGIS online map services
http://www.arcgis.com

## Slide 48: HydroShare is a web based collaborative system to support analysis, modeling and data publication
www.hydroshare.org
Notes: HydroShare will be a collaborative environment for sharing hydrologic data and models aimed at giving hydrologists the technology infrastructure they need to address critical issues related to water quantity, quality, accessibility, and management.
HydroShare will expand the data sharing capability of the CUAHSI Hydrologic Information System by broadening the classes of data accommodated, expanding capability to include the sharing of models and model components, and taking advantage of emerging social media functionality to enhance information about and collaboration around hydrologic data and models.
Functionality will include
A web portal for model and data sharing
Sharing features added to HydroDesktop client software
Access to more types of hydrologic data using standards compliant data formats and interfaces
Enhanced catalog functionality that broadens discovery functionality to different data types and models
New model sharing and discovery functionality
Enhanced easy to use access to high performance computing
Social media and collaboration functionality
Linkages to other data and modeling systems such as USGS and CUAHSI data services, NASA earth exchange and HPC resources e.g. at CSDMS

## Slide 49
Clearing your desk. The trend towards network (cloud) computing.
Data Sources
Functions and Tools
Server
Software as a Service
Users
Based on slide from Norm Jones
Delivering Geographic and Hydrologic Analysis functionality as services over the web?

## Slide 50: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map

## Slide 51: Origin of Geographic Coordinates
(0,0)
Equator
Prime Meridian

## Slide 52: Latitude and Longitude
Longitude line (Meridian)
N
S
W
E
Range: 180ºW - 0º - 180ºE
Latitude line (Parallel)
N
S
W
E
Range: 90ºS - 0º - 90ºN
(0ºN, 0ºE)
Equator, Prime Meridian

## Slide 53: Latitude and Longitude in North America
90 W
120 W
60 W
30 N
0 N
60 N
Austin:
Logan:
(30°18' 22" N, 97°45' 3" W)
(41°44' 24" N, 111°50' 9" W)

## Slide 54: Map Projection
Curved Earth
Geographic coordinates: f, l
(Latitude & Longitude)
Flat Map
Cartesian coordinates: x,y
(Easting & Northing)
Notes: DRM

## Slide 55: Earth to Globe to Map
Representative Fraction
Globe distance Earth distance
=
Map Scale:
Map Projection:
Scale Factor
Map distance Globe distance
=
(e.g. 1:24,000)
(e.g. 0.9996)

## Slide 56: Coordinate Systems
(fo,lo)
(xo,yo)
X
Y
Origin
A planar coordinate system is defined by a pair
of orthogonal (x,y) axes drawn through an origin
Geographic Coordinates
Projected Coordinates

## Slide 57: ArcGIS Help for Map Projections
http://desktop.arcgis.com/en/desktop/latest/guide-books/map-projections/what-are-map-projections.htm

## Slide 58: Summary (1)
GIS in Water Resources is about empowerment through use of information technology – helping you to understand the world around you and to investigate problems of interest to you
This is an “open class” in every sense where we learn from one another as well as from the instructors

## Slide 59: Summary (2)
GIS offers a structured information model for working with geospatial data that describe the “water environment” (watersheds, streams, lakes, land use, ….)
Water resources also needs observations and modeling to describe “the water” (discharge, water quality, water level, precipitation)

## Slide 60: Summary (3)
Geography “brings things together” through georeferencing on the earth’s surface
Understanding geolocation on the earth and working with geospatial coordinate systems is fundamental to this field
GIS has traditionally been used on the desktop but increasingly there is a transition to information sharing on the web