## Slide 1: Indices of Road Erosion Bear Valley Watershed, Idaho
CEE 6440: GIS in Water Resources
Nov. 30, 2010
Jeanny Wang Miles

## Slide 2: Measuring Road Erosion Risk
Fine Sediment from Unsealed Roads harm downstream ecosystems (suffocate redds)
Roads Need Adequate Drainage & Maintenance
Inadequate Culverts Impede Fish Passage
Difficult to Assess Actual Impact from Roads
Good Models Need Good Field Data
Image Analysis to Help Prioritize Erosion Risk on Watershed Scale?

## Slide 3: Primary Questions
  How and where does the road system modify surface and subsurface hydrology?
  How and where does the road system cause surface erosion?
  How and where is the road system hydrologically connected to stream system?
  How and where does the road system cause mass wasting?

## Slide 4: Indicators of Road Hazard
Road Density (< 1, 1-2.5, > 2.5 mi/mi2)
Stream Channel Proximity (300 ft from stream)
Predicted Stream Crossings
Slope Class (within 10 percent gradients)
Mass wasting: Bedrock geology or geomorphology as indicators of road erosion hazard (unstable surfaces)
Not used in this analysis
Slope Position as an indicator of road hazard (upper 20%, middle 40%, lower 40%)
Maintenance: Best management practices as indicators of road hazard

## Slide 5: Bear Valley Watershed, Idaho
- Listed as 303(d) impaired for sediment under Clean Water Act
- 191 square miles in watershed
>148 miles of roads

## Slide 6: Subwatersheds
Includes two 5th HUC watersheds:
Bear Valley Creek and Elk Creek
Includes seven 6th HUC subwatersheds

## Slide 7: Road Density
1.86 mi/mi2
0.86
mi/mi2
1.5 mi/mi2
Good : < 1 mi/mi2
Fair: 1 - 2.5 mi/mi2
Poor: > 2.5 mi2
0.27 mi/mi2
HUC_12 | HU_6_NAME | Road (mi) | SqMi | Density
170602050101 | Upper Bear Valley | 49.00 | 26.28 | 1.86
170602050202 | Bearskin | 26.33 | 17.58 | 1.50
170602050203 | Lower Elk | 18.27 | 20.79 | 0.88
170602050102 | Cache | 34.37 | 39.97 | 0.86
170602050103 | Wyoming | 11.95 | 25.74 | 0.46
170602050104 | Fir Creek | 5.51 | 20.18 | 0.27
170602050201 | Upper Elk | 2.85 | 40.81 | 0.07
TOTAL | Bear Valley Watershed | 148.27 | 191.34 | 0.77
0.88
mi/mi2
0.46 mi/mi2

## Slide 8: Stream Channel Proximity
Roads within
300 feet stream buffer
Subwatershed | m | mi in Buffer | total mi | % rds
Fir Creek | 6930.6 | 4.3 | 5.1 | 79%
Bearskin | 23080.3 | 14.3 | 14.9 | 56%
Wyoming | 9385.1 | 5.8 | 6.3 | 51%
Cache | 23313.6 | 14.5 | 14.9 | 43%
Upper Bear Valley | 27127.9 | 16.9 | 17.2 | 35%
Lower Elk | 8597.2 | 5.3 | 5.6 | 30%
Upper Elk | 956.7 | 0.6 | 0.9 | 28%
Good : <10% roads within buffer
Fair: 10-20% roads within buffer
Poor: >20% roads within buffer

## Slide 9: Stream Crossings
StreamCross - intersect of roads & DEQ streams layers
180 StreamNetCross – intersect of roads & TauDEM flownet
176 STRM_CRO observations
191 inventoried from GRAIP
Good : < 0.2 X-ings/stream mi
Fair: 0.2 – 0.4 X-ings/str mi
Poor: > 0.4 X-ings/stream mi
HU_6_NAME | Stream Density | Stream Crossings | Stream Miles | # Cross/ Str Mi
Upper Bear Valley | 1.2 | 19.0 | 31.5 | 0.60
Bearskin | 1.4 | 14.0 | 25.5 | 0.55
Cache | 1.2 | 13.0 | 49.1 | 0.26
Wyoming | 1.5 | 7.0 | 38.6 | 0.18
Fir Creek | 1.2 | 4.0 | 23.4 | 0.17
Lower Elk | 1.6 | 3.0 | 33.0 | 0.09
Upper Elk | 1.3 | 1.0 | 51.7 | 0.02
TOTAL (average) | 1.3 | 61 | 252.8 | 0.24

## Slide 10: Slope Class
Chart: Bear Valley Drain Slope Frequency
| 0.1 | 0.2 | 0.30000000000000032 | 0.4 | 0.5
Frequency | 249 | 94 | 64 | 44 | 14
Cumulative % | 0.53548 | 0.73763 | 0.87527 | 0.96989 | 1
Chart: Percent connected
| 0.1 | 0.2 | 0.30000000000000032 | 0.4 | 0.5
Percent connected | 0.042308 | 0.078431 | 0.015385 | 0.043478 | 0.066667
Slope at Drainpoints - Broad Based Dips

## Slide 11: Mass Wasting (LandTypes)
 | C1 | C2 | D1 | D2 | F1 | F5 | G1 | G2
Upper Elk |  | 31% | 19% | 15% |  |  |  | 
Wyoming | 7% | 3% | 63% | 12% |  | 0.4% |  | 
Fir Creek | 19.4% |  | 1.95% |  |  | 4.5% |  | 74 %
Lower Elk | 1.2% |  | 0.3% |  |  | 2.1% |  | 26.8%
Bearskin | 24.7% | 12.9% | 10.5% | 24.7% | 1 % |  |  | 1.0%
Cache | 17.3% | 19.6% | 47.1% |  |  |  | 0.2% | 2.6%
Upper Bear Valley | 19.0% | 49.9% | 0.7% | 20.0% |  |  |  | 2.7%
Percent of roads network
within “unstable” landtypes.
C1: Fluvial lands with moderate to high mass wasting potential

## Slide 12: Geomorphic Road Assessment and Inventory Package (GRAIP)
- process and tools for analyzing road erosion
- combines road inventory with GIS analysis
- predicts road sediment production & delivery, mass wasting risk from gullies and landslides, and road hydrologic connectivity
- overlays road path on Digital Elevation Model (DEM) and uses TauDEM for flow accumulation
Sediment production for each road segment:
E = B x L x S x R x V
(base rate, length, slope, surface, vegetation)

## Slide 13: GRAIP Sediment Accumulation
Percent SedDel / SedProd | 
 | %
Fir Creek | 20.4%
Upper Bear Valley | 12.6%
Bearskin | 11.2%
Wyoming | 8.1%
Cache | 7.5%
Lower Elk | 4.4%
Upper Elk | 2.0%

## Slide 14: GRAIP Sediment Delivery
Sediment Delivery (kg/yr) | 
 | sedDel
Upper Bear Valley | 388,658
Bearskin | 140,574
Cache | 94,441
Fir Creek | 58,874
Lower Elk | 48,336
Wyoming | 10,500
Upper Elk | 3,150
Percent SedDel / SedProd | 
 | %
Fir Creek | 20.4%
Upper Bear Valley | 12.6%
Bearskin | 11.2%
Wyoming | 8.1%
Cache | 7.5%
Lower Elk | 4.4%
Upper Elk | 2.0%

## Slide 15: Relative Comparison
HUC_6_NAME | 1. Density | 2. Stream Proximity | 3. Crossings / Stream Mile | Ave ranking | 123 Index | sedDel (kg/yr) | % Total sedDel
Upper Bear Valley | 1.86 | 34% | 0.60 | 2.67 | 38.72% | 388,658 | 52.2%
Bearskin | 1.50 | 54% | 0.55 | 2.67 | 44.86% | 140,574 | 18.9%
Lower Elk | 0.88 | 29% | 0.26 | 2.00 | 6.80% | 48,336 | 6.5%
Cache | 0.86 | 42% | 0.18 | 1.67 | 6.57% | 94,441 | 12.7%
Wyoming | 0.46 | 49% | 0.17 | 1.67 | 3.87% | 10,500 | 1.4%
Fir Creek | 0.27 | 78% | 0.09 | 1.67 | 1.94% | 58,874 | 7.9%
Upper Elk | 0.07 | 21% | 0.02 | 1.67 | 0.03% | 3,150 | 0.4%
TOTAL | 0.77 | 44% | 0.24 | 2.0 | 8.23% | 744,532 | 100%

## Slide 16: Conclusion Bear Valley Watershed Road Erosion
Upper Bear and Bearskin roads deliver most sediment to streams
Sediment Delivered (kg/yr) | 
 | sedDel
Upper Bear Valley | 388,658
Bearskin | 140,574
Cache | 94,441
Fir Creek | 58,874
Lower Elk | 48,336
Wyoming | 10,500
Upper Elk | 3,150

## Slide 17: Conclusion
Sediment Delivered (kg/yr) | 
 | sedDel
Upper Bear Valley | 388,658
Bearskin | 140,574
Cache | 94,441
Fir Creek | 58,874
Lower Elk | 48,336
Wyoming | 10,500
Upper Elk | 3,150
Image analysis can help prioritize erosion problems
Indicators confirm
GRAIP model predictions
(in a relative sense)

## Slide 18: Questions?

## Slide 20: Secondary Questions
  How and where do road-stream crossings influence local stream channels and water quality?
  How and where does the road system restrict the migration and movement of aquatic organisms?
  How and where does the road system affect shading, litterfall, and riparian plant communities?
  How and where does the road system contribute to fishing, poaching, or direct habitat loss for at-risk aquatic species?
  How and where does road system facilitate introduction on non-native species?