## Slide 1: Identifying spatial and temporal extent of critical condition for water wells in Salt lake valley
Ali Forghani
Utah State University
GIS in Water Resources Term Project
Nov 2011

## Slide 2
Water Resources:
- Surface water
- Groundwater
In this project:
Groundwater conditions in Salt lake valley (HUC8=16020204) have been studied
- Considering groundwater elevation
Introduction:

## Slide 3
Objectives:
1- Obtaining interpolated surface of groundwater elevation in the study area
2- Specifying the critical areas
3- Specifying the regions possibly affected by artificial recharge system
4-Obtaining interpolated surface of depth of unsaturated zone
5- specifying the regions with high pumpage cost

## Slide 4
Note:
1- lacking a complete data for extraction wells
2- lacking the monthly data for observation wells esp. after year 2000

## Slide 5
Needed data:
1- Digital Elevation model (DEM)
2- groundwater elevation data
- USGS:“water level below land surface” (Depth of groundwater)

## Slide 6
-Not existing stations in northwest of the region
-defining 4 new stations near surface waters (depth=0)

## Slide 7
Objective 1: interpolated groundwater elevation
2 procedures:
1- determining groundwater elevation in each observation well and then interpolating
2- interpolating depth of water table and then subtracting it from DEM
The results of procedure 2 was more reliable.

## Slide 9
Objective 2: Specifying the critical areas
Critical area: the area with decrease in water table more than critical value
Obtaining the map of groundwater elevation differences in desired time periods
Definitions:
Yearly critical value:1m
10 years period critical value:4m

## Slide 10
Critical area: (10 years period)
(Critical value:4m)
Red regions (3.8%)

## Slide 11
Critical area: (1 year period)
(Critical value:1m)
Red regions (14%)

## Slide 12
Objective 3:
The regions with highest increase (possibly affected by artificial recharge)
Dark green region

## Slide 13
Objective 4: interpolated surface of unsaturated depth

## Slide 14
Objective 5: Regions with high pumpage cost (in which depth of unsaturated zone is high)
Definition:
high depth: depth more than 30m

## Slide 15: Suggestion for further studies
Obtaining the complete data for extraction wells in the region
Using different interpolation methods and comparing results

## Slide 16: Thanks for your attention
Any Questions???