## Slide 1
To:
Dr. David Tarboton
Instructor
By:
Ali A. Salha
Nov. 29, 2011
Estimation of Crop Water Requirements in Gaza Strip, Palestine - GIS Based Application
Geographic Information System in Water Resources
CEE6440
Fall Semester 2011

## Slide 2: OBJECTIVES
To estimate the crop water requirement (CWR) in Gaza Strip, Palestine. Through integration FAO’s crop equations using GIS techniques.
Producing spatial map representation of final results of crops distribution and monthly/yearly crop water requirement in Gaza Strip, Palestine.

## Slide 3: STUDY AREA
Area: 141 square miles (≈365 KM2).
Population: 1,657,155 (July 2011 est.)
Semi-arid region – Water scarcity is a big issue!
Agricultural activities are one of the main economical aspects in Gaza Strip.
National Geographic location of GS (Courtesy of Wikipedia)

## Slide 4: INTRODUCTION
Irrigation practices in Gaza Strip are only based on farmer’s knowledge and experience.
FAO guidelines are barely used in Gaza Strip for most common cultivated crops (citrus, almonds, date palms, grapes) due to socio-economical issues.
Thus, it is an opportunity to understand the current water consumption in agricultural sector in Gaza Strip vs. FAO guidelines during this term project.

## Slide 5: DATA COLLECTED
Gaza Strip (shape file) (National Grids-Palestinian Grid 1923) (source: Ministry of Planning and International Cooperation and PWA).
Agricultural Land-use (crops cover shape file) (source: PWA).
20 years rainfall records for 8 meteorological stations covering Gaza Strip (only 2009 average monthly record was used) (source: Coastal Municipalities Water Utility).
Crop information such as growing season, crop height, and crop coefficient (source: FAO papers 24, 33, 56).

## Slide 6: EQUATIONS AND CALCULATIONS – Cont.
CWR (Crop water requirement) calculation using FAO equation (source: FAO paper 56)
Where,
ETo is the reference evapotranspiration (mm).
Kc is the crop coefficient values
Peff is the effective rainfall (mm)

## Slide 7: EQUATIONS AND CALCULATIONS – Cont.
Where, (source: meteorological data were obtained from CMWU)
ETo reference evapotranspiration [mm day-1],
Rn net radiation at the crop surface [MJ m-2 day-1],
G soil heat flux density [MJ m-2 day-1],
T mean daily air temperature at 2 m height [°C],
u2 wind speed at 2 m height [m s-1],
es saturation vapor pressure [kPa],
ea actual vapor pressure [kPa],
es - ea saturation vapor pressure deficit [kPa],
D slope vapor pressure curve [kPa °C-1],
γ psychometric constant [kPa °C-1].
ETo (Reference Evapotranspiration) calculation using Penman Monteith FAO equation (source: FAO paper 56)

## Slide 8: EQUATIONS AND CALCULATIONS – Cont.
Description | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Reference Evapotranspiration ETo (mm) | 1.99 | 2.3 | 3.28 | 4.3 | 4.15 | 4.84 | 5.2 | 5.05 | 4.49 | 3.2 | 2.06 | 2.1
Kc (Crop coefficient) | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Citrus | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.65 | 0.65 | 0.65 | 0.65 | 0.65
Fruit trees | 0.9 | 0.9 | 0.9 | 0.65 | 0.65 | 0.65 | 0.65 | 0.4 | 0.4 | 0.4 | 0.4 | 0.9
Vegetables1 | 1.15 | 1.15 | 0.95 |  |  |  |  |  | 0.6 | 1 | 1 | 0.75
Vegetables2 | 0.8 |  |  | 0.6 | 0.6 | 1.15 | 1.15 | 0.8 | 0.6 | 1.15 | 1.15 | 0.8
Field crops | 1.15 | 0.4 |  |  |  |  |  |  |  | 0.3 | 0.3 | 1.15
Crop Category FAO papers 56 and 33 | Crop Type
Citrus | Orange / lemon / grapefruit
Fruit trees | Apples / pears / peaches / apricots / almonds
Vegetables1 | Cucumber / squash / cabbage
Vegetables2 | Tomato / sweet peppers / egg plants / potato
Field crops | Wheat / barley

## Slide 9: EQUATIONS AND CALCULATIONS – Cont.
Peff (Effective Rainfall) calculation using US Department of Agriculture – Soil Conservation Service procedure (USDA-SCS) (source: T. A. Obreza and D. J. Pitts, 2002)
Where,
f = correction factor depends on average net application depth or soil moisture depletion before each irrigation (will be 1 in this term project)
P = the gross monthly rainfall (mm)
ETo = the monthly reference evapotranspiration (mm)

## Slide 10: METHODOLOGY
Using ArcCatalog create personal geodatabase. Adding data/tables and then exporting them to be layers within the assigned geodatabase file.
Unifying the coordinate systems to (National Grids-Palestinian Grid 1923) using define projection.
Joining the attribute file of Agricultural land-use with ETo and ETo*Kc data that were assigned for each crop.
CWR was computed for each month and then the Total CWR was the summation of all monthly CWRs.

## Slide 11: METHODOLOGY
ModelBuilder
Main tools used were conversion tool (feature class to raster) and Map Algebra tool (raster calculation).
49 procedures were built in the model.

## Slide 12: RESULTS

## Slide 13: RESULTS – Cont.

## Slide 14: RESULTS – Cont.
Chart: Yearly Crop water requirement in Gaza strip Total = 64.7 MCM
| Citrus | Fruit trees | Vegetables1 | Vegetables2 | Field crops
 | 11.23 | 2.7 | 3.59 | 2.25 | 44.92

## Slide 15: RESULTS – Cont.
Chart: Monthly Crop water requirements
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
MCM | 3.447 | 1.379 | 2.643 | 5.745 | 5.63 | 6.894 | 8.192 | 6.32 | 6.894 | 10.192 | 1.724 | 5.63

## Slide 16: DISCUSSION
The total crop water requirement for Gaza Strip is calculated as 64.7 MCM/year. If this figure is compared with the annual agricultural sector:
- 85 MCM (Palestinian Water Authority, Water Strategic Planning Study, 2000.)
- 83 MCM (Future Water Needs study in Palestine, MAS , 2009).
The total losses due to delivery system, partially traditional irrigation techniques, and over application by farmers is about 22-24 %.

## Slide 17: FURTHER WORK
This term project can be elaborated to be a management tool for planners and decision makers in drafting/design plans for improving farmers’ practices in agricultural sector.
It can be part of a regional water resources management project. As it could be linked with water resources availability in the region and water rights for different demand sectors.

## Slide 18: SOURCES
FAO - Food and Agriculture Organization of the United Nations. Rome, 1998
Paper title;
Crop evapotranspiration - Guidelines for computing crop water requirements - FAO Irrigation and drainage paper 56

## Slide 19
Nov. 29, 2011
Estimation of crop water requirements in Gaza Strip, Palestine - GIS Based Application
CEE 6440
THANK YOU