## Slide 1: underseepage analysis in levees using GIS
CEE 6440
Lourdes Polanco
November 27th, 2012

## Slide 2: Objectives
To present an informative map showing vulnerable leveed areas along the Natomas basin based on underseepage analysis
Show possible flooded depths of the area if the levee were to fail
Pilot analysis

## Slide 3: What are levees?
Levees are embankments designed to prevent the flooding of a river into an adjacent landward floodplain.
From mvm.usace.army.mil
What is
underseepage?
California, Arboga, after the 1997 flood
From stanford.edu
Seepage is the flow of water through soils.
3 of 19
Notes: Seepage is the flow of water through soils.
  The water may seep out gently
  The water can erode the soil forcing it to erupt on the landside as “sand boils”.

## Slide 4: Location of research
Levees

## Slide 5: Why is it important?
DESCRIPTION
Open Water
Developed, Open Space
Developed, Low Intensity
Developed, Medium Intensity
Developed, High Intensity
Barren Land (Rock/Sand/Clay)
Shrub/Scrub
Grassland/Herbaceous
Pasture/Hay
Cultivated Crops
Woody Wetlands
Emergent Herbaceous Wetlands

## Slide 6: Deterministic Factor of Safety
Most common method used by engineers to assess underseepage.
Generally, for levee underseepage a F.S. > 3.0 is acceptable.
usually between 0.8 and 1.0
ie calculated by finite element analysis, provided in Corps report
Computation
ic is the gradient needed to initiate erosion
      ie is the gradient calculated with FEM analysis
From earthsci.org
Notes: The critical gradient (ic) is generally taken to be a function of the saturated buoyant unit weight of the soil (γb) and the unit weight of the water,
The critical gradient (ic) is the gradient needed to initiate erosion in the soil and usually varies from about 0.80 to 1.0 (Mansur, Postol, and Salley, 2000), depending on the unit weight of the soil. The exit gradient (ie) is the gradient at the point of erosion calculated with Finite Element Analysis and it is a function of the subsurface geometry and the permeability of the subsurface soils.

## Slide 7: SSURGO Data
Sutter county
Sacramento county
7 of 19

## Slide 8: US Army Corps of Engineers Sacramento District data

## Slide 9: Data points
NAD_1983_HARN_StatePlane_California_II_FIPS_0402
Lambert_Conformal_Conic

## Slide 10: IDW Interpolation of gradients
100 yr – flood hydraulic gradients
200 yr – flood hydraulic gradients
Critical gradients

## Slide 11: F.S. raster calculation
100 yr – flood F.S.
200 yr – flood F.S.

## Slide 12: Extract by mask

## Slide 13: Vulnerable areas
100 yr – flood
200 yr – flood
Overlap

## Slide 14: Comparison
100 yr – flood
SPLINE
100 yr – flood
IDW
Overlap

## Slide 15: DEM
Mosaic to new Raster

## Slide 16: Flooded depths
< 4.0 m
< 4.5 m
< 5.0 m
< 5.5 m
< 6.0 m
< 4.0 m
< 4.5 m
< 5.0 m
< 5.5 m
< 6.0 m
< 4.0 m
< 4.5 m
< 5.0 m
< 5.5 m
< 6.0 m
< 4.0 m
< 4.5 m
< 5.0 m
< 5.5 m
< 6.0 m

## Slide 17: Limitations of analysis
Interpolation of gradients is not accurate but informative
Surface soils were used instead of stratigraphy soils
Conclusions
Design against underseepage feasible for 100yr-flood based on comparison
GIS is a great tool to make an informative map and compile data

## Slide 18: Future work
Use piezometric heads
Use soils beneath the levees
Divide levee system into levee reaches
Compute probability of initiation of erosion
Extent analysis to Pocket area and other surrounding levees

## Slide 19: THANK YOU! QUESTIONS?