## Slide 1: Snowfall Runoff Forecasting in San Juan County, UT
Dane Hurst
GIS in Water Resources
Utah State University
Fall 2014

## Slide 2: Project Objective
Develop a model to forecast total seasonal snowmelt runoff for two major reservoirs downstream of the Abajo Mountain range in San Juan County, UT

## Slide 3
www.wikipedia.com

## Slide 4: Project Geography
Watershed Name | Area (km2) | Area (mi2)
Recapture Creek | 143 | 55.1
South Creek | 26.8 | 10.4
Recapture Creek @ Gauge | 11.5 | 4.4
Indian Creek | 6.6 | 2.6

## Slide 5: Available Datasets
SNOTEL
  2 Sites
  Daily snow water equivalent (SWE)
USGS stream gauges
  2 sites
  Daily average flow rate
SNODAS
  Modeled daily SWE over continental United States
www.sjrnews.com

## Slide 6: End User Process
SNOTEL SWE Reading
Correlation to SNODAS SWE value at the site
Average accumulated SWE over watershed(s)
Correlation to stream flow
Predicted available runoff
Accounts for spatial variation of snowfall
Accounts for losses (infiltration, evaporation etc.)
Accounts for errors in modeled data

## Slide 7: Model Development Process
Define project
Define Goals
Gather Data
Stream flow
Process Data
Find seasonal cumulative snowfall using SNODAS
SNODAS
SNOTEL
Find daily SNODAS value at SNOTEL sites
Find total seasonal stream flow volume
Analyze Data
Correlate local SNOTEL SWE to local SNODAS SWE
Correlate SNODAS SWE volume to stream flow volume
Correlate local SNOTEL SWE to stream flow volume
Present Data
Simple Excel workbook to perform calculations
Consider constraints
Develop process plan

## Slide 8: Sample Model Development:
Description | Value
Maximum SNOTEL SWE | 328 mm
SNODAS SWE at Camp Jackson | 290 mm (113% of SNOTEL)
Average SWE in watershed | 211 mm (72.9% of Camp Jackson)
Area of watershed | 11.51 km2
Volume available in watershed | 2,748,000 m3
Total Spring runoff at gauge | 129,800 m3
Runoff ratio | 0.0472
2009 Camp Jackson and Recapture Creek (South side)

## Slide 9: Sample Model Use
Description | Value
Maximum SNOTEL SWE | 422 mm
Modeled volume available in watershed | (422 mm)(113%)(72.9%)(11.51 km2) =3,130,393 m3
Modeled runoff | (3,130,393 m3)(0.0472) =147,800 m3
Actual runoff | 158,400 m3
Error | -7.2%
2010 Camp Jackson and Recapture Creek (South side)
www.hikesandlakes.com

## Slide 10: Remaining Work
Calculate seasonal cumulative SWE
Establish correlations
Create Excel workbook to perform calculations
www.hikesandlakes.com
www.sjrnews.com

## Slide 11: Future Improvements
Build tool to automate process
  Data collection
  Processing/Analysis
More rigorous hydrologic model
ckmcdonald on panormio.com