## Slide 1: Analysis of Water Resources of Metropolitan Water District of Salt Lake and Sandy
Presented By: Dan Ethington E.I.T.

## Slide 2: Introduction
Established in 1935
Serves a population of over 300,000
Salt Lake Aqueduct completed 1951 to supplement water from LCC
  42 mile pipeline From Deer Creek to Salt Lake City

## Slide 3: Introduction
Little Cottonwood Water Treatment Plant
Point of the Mountain Water Treatment Plant
Design Capacity: 150 MGD
Design Capacity: 70 MGD

## Slide 5: Project Objectives
Determination of Districts water resources
Analysis of water/watersheds
Determination of water demands
Determination of water resource adequacy

## Slide 6: District Water Sources
Little Cottonwood Creek
Deer Creek Reservoir
  Jordanelle Reservoir
Little Dell Reservoir

## Slide 11: District Water/Watershed Analysis
Little Cottonwood Creek Watershed
  Landcover and Imperviousness Unchanged 2006 to 2011
  No water impairments
Little Dell Reservoir Watershed
  Landcover and Imperviousness Unchanged 2006 to 2011
  No water impairments

## Slide 12: District Water/Watershed Analysis
Deer Creek Watershed
Total Land Cover Change = 0.63%
Occurred from 2006 to 2011
22 mi^2 of agricultural land
18 mi^2 of developed space
41 Stream reaches have impaired water dating back to at least 1992
Impairments Include:
Mercury, High Ph, E. Coli/ Pathogens, Temperature
Note the location of these impaired waters

## Slide 13: Demand Forecasting
Utilization of State of Utah Governors Population forecast
Determine trend to forecast even farther
  Linear Regression
City | 2010 | 2020 | 2030 | 2040 | 2050 | 2060
SLC | 186,440 | 210,592 | 227,824 | 229,985 | 233,031 | 234,704
% growth | - | 12.954 | 8.183 | 0.948 | 1.324 | 0.718
Sandy | 87,461 | 97,826 | 102,107 | 104,993 | 106,471 | 105,929
% growth | - | 11.851 | 4.377 | 2.826 | 1.407 | -0.509
Total Pop. | 273,901 | 308,417 | 329,932 | 334,978 | 339,502 | 340,633
% growth |  | 12.602 | 6.976 | 1.530 | 1.350 | 0.333
Demand (ac-ft) | 61945 | 69751 | 74617 | 75758 | 76781 | 77037
Chart: 
| 2030 | 2040 | 2050 | 2060
 | 329931.7255 | 334978.4688 | 339501.668 | 340633.0159
 | Sandy City | Salt Lake City | Total
Avg. Demand per year (ac-ft) | 16432 | 45513 | 61945
Demand (ac-ft) /pers./yr | total demand/ total pop. | 0.226 | 

## Slide 14: Demand Analysis
Chart: Water Supply Analysis
| 2010 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070 | 2080 | 2090 | 2100 | 2110 | 2120 | 2130 | 2140 | 2150 | 2160 | 2170 | 2180 | 2190 | 2200
Demand Growth | 61945 | 69751.191 | 74616.8168 | 75758.18 | 76781.1393 | 77037.003 | 78118.8347 | 78947.1849 | 79775.5352 | 80603.8854 | 81432.2356 | 82260.5858 | 83088.936 | 83917.2862 | 84745.6364 | 85573.9866 | 86402.3369 | 87230.6871 | 88059.0373 | 88887.3875
Current Supply | 86564 | 86564 | 86564 | 86564 | 86564 | 86564 | 86564 | 86564 | 86564 | 86564 | 86564 | 86564 | 86564 | 86564 | 86564 | 86564 | 86564 | 86564 | 86564 | 86564
With > 1% growth every 10 yrs current water supply will be inadequate in 2170
 | Jordanelle Reservoir | Deer Creek Reservoir | Little Cottonwood Creek | Little Dell Reservoir | Total
Capacity (ac-ft) | 360500 | 152564 | - | 20500 | 533564
MWDSLS Supply per year (ac-ft) | 20000 | 41416 | 20318 | 4830 | 86564

## Slide 15: Questions