## Slide 1: Avalanche Risk
Terrain Susceptibility
Kyle Renner
GIS in Water Resources 2015

## Slide 2: Avalanche Definition and Facts
‘a rapid flow of snow down a sloping surface as a result of snowpack failure.’
Failure occurs when load (weight of snowpack) exceeds strength
Avalanches are expected in every mountain range, every winter season
Avalanches kill more than 150 people worldwide annually
Slab avalanches can reach speeds of 80 miles per hour within 5 seconds and are the most destructive form of avalanche.

## Slide 3: Major Avalanche Types
Loose
  Powder
Slab

## Slide 4: Avalanche Factors
Weather
  Temperature
  Recent Snowfall
  Wind
Snow Conditions
  Snowpack depth
Terrain
  Slope
  Slope Profile – Curvature
  Aspect
  Land Cover

## Slide 5: Current Risk Assessment Methods
North American Public Avalanche Danger Scale (US)
  Used primarily by recreationalists, must be updated by recreation managers

## Slide 6: Forecast Model, Limited Coverage

## Slide 7: A new perspective: Terrain Analysis
An analysis of terrain conditions that lead to an avalanche given appropriate weather and snow conditions.
Can be used to identify at risk locations by planners, developers, or managers.
  Example: a home owner wishes to insure a home, insurance company can cite the location of the house within an at risk area for an increase in insurance costs.
A model that incorporates Slope, Aspect, Curvature, and Land Cover.

## Slide 8: Slope, Aspect, Curvature, Land Cover
Shallow slopes require more weight to cause failure (<25°)
Steep slopes struggle to accumulate snow (>60°)
Aspect influences temperature, a colder snowpack = prone to failure
Northern Slopes receive less sunlight, maintain colder snowpack
Convex slopes create tension zones in the snowpack
Barren land coverage lacks friction capabilities
Dense land coverage provides anchor points to increase snowpack strength

## Slide 9: Model Inputs
Elevation Data: 3D Elevation Program (3DEP), USGS
  National Map, Elevation
  Available in various formats – 1/3 arc-second seamless DEM recommended
  Available at http://nationalmap.gov/elevation.html
Land Cover Data: National Land Cover Database (2011)
  Spatial Resolution of 30 meters
  16- class land cover classification based on Landsat satellite data.
Available at http://www.mrlc.gov/nlcd2011.php
Also available through ArcGIS Server: Landscape 5
Area of Interest: County, State, or any other usable polygon
*Data must be orthogonal in order to work correctly
Notes: Decision-tree classification of 2011 Landsat satellite data

## Slide 10: Tools
Elevational Data will be the input raster in several tools
  Slope Tool- the rate of maximum change in the z-value (elevation). Expressed as degrees ranging from 0 to 90.
  Aspect Tool- identifies the downslope direction of the maximum rate of change. (Slope Direction)
  Curvature Tool- curvature is the second derivative of the surface, or the slope of the slope. Optional output curvature types are profile curvature, the direction of the maximum slope, and the plan curvature is perpendicular to the direction of the maximum slope.

## Slide 11: Reclassifications
All four layers reclassified to a value of between 0 and 3.
A value of zero corresponds to a extremely unlikely chance of a slide occurring in the given conditions (example: open water land classification).
A value of three indicates an extremely likely chance of a slide occurring, such as in the case of a slope between thirty and forty-five degrees or over barren land.
Values of one or two will indicate low or moderate risk.

## Slide 12
Land Class | Value | Land Class | Value
Open Water | 0 | Dwarf Scrub (Alaska Only) | 2
Perennial Ice/Snow | 3 | Shrub/Scrub | 2
Developed, Open Space | 0 | Grassland/Herbaceous | 3
Developed, Low Intensity | 0 | Sedge/Herbaceous | 3
Developed, Medium Intensity | 0 | Lichens (Alaska Only) | 3
Developed, High Intensity | 0 | Moss (Alaska Only) | 3
Barren Land | 3 | Pasture/Hay | 2
Deciduous Forest | 1 | Cultivated Crops | 2
Evergreen Forest | 1 | Woody Wetlands | 1
Mixed Forest | 1 | Emergent Herbaceous Wetlands | 1
Legend and Description available at http://www.mrlc.gov/nlcd11_leg.php
Land Classification Reclassification Table

## Slide 13: Slope, Aspect, and Curvature Reclassification
Slope:
  Between 30-45 degrees – 3 (high risk)
  Below 25 degrees, Above 60 degrees – 1 (low risk)
Aspect:
  Northern – 3 (high risk)
  Eastern – 2 (moderate risk)
  Southern, Western – 1 (lower risk)
Curvature
  Convex – 3 (more likely)
  Concave – 1 (less likely)

## Slide 14
The following equation will then be utilized using Map Algebra:
Risk = Σ[ slope + aspect + curvature + land-cover ]
-or-
Risk = (0.4)(slope reclassification) + (0.15)(aspect reclassification) + (0.2)(curvature reclassification) + (0.25)(land cover reclassification)
An output raster displaying the ‘Avalanche Risk Scale’
  A value of 0 indicates no risk
  A value of 1 indicates low risk
  A value of 2 indicates moderate risk
  A value of 3 indicates extreme or high risk
Importance Coefficient

## Slide 15: Limitations and Assumptions
This model predicts only the terrains impact on avalanche risk. Appropriate weather and snow conditions are necessary for a slide.
This model’s coefficients are estimated using prior research to gauge importance of the contributors (variables).
This model has an arbitrary reclassification based upon prior knowledge and choice upon whether a certain condition would have no, low, moderate, or extreme risk of contributing to a slide
Notes: Spencer Logan, Forecaster, Colorado Avalanche Information Center- subjective rating and descriptors are the best way researchers have found to quantify avalanche risk. The observational data is not available to attempt to model risk in a statistically valid way.

## Slide 16: Case Study – Lake County, Colorado
Inputs-
  Lake County Boundary shapefile obtained from 2010 Census Data
  2011 National Land Cover Dataset
  1/3 Arc-Second DEM available from USGS, Lake County

## Slide 17: Process

## Slide 18: Results

## Slide 19: Further Work, Additional Research
Setting an appropriate threshold for the avalanche risk scale can produce an at risk area
  This area can be used as an input for other tools such as the D-Infinity Avalanche Runout tool
    http://hydrology.usu.edu/taudem/taudem5/help53/DInfinityAvalancheRunout.html
    Displays the area of the avalanche path
Upon the acquisition of appropriate data, a regression analysis could be ran to determine appropriate coefficients
Further research could be conducted to provide better reclassification guidelines
Better coding and understanding of computer language

## Slide 20: QUESTIONS?