## Slide 1: Automated Unimpaired Hydrologic Metric Scaling for California Streams
By Karl Christensen

## Slide 2: Introduction
Karl Christensen
Masters Student at Utah State University
Civil Engineering
Emphasis in Hydraulics and Hydrology

## Slide 3: Overview
Understanding the Project Components
Predicting Flow Regimes
Case Study
Testing the Scaling Methods
Review
Future Direction for Work

## Slide 4: Project Title Automated Unimpaired Hydrologic Metric Scaling for California Streams
Automated – Python based ArcGIS script
Unimpaired – Natural Stream-flow regimes
Hydrologic Metric Scaling – Method of scaling from known hydrographs to a daily flow regime
California Streams
Notes: I know it’s long!

## Slide 5: Unimpaired vs Impaired Flow
Unimpaired
  Natural flow regimes
Impairments
  Dams
  Irrigation
  Industrial/municipal consumption

## Slide 6: Impact of Flow Regimes
Connection between aquatic biodiversity and hydrology (Bunn and Arthington, 2002)
  Habitat
  Adaptation by species
  Longitudinal and Lateral connectivity
  Invasive species
Notes: flow is a major determinant of the habitat, a key driver of the aquatic composition
aquatic species have evolved life-history strategies in response to the natural flow regime
the natural pattern of the longitudinal and lateral connectivity in the river system is important for supporting populations of aquatic species
the invasion and success of non-native species is facilitated by alterations to streamflow.

## Slide 7: Predicting Flow Regimes
Why do we need to predict flow regimes?
  Data before impairment may not be available
  Conditions in the future may be subject to change
  Flow estimations may be an indicator of stream ‘health’
Notes: After a stream becomes impaired we might not have pre-impairment data to return the natural stream course
Changing conditions allow for prediction of future flows
Estimations of flow regimes can be used to identify healthy/unhealthy streams or determine if a stream is impaired or not

## Slide 8: Predicting Flow Regimes
How do we predict flow regimes?
Options considered in this project
  Three Traditional Methods
  Stream Classification Approach
Notes: Several Methods

## Slide 9: Predicting Flow Regimes
Traditional Methods
  Drainage-area ratio technique (DAR)
  Mean streamflow ratio
  Mean and standard deviation ratio
Notes: Benefit:
This is a very direct approach.
Disadvantage:
Does not account for factors other than streamflow or area.

## Slide 10: Predicting Flow Regimes
Stream Classification
  Creates regions of similar characteristics
  Has the potential to overcome limitations of traditional scaling methods
Notes: Benefit:
Handles variance in stream characteristics
Requires less inputs
Disadvantage
Over generalization may lead to inaccuracies
More effort to create

## Slide 11: Predicting Flow Regimes
  Regional Characteristics (Hersch and Maidment, 2007)
    Water quality
    Climatology
    Hydrology & Hydraulics
    Geomorphology & Physical processes
    Biology
(Hersch & Maidment, 2007)
Texas
Notes: Creating regional flow characteristics is common all over the world, including Texas!

## Slide 12: Predicting Flow Regimes
Regional Characteristics
  20 ‘Hydrologic Indexes’
(Lane et al, 2017)
8 Flow Classes
Notes: Flow regimes for California have to handle a very diverse range of geography
Point to hydrologic indices
Names of regions name by the primary source of flow for collective reaches
Lowest and Highest elevations in the contiguous united states!

## Slide 13: Predicting Flow Regimes
Notes: Compare the regions

## Slide 14: Flow Regime: Case Study
Unimpaired Daily Flow Regime for Merced River Happy Isles Bridge (Near Yosemite, CA)
Class 1 – Snowmelt Region
USGS Gauge 11264500
Notes: Example of an unimpaired flow regime.
What would it look like if a dam was place upstream, and the flow was forced to be constant throughout the year?
Notice the relatively low flows in the summer and fall and the peak of flow from spring runoff. This hydrograph represents a Class 1 stream flow. (More about that later)

## Slide 15: Flow Regime: Case Study
Unimpaired Daily Flow Regime for Merced River Happy Isles Bridge (Near Yosemite, CA)
USGS Gauge 11264500
Chart: Daily Flow for USGS Gauge 11264500
Notes: Example of an unimpaired flow regime.
What would it look like if a dam was place upstream, and the flow was forced to be constant throughout the year?
Notice the relatively low flows in the summer and fall and the peak of flow from spring runoff. This hydrograph represents a Class 1 stream flow. (More about that later)

## Slide 16: Flow Regime: Case Study
USGS Gauge 11264500
Chart: Daily Flow for USGS Gauge 11264500
Chart: Daily Flow for USGS Gauge 11268000
Initial Gauge
Class 1 - Snowmelt
Nearby Gauge
Class 2 – Low Volume
Snowmelt and Rain
Notes: Can you see how the traditional methods wouldn’t account for location of the peak?
Can you see the hump in the summer? That does not fit the shape of the stream flow hydrograph.

## Slide 17: Flow Regime: Case Study
USGS Gauge 11264500
Chart: Daily Flow for USGS Gauge 11264500
Chart: DRH for USGS Gauge 11264500
Initial Gauge
Class 1 - Snowmelt
DRH
Accounts for 20 years of flow
Notes: Compare Daily to DRH
See the slope. The peak appears to be slightly to the left of the actual data. This shift may be due to variance over 20 years.

## Slide 18: Flow Regime: Case Study
USGS Gauge 11264500
Chart: Daily Flow for USGS Gauge 11264500
Chart: DRH for USGS Gauge 11264500
Chart: DRH Class 1 Snowmelt Runoff
Notes: Class 1 average is definitely skewed left. Very smooth curve. Still maintains that gentle curve

## Slide 19: Testing the Scaling Methods
How can we compare the different methods of scaling and choose the best one?
Are some methods better for some classes than others?

## Slide 20: Testing the Scaling Methods
Three gauge sites are selected in ArcGIS that are the same Class and are relatively close geographically
Results will be 20 years of daily flow data
Reference Gauges
California

## Slide 21: Testing the Scaling Methods
10 Different Ratios
  DRH for entire Class x Annual Average Flow
  DRH for entire Class x Monthly Average Flow
  DRH for nearest site x Annual Average Flow
  DRH for nearest site x Monthly Average Flow
  DRH for three nearest sites x Annual Average Flow
  DRH for three nearest sites x Monthly Average Flow
  Direct Area Ratio x Nearest Daily Flow
  Monthly Average Ratio x Nearest Daily Flow
  Annual Average Ratio x Nearest Daily Flow
  Monthly Average/Stand. Dev. Ratio x Nearest Daily Flow
Classification
Traditional

## Slide 22: Testing the Scaling Methods
Scenario | Stream Class | USGS Ref Gage (List FID(s)) |  |  | Prediction Site | Begin WY | Successful Run | Run Time
 |  | Nearest | 2nd/3rd Nearest |  |  |  | Date and Time | Seconds
1 | 1 |  |  |  | 11264500 | 1969 | 12/4/17 5:43 PM | 4.49
2 | 1 |  |  |  | 11264500 | 1969 | 12/4/17 5:43 PM | 6.33
3 | 1 | 11266500 |  |  | 11264500 | 1969 | 12/4/17 5:43 PM | 4.44
4 | 1 | 11266500 |  |  | 11264500 | 1969 | 12/4/17 5:43 PM | 6.33
5 | 1 | 11266500 | 11226500 | 11275000 | 11264500 | 1969 | 12/4/17 5:43 PM | 4.42
6 | 1 | 11266500 | 11226500 | 11275000 | 11264500 | 1969 | 12/4/17 5:43 PM | 6.25
7 | 1 | 11266500 |  |  | 11264500 | 1969 | 12/4/17 5:44 PM | 64.23
8 | 1 | 11266500 |  |  | 11264500 | 1969 | 12/4/17 5:46 PM | 64.29
9 | 1 | 11266500 |  |  | 11264500 | 1969 | 12/4/17 5:47 PM | 67.09
10 | 1 | 11266500 |  |  | 11264500 | 1969 | 12/4/17 5:48 PM | 63.18
11 | 1 |  |  |  | 11264500 | 1969 | 12/4/17 5:49 PM | 63.94
Visual Basic in Excel was used to automate the testing
VBA Code Snippet

## Slide 23: Testing the Scaling Methods
Example Results for USGS Gauge 11264500 (1975 Water Year)
  Results show a great deal of variability
Chart: 
Notes: Accuracy of the traditional methods

## Slide 24: Testing the Scaling Methods
Example Results for USGS Gauge 11264500 (1975 Water Year)
  Can be compared to the actual results using excel’s correlation command ‘Correl()’
Chart: 
| Series 1 | Series 2 | Series 3 | Series 4 | Series 5 | Series 6 | Series 7 | Series 8 | Series 9 | Series 10 | Actual
 | -0.12005 | 0.4741 | -0.1009 | 0.36259 | -0.14243 | 0.16218 | 0.98494 | 0.98574 | 0.99054 | 0.99163 | 1

## Slide 25: Review
Importance of flow regimes in stream ecology
Traditional Ratios vs Regional Classification Methods
Testing methods produce daily hydrographs

## Slide 26: Direction for Work
Analyze several sites from each class
Compare accuracy of scaling methods
Select method(s) best suited for each region
Write ArcPy script to automate stream gauge estimation
Modify ArcPy script to estimate stream flows in areas without any gauge data

## Slide 27
Questions?