## Slide 1: What Causes Flooding along the Logan river
By Garrick Stephenson
Graduate Student in Hydraulics and Fluid Mechanics
CEE 6440

## Slide 2: overview
Background
Objective and purpose
Analysis of flood factors
Height above nearest drainage (hand) map
summary

## Slide 3: Background

## Slide 4: Introduction
Each spring the Logan river has the potential of flooding during spring runoff
Objectives and purpose
  Analyze the Logan river watershed to determine factors leading to flooding
    Precipitation (snow pack)
    Temperature
    discharge
  Compile height above nearest drainage (HAND) map for Logan canyon

## Slide 5: Years of study
Flooding criteria
  Full bank (1370 cfs)
  Flood stage (1500 cfs)
Flood years
  2011 (1710 cfs) , 2017 (1510 cfs)
Normal year
  2016 (797 cfs)

## Slide 6: Data Retrieval
Temperature Data
  Natural Resources Conservation Service
Snowpack Data
  National Oceanic and atmospheric administration
Flow data
  U.s. geological survey

## Slide 7: Results
Snowpack
  Larger snowpack leads to greater runoff
Chart: 2011 Average Snowpack vs. Runoff
Average Discharge | 98.4 | 114.6 | 112.3 | 109.9 | 101.8 | 133.7 | 302.3 | 769 | 1309 | 1047 | 405.5 | 248.2
Chart: 2017 Average Snowpack vs. Runoff
Average Discharge | 122.2104 | 131.7972 | 119.5666 | 118.5156 | 229.7541 | 405.0604 | 577.0035 | 945.9761 | 1103.7966 | 439.3041 | 232.7507 | 203.7844

## Slide 8: results
Temperature
  Larger temperature flux results in smaller runoff
Chart: 2017 Average Snowpack vs. Temperature
Chart: 2011 Average Snowpack vs. Temperature

## Slide 9: Height Above Nearest Drainage (HAND)
1/3 arc-sec dem from usgs
Cyber gis d8 flow accumulation for stream raster
Cyber gis d-infinity distance down for hand map

## Slide 10: Height Above Nearest Drainage (HAND)
Stage-discharge curve for years of study
Chart: Stage-Discharge Curve
| 191.53889102789614 | 633.28252261673333 | 1295.7773900118316 | 2232.6056056717234 | 4839.3090361946734 | 8397.3549814486687 | 35573.457762032282
 | 0.25 | 0.5 | 0.75 | 1 | 1.5 | 2 | 4
Stage h (ft) | 0.82 | 1.64 | 2.46 | 3.28 | 4.92 | 6.56 | 13.12
Stage h (m) | 0.25 | 0.50 | 0.75 | 1.00 | 1.50 | 2.00 | 4.00
As (m2) | 77400.00 | 92000.00 | 107100.00 | 118900.00 | 142600.00 | 167300.00 | 243500.00
Ab (m2) | 77500.60 | 92110.40 | 107229.00 | 119061.00 | 142861.00 | 167635.00 | 244961.00
V (m3) | 17802.00 | 39090.80 | 63831.60 | 92254.51 | 157844.00 | 234220.00 | 648197.00
L (m) | 2782.00 | 2782.00 | 2782.00 | 2782.00 | 2782.00 | 2782.00 | 2782.00
A = V/L (m2) | 6.40 | 14.05 | 22.94 | 33.16 | 56.74 | 84.19 | 233.00
P = Ab/L (m) | 27.86 | 33.11 | 38.54 | 42.80 | 51.35 | 60.26 | 88.05
R =A/P (m) | 0.23 | 0.42 | 0.60 | 0.77 | 1.10 | 1.40 | 2.65
So | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01
n | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05
Q (m3/s) | 5.43 | 17.94 | 36.71 | 63.25 | 137.09 | 237.89 | 1007.75
Q (cfs) | 191.54 | 633.28 | 1295.78 | 2232.61 | 4839.31 | 8397.35 | 35573.46
 |  | Q (cfs) | stage h (m) |  |  |  | 
 | 2017 | 1510 | 0.8 |  |  |  | 
 | 2011 | 1710 | 0.85 |  |  |  | 
 | 2016 | 797 | 0.6 |  |  |  | 

## Slide 11: Height Above Nearest Drainage (HAND)

## Slide 12: summary
Factors contributing to flooding
  Larger snowpack will lead to greater runoff.
  Consistent Warm temperatures will lead to greater runoff.
Limitations
  Availability of historical data (number of years used)
  Thiessen polygon method (number of Snotel sites)
  Other factors leading to flooding (debris, rain, etc.)
What’s next?
  increase years of study
  Forecast future flood events

## Slide 13: Questions?