## Slide 1: The Tank Hollow Fire and the Increase of Flood Potential for Spanish Fork
Jaxon White

## Slide 2: Introduction
Tank Hollow Fire 11,067 acres
Forest fires can cause a lower infiltration rate
Will the fire cause increase in downstream stage height?
Hypothesis: The fire will cause increase in risk of flooding

## Slide 3: Methods
Develop flood map using Height Above Nearest Drainage (HAND) method
Develop flow-rating curve for section of the Spanish Fork River
Determine the pre-fire and post-fire runoff
  SCS Curve Number method
  1-year, 10-year, and 25-year 2-hour storm events
Results
HAND
Flow-Rating Curve
Runoff

## Slide 4: Area of Interest

## Slide 5: Flood Map
HAND associates the stream bed elevation to a cell of interest

## Slide 6: Flow Rating Curve
Manning’s Equation
Chart: Flow Rating Curve
| 610.20137391423134 | 1191.2982372555496 | 2229.2576235542324 | 3532.9580742602743 | 32845.526009378933
 | 1.6404 | 3.2808 | 4.9213 | 6.5617 | 16.4042

## Slide 7: Runoff
SCS Curve Number method
Purdue Engineering. Curve Number. [Photograph]Retrieved from https://engineering.purdue.edu/mapserve/LTHIA7/documentation/scs.htm

## Slide 8: Curve Number
Based on the hydrologic soil group and land use
  Soil Group C
  Pre-fire curve number of 73
  Post-fire curve number of 88
    Higginson and Jarnecke method add 15

## Slide 9: Precipitation
NOAA point precipitation web tool

## Slide 10: Runoff Results

## Slide 11: USGS Streamflow Gages

## Slide 12: Flooded Addresses

## Slide 13: Questions?