## Slide 1: A Case Study of Dissolve Oxygen Sampling in Utah’s Bonneville Cutthroat Trout Range
Greg Goodrum
Cee 6440 – Dr. david tarboton/dr. david maidment
Assessing Spatial Representation of Large-Scale Environmental Datasets:

## Slide 2: Introduction
My research involves modeling aquatic habitat at state-wide scales
Based on limiting factors such as temperature, dissolved oxygen, and turbidity
Datasets designed with different objectives in mind
Does this present a problem in representing streams?
UDEQ & EPA
Dissolved Oxygen
Data Collection Sites
Photo: Utah Division of Wildlife Resources
Habitat Model

## Slide 3
How Does This Represent This?

## Slide 4: Research Questions
Can we use available
DO sensor data in modeling
streams in trout range?
How does the distribution of sample locations capture stream characteristics?
What conditions are we missing?
Where to add new monitoring locations
to improve representation?

## Slide 5: Study Area and Data Sources
Bonneville cutthroat trout (BCT) range
Dissolved oxygen (DO) sample locations
NHDPlus Stream Data

## Slide 6: How to Characterize Streams?
Why These?
Important Aspect of Stream Character
Near-complete coverage of watershed stream segments
Metrics Chosen:
Total Drainage Area (km²)
Velocity (fps)
Discharge (cfs)

## Slide 7
Import and process raw data
Snap sample locations to stream segments
Create population of sampled streams
Use Log10 function to generate normal-distribution classes for stream attributes
Compare sampled stream populations to full watershed
Methods

## Slide 8: Sample Distribution
Classes created by Log10 transformation
Trend to undersample attribute classes that contain most stream segments
How many attribute classes are completely unsampled?
Results
Chart: Distribution of Total Drainage Area Values
Chart: Distribution of Velocity Values
Chart: Distribution of Discharge Values

## Slide 9: Unsampled Classes
13 Stream Attribute Classes Unsampled
Total Drainage Area and Velocity unsampled
All Discharge classes sampled
How does this apply to study area?
Results
Chart: Percentage of Stream Segments with Sampled Total Drainage Area
| Total Drainage Area Class Unsampled | Total Drainage Area Class Sampled
 | 0.059335 | 0.94066
Chart: Percentage of Stream Segments with Sampled Velocity Class
| Velocity Class Unsampled | Velocity Class Sampled
 | 0.048741 | 0.95126
Chart: Percentage of Stream Segments with Sampled Discharge Class
| Discharge Class Unsampled | Discharge Class Sampled
 | 0 | 1
Unsampled Stream Attribute Classes | 
Stream Attribute | Class Definition
Total Drainage Area (km²) | 0.88495 - 1.10459317494942
 | 1.10459317494942 - 1.37875165566025
 | 2074.18679945422 - 2588.99706131816
 | 5034.80473477698 - 6284.43622632167
Velocity (fps) | <=0.3662
 | 0.3662 - 0.38939259508925
 | 0.38939259508925 - 0.414054265140453
 | 0.414054265140453 - 0.440277849766777
 | 0.440277849766777 - 0.468162270782314
 | 0.468162270782314 - 0.497812715084699
 | 0.6364206778077 - 0.676727547963407
 | 2.61303055145558 - 2.77852341933854
 | > 3.552159

## Slide 10: What are we missing?
9% of Stream Segments have one attribute that falls into an unsampled class
Widespread throughout range
Only 13 classes need additional samples
Results

## Slide 11: Where to Add Samples?
Segment within 1km of road
  Close to access point
Part of segment on Public Land
  Ease of identifying administrator and acquiring access
Analysis

## Slide 12: Where to Add Samples?
Result: 188 Possible Sites meet location criteria
Priority: Sites where we can add multiple unsampled attribute classes
Analysis

## Slide 13: Where to Add Samples?
Maximum of 2 sites can add multiple unsampled classes (i.e. 2 sites add 4 classes)
9 unsampled classes remain
11 total sites required to sample in all stream attribute classes
Analysis

## Slide 14: Conclusions
  DO sensors currently capture 91% of stream segments
  Currently missing 13 classes of velocity and total drainage area
  11 sites to represent 100% of stream segments
  Continued Work
    Optimize site selection from possible locations

## Slide 15: Questions?