## Slide 1: IS hand an effective way to model dam failures?
Tyler Withers

## Slide 2: Teton dam
Located near Rexburg, Idaho
Total Height: 305 feet
Storage capacity: 200,000 Acre-feet

## Slide 3: Teton Dam Failure
Peak discharge: 2,300,000 cfs

## Slide 4: Hand Analysis
Teton Dam
 | Area | % | Flow
North | 18423.14 | 0.37 | 849758.1071
South | 31441.9 | 0.63 | 1450241.893
 | 49865.04 |  | 

## Slide 5: Hand Analysis

## Slide 6: Hand using DEM derived catchments
Teton Dam

## Slide 7: Hand using DEM derived catchments

## Slide 8: Hand using DEM derived catchments

## Slide 9: Hand using DEM derived catchments
Stage h (m) | 5 | 10 | 10.9 | 12 | 15
stage (ft) | 16.40 | 32.81 | 35.76 | 39.37 | 49.21
cell size (m^2) | 100 | 100 | 100 | 100 | 100
flooding cell num | 263621 | 374113 | 388076 | 400301 | 444522
sb | 1.000111 | 1.000127 | 1.000128648 | 1.00013183 | 1.000136663
As (m2 ) | 26362100 | 37411300 | 38807600 | 40030100 | 44452200
Ab (m2 ) | 26365023 | 37416064 | 38812592.54 | 40035377.3 | 44458274.98
Inundation depth (m) | 2.672986 | 6.306695 | 6.962580926 | 7.83265748 | 9.910620289
Depth (ft) | 8.77 | 20.69 | 22.84 | 25.70 | 32.52
V (m3) | 70465512 | 2.36E+08 | 270201055.6 | 313542062 | 440548875.2
L (m) | 18586.41 | 18586.41 | 18586.4084 | 18586.4084 | 18586.4084
z1 (m) | 1488.52 | 1488.52 | 1488.52 | 1488.52 | 1488.52
z2 (m) | 1468.7 | 1468.7 | 1468.7 | 1468.7 | 1468.7
A = V/L (m2 ) | 3791.2 | 12694.3 | 14537.6 | 16869.4 | 23702.7
P=Ab/L (m) | 1418.51 | 2013.09 | 2088.22 | 2154.01 | 2391.98
R=A/P (m) | 2.673 | 6.306 | 6.962 | 7.832 | 9.909
S | 0.001066 | 0.001066 | 0.001066371 | 0.00106637 | 0.001066371
n | 0.05 | 0.05 | 0.05 | 0.05 | 0.05
𝑄 = 1 /𝑛*𝐴𝑅^2/3*𝑆o^1/2 (m3 /s) | 4768.7 | 28298.1 | 34616.7 | 43449.6 | 71418.4
Q (ft3 /s) = Q (m3 /s) x 35.3 | 168334.1 | 998923.8 | 1221968.3 | 1533770.5 | 2521071.0

## Slide 10: Comparing results with Actual Flood Event
Teton Dam flood of June 1976, Pingree quadrangle, Idaho
Hydrologic Atlas 581
By: Larry L. Hubbard and John H. Bartells

## Slide 11: Comparing results with Actual Flood Event
Teton Dam flood of June 1976, Pingree quadrangle, Idaho
Hydrologic Atlas 581
By: Larry L. Hubbard and John H. Bartells

## Slide 12: conclusions
It worked well for the regions where the slopes surrounding the river are steep.
In flatter areas like in Rexburg.
Other programs in existence would be more effective.

## Slide 13: Thank you!