GIS in Water Resources	Homework #2

1.  (a) Given the following grid of elevations, identify any cells that are pits (sinks) in the grid by drawing a circle around the elevation in that cell.  Label the pit cells with the elevation they would have once the pits are filled.  Focus only on the ungrayed center cells.  The grayed edge cells can by definition not be pits because the elevations off the area shown are not known.

Grid cell size 100m

| 57 | 55 | 47 | 48 | 48 | 50 | 53 |
| --- | --- | --- | --- | --- | --- | --- |
| 53 | 67 | 56 A | 49 | 52 | 54 | 42 |
| 53 | 52 | 45 | 36 | 37 | 43 | 38 |
| 51 | 58 | 40 | 42 | 40 | 39 | 38 |
| 55 | 39 | 38 | 38 | 36 | 38 | 38 |

(b).  Calculate the slope at grid cell labeled A using

(i)  The standard slope function

(ii)  The 8 direction pour point model

(iii)  The D(

In these calculations use the pit filled elevation values.

(c).  Determine the flow direction grid using the 8-direction pour point method (D8) and pit filled elevations (from part a).   Indicate the flow direction by using an arrow in each cell on the grid below.  Again do this only for the ungreyed center cells as the flow directions for edge cells can not be determined.

Flow direction grid.  Indicate values with arrows.

(d).  Determine the flow accumulation grid corresponding to the D8 flow directions.  Label each cell with the number of upstream cells draining into it (ESRI convention), again only for the ungreyed center cells.

Flow accumulation grid, fill in values

(e).  If the annual runoff (R) is given by the function R=0.51P-336, determine the annual runoff grid (mm/yr) given the annual rainfall grid below.

| Annual Rainfall (mm/yr) 900 980 1240 1260 1280 1290 1300 950 970 960 980 1050 1100 1180 940 945 950 958 985 1040 1100 860 890 920 940 970 990 1040 830 870 880 900 950 1000 1060 | Annual Runoff grid. Fill in values B |
| --- | --- |

f).  If these are 100 m cells calculate the mean annual streamflow draining out of the outlet cell marked B in m3/yr.

2.  Verify the calculations in (1) using ArcGIS Terrain Preprocessing either from ArcHydro Tools or TauDEM.  You may create the necessary grids in ArcGIS by saving the following to text files and using the ASCII to Raster tool in ArcToolbox.

| Elevations ncols 7 nrows 5 xllcorner 0 yllcorner 0 cellsize 100 NODATA_value -9999 57 55 47 48 48 50 53 53 67 56 49 52 54 42 53 52 45 36 37 43 38 51 58 40 42 40 39 38 55 39 38 38 36 38 38 | Annual Rainfall ncols 7 nrows 5 xllcorner 0 yllcorner 0 cellsize 100 NODATA_value -9999 900 980 1240 1260 1280 1290 1300 950 970 960 980 1050 1100 1180 940 945 950 958 985 1040 1100 860 890 920 940 970 990 1040 830 870 880 900 950 1000 1060 |
| --- | --- |

In Exercise 3 you will learn how to use ArcHydro.  The steps that you need to follow are:

- Fill Sinks

- Spatial Analyst(Surface Analysis(Slope

- Flow Direction

- Flow Accumulation

- Raster Calculator to evaluate runoff

- Weighted Flow Accumulation

In TauDEM use:

- BasicGrid Analysis(D8 Flow Directions (outputs D8 slope)

- BasicGrid Analysis(D( Flow Directions (outputs D( slope)

TauDEM is available from www.engineering.usu.edu/dtarb/taudem.