GIS in Water Resources	Homework #3 Solution

1.  [Past test question] The grids below depict initial snow depth and average temperature over a day for an area.

| (a) Initial snow depth (cm) | (b) Temperature (oC) |
| --- | --- |

One way to calculate decrease in snow depth due to melt is to use a temperature index model that uses the formula

Here Dold and Dnew give the snow depth at the beginning and end of a time step, T gives the temperature and m is a melt factor.  Assume melt factor m = 0.5 cm/OC/day.

(i) Interpolate from grid (b) a temperature for each of the nine 100 x 100m grid cells in grid (c) below.

| (c) Temperature (oC) | Briefly describe how you did the interpolation. Interpolated values are shown. They were estimated by averaging over the the fraction of the larger 150 m grid cells that overlap with the 100 m grid cells. |
| --- | --- |

(ii) Calculate the new snow depth for each cell in grid (d) using raster calculations that apply the above formula.

(d) Final snow depth (cm)

2.  Verification using ArcGIS.

The values are not the same at all locations due to ArcGIS using nearest neighbor interpolation by default in raster calculation, rather than a smoother averaging.  To reproduce the exact result above you need to use the procedure presented in Session 10 implemented by the hmwk3.tbx model builder tools.

# Text boxes

4

5

6

5

4

3

4

3

2

39

42.5

41

40.5

45

40.53

52

47.5

38

These values were obtained using the formula Dnew=Dold-m.T