## Slide 1: Flood Predictions in Smithfield and Birch Creek Canyons resulting from 100 year Precipitation events in Cache County, Utah.
GIS in Water Resources Presentation
By: Zac Sharp

## Slide 2: Project Outline
Project Description
Objective
Base Map Construction
Catchment Attributes
Rain Fall Data
Rational Flood Prediction
HEC HMS Flood Prediction
Results

## Slide 3: Project Description
Flood in 1983
Channel construction
New city offices
Catchment description
Two flood models

## Slide 4: Objective
The objective of this study is to determine, with reasonable certainty, the flow in summit creek through the city of Smithfield during design precipitation events.

## Slide 5: Base Map Construction
Sub basin information from NHDplus.
DEM from the USGS seamless server.
Soil attributes from the Utah GIS portal.
All flood model parameters come from the base map.

## Slide 6: Catchment Attributes
Basin (#) | Area (sq. miles) | Soil/Curve No. (#) | L (mi) | Lc (mi) | S (ft/mile) | Lag (hrs)
1 | 1.69 | B/70 | 2.08 | 1.01 | 1173.7 | 0.72
2 | 0.56 | B/70 | 0.92 | 0.74 | 2024.8 | 0.45
3 | 0.87 | B/70 | 1.29 | 0.81 | 1456.3 | 0.55
4 | .052 | B/70 | .21 | .15 | 946.5 | 0.32
5 | 2.76 | B/70 | 1.90 | 1.17 | 348.5 | 0.89
6 | 1.91 | B/70 | 2.42 | 1.65 | 1261.9 | 0.87
7 | 2.01 | B/70 | 1.78 | 1.30 | 1295.6 | 0.73
8 | 8.21 | B/70 | 6.12 | 4.12 | 257.5 | 2.09
9 | 5.03 | B/70 | 5.29 | 3.78 | 437.1 | 1.77

## Slide 7: Rain Fall Data

## Slide 8: Rain Fall Data
Chart: Time Ratio
| 0 | 4.1666666666666685E-2 | 8.3333333333333412E-2 | 0.16666666666666671 | 0.25 | 0.33333333333333331 | 0.37500000000000022 | 0.39583333333333331 | 0.41666666666666696 | 0.45833333333333326 | 0.5833333333333337 | 0.75000000000000044 | 0.8333333333333337 | 0.91666666666666652 | 0.9583333333333337 | 1
Representative Distribution | 0 | 0.0094 | 0.0219 | 0.05 | 0.0875 | 0.15 | 0.1969 | 0.5031 | 0.6344 | 0.7125 | 0.8063 | 0.9125 | 0.95 | 0.9781 | 0.9906 | 1
Linear Distribution | 0 | 1

## Slide 9: Rational Flood Prediction
Q = C*i*A.
C is 0.17.
1 and 24 hour
storms.

## Slide 10: HEC HMS
Rain fall distributions for each catchment.
SCS curve number method to compute runoff hydrographs.
Muskingham method to route hydrographs through main channels

## Slide 11: Results
Rational Method
HEC HMS
1 hr max flow = 715 cfs
24 hr max flow = 5580 cfs
1 hr linear max = 715 cfs
24 hr linear max = 610 cfs
1 hr max flow = 479 cfs
24 hr max flow = 5813 cfs
1 hr linear max = 483 cfs
24 hr linear max = 2372 cfs

## Slide 12: Results
Culvert Master analysis shows max flow is 383 before flooding will occur.
Conclusion: Put the building somewhere else.