## Slide 1: Visualizing Raster Data in 3D using Matlab
Project for GIS in Water Resources
Fall 2008
Joshua Roundy

## Slide 2: Outline
Matlab Mapping Toolbox
Data Sources
Creation of Matlab Tool Kit (DRI)
Precipitation Analysis Using DRI Tool kit

## Slide 3: Why Matlab?
Great 3D Plotting Capabilities
Ability to view Raster data along with Elevation data
Access large datasets with multiple files
Thousands of built in functions for analysis
Link Complex models written in FORTRAN or C

## Slide 4: Matlab GIS Data Structure
Vector Data
  Map Structure
  shaperead (Matlab Function)
    Reads in shapefiles
  shapewrite (Matlab Function)
    Writes shapefiles from Map Structure
Raster Data
  Reference Vector
    Number of Cells per Degree
    Latitude and Longitude of Top Left Corner
  Matrix of Data
    Top of Matrix is bottom of Map

## Slide 5: Data Sources
Digital Elevation Model (DEM)
  Data Format
    DEM Format
  Projection
    (WGS84) & (NGVD 29)
  1-degree quadrangles (3 arc second grid ~90 meters)
  Download from Web at
    http://edc2.usgs.gov/geodata/index.php
NEXRAD Radar Data
  Data Format
    XMRG Binary Files
  Projection
    HRAP
    Polar Stereographic Projection
    Spherical Datum
  6 hour Precipitation (1996-97)

## Slide 6: Create Matlab Tool (DRI)
DEM (Easy)
  usgsdems (Matlab)
    List required DEM files for given map limits
  usgsdem (Matlab)
    Reads DEM files into GEO-Referenced Grid
  Created routine to piece together different grids
NEXRAD (Hard)
  Could not read binary had to convert to ASCII
  Create Lat-Lon grid and resample from Radar Data at 2 KM resolution
  Create function to Convert Lat-Lon to HRAP Coordinates

## Slide 7: Precipitation Analysis
Animas River Basin (Durango, CO)
  Area of ~ 3,555 KM2
  Animas River
    Average Annual Discharge ~890 CFS
  See what kind of relationship exists between precipitation and elevation

## Slide 8: Precipitation Analysis
January 1997

## Slide 9: Precipitation Analysis
Total 6 hour periods with precipitation
Average Value of Precipitation
January 1997

## Slide 10: Precipitation Analysis
January 1997

## Slide 11: Conclusion
Precipitation increases with elevation
  Should consider this for hydrologic modeling
Uncertainty
  Accuracy of Radar Data
  Compare to Rain Gages
Remaining Tasks
  Clean up and comment code
  Write a readme file detailing how to use with other raster data sets

## Slide 12: Sources & Questions
Sources
  Matlab Mapping Toolbox Documentation available on line at http://www.mathworks.com
  Reed, S.M., and D.R. Maidment, "Coordinate Transformations for Using NEXRAD Data in GIS-based Hydrologic Modeling," Journal of Hydrologic Engineering, 4, 2, 174-182, April 1999