## Slide 1: Precipitation and Runoff Generation
CEE-6440
GIS in Water Resources
Bereket Tesfatsoin

## Slide 2: Outline:
Objective and Area of Study
Data Collection
Methodology
Reconstruction of unavailable data
Graphical display of relationship between discharge and precipitation
Conclusion

## Slide 3: Precipitation and Runoff
Objective:
Explore the relationship between the average monthly precipitation over Chalk Creek Watershed and the discharge at its out let.
Area of Study:
Chalk Creek Watershed, located within Weber Basin

## Slide 5: The Chalk Creek Watershed
There are two obvious reasons for the choice of Chalk Cree Watershed:
  It has precipitation stations
  It has a gaging station placed at its outlet.
Chalk Creek:

## Slide 6: Source of Data:
Watershed boundries and flowlines:
The Great Basin hydrologic region is further divided into production units: 16 a and b. Weber Basin lies within the Great Basin(Hydrologic Region 16), unit b.
NHDPLus Data:

## Slide 7: Source of Data (Cont’d)
Monthly Precipitation and SWEQ:
  SITENUMBER392 (from 1979-present)
  SITENUMBER393(from 1979-present)
NRCS website:

## Slide 8: Sourc of Data (cont’d)
Monthly Discharge:
  USGS101307: located inside the Chalk Creek Watershed (1964-1974)
  USGS10131000: located downstream of Chalk Creek Watershed (1927-present)
USGS website:

## Slide 9: Methodology:
Reconstruct the data at USGS10130700 based on available data
Convert Precipitation on the Watershed into and Equivalent Flow.
  For the purpose of this project Equivalent Flow is volume of accumulated water divided by the time period that the water accumulates.
Display and Explore the relationship between reconstructed discharge at USGS10130700 and Equivalent Flow at the Watershed.

## Slide 10: Reconstructing Data
Two ways were considered:
  Based on the dischareg at a downstream gage and area of Chalk Creek Watershed.
  Based on the ten year data, constructing a linear relationship between the flow at the two stations.
  The later produces better results.

## Slide 11: Reconstructing Data:
Flow relationship at two discharge gaging stations:
Chart: East Fork Chalk Creek (USGS10130700)

## Slide 12: Equivalent Flow:
Year | Month | Days | Precip, in |  | Avg Precip | Volume(Acre-Feet) | Equivalent Flow(cfs) | Ln(Equivalent Flow) | USGS10131000 (cfs) | USGS10130700 (cfs)
 |  |  | SITE_392 | SITE_393 |  |  |  |  |  | 
1979 | 1 | 31 | 10.9 | 7.4 | 9.15 | 16579.8 | 269.6 | 5.6 | 19.3 | 7.6
1979 | 2 | 29 | 14.9 | 9.9 | 12.4 | 22468.8 | 365.4 | 5.9 | 20.3 | 8.0
1979 | 3 | 31 | 18.2 | 11.9 | 15.05 | 27270.6 | 443.5 | 6.1 | 29.7 | 11.7
1979 | 4 | 30 | 21.9 | 15.3 | 18.6 | 33703.2 | 548.1 | 6.3 | 59.7 | 23.6
1979 | 5 | 31 | 24.2 | 17.1 | 20.65 | 37417.8 | 608.5 | 6.4 | 126.2 | 49.9
1979 | 6 | 30 | 25.4 | 17.6 | 21.5 | 38958 | 633.6 | 6.5 | 48.6 | 19.2
1979 | 7 | 31 | 26.5 | 17.8 | 22.15 | 40135.8 | 652.7 | 6.5 | 13.5 | 5.3
1979 | 8 | 31 | 28.7 | 19.4 | 24.05 | 43578.6 | 708.7 | 6.6 | 27.1 | 10.7
1979 | 9 | 30 | 30.4 | 20.1 | 25.25 | 45753 | 744.1 | 6.6 | 9.5 | 3.8
1979 | 10 | 31 | 0 | 0 | 0 | 0 | 0.0 | 0.0 | 10.7 | 4.2
1979 | 11 | 30 | 1.6 | 1.4 | 1.5 | 2718 | 44.2 | 3.8 | 15.2 | 6.0
1979 | 12 | 31 | 6.1 | 4.2 | 5.15 | 9331.8 | 151.8 | 5.0 | 12.9 | 5.1

## Slide 13: Discharge and Equivalent Flow
Discharge as a function of Equivalent flow
Chart: Equivalent Flow, cfs

## Slide 14: Discharge and Equivalent Flow
Discharge as a function of Ln(Equivalent Flow):
Chart: Ln(Equivalent Flow)

## Slide 15: Time series of Equivalent Flow and Discharge:
Chart: Months(1979-2009)

## Slide 16: Time series of Equivalent Flow and Discharge (cont’d):
Chart: Months (1979-1980)

## Slide 17: Observations and Conclusions:
There is a pattern.
There is a positive relationship.
The observed pattern may be characterized:
  Mathematically: There seems some exponential relationship exists, but based on the R2 values, this is less persuasive.
  Descriptively: As Equivalent flow increases, Discharge also increases. But there is a dramatic increase in Discharge after a certain threshold value of Equivalent Flow.

## Slide 18: Observations and Conclusions(cont’d):
The time series show a time lag of about 4 months between pick monthly discharge and pick monthly precipitation.

## Slide 19: Questions?
Thank you!!