## Slide 1: Using GIS to show the temporal –spatial variation of Phosphorus in Wellsville City Sewage Lagoons as simulated by a water quality model By Maureen Kesaano (GIS in Water resources: CEE 6440)

## Slide 2: OUTLINE
BACKGROUND AND JUSTIFICATION
OBJECTIVES
METHODOLOGY
RESULTS AND DISCUSION
CHALLENGES FACED
RECOMMENDATIONS

## Slide 3
KEY POINTS OF TERM PROJECT
Process model
GIS display
Excel

## Slide 4: BACKGROUND OF STUDY
PROBLEM: Deteriorating WQ of LBR due to increased nutrient loading (TP) from Wellsville City Sewage lagoons (LBR TMDL).
STEPS TAKEN SO FAR: City contracted J.U.B engineers to assess the situation and come up with alternatives (2007)
2010: No action alternative thus the discharge limits’ violations is still on going

## Slide 5: JUSTIFICATION OF STUDY
2007: State issued a UPDES permit to Wellsville City Lagoons limiting the total P discharges to 72 kg of TP /season (warm season, June – September) and 360 kg of TP/season (cool season, October – May)
Discharge is determined by the facility operators, therefore it is important for them to know which cell has the least P and when this occurs so that they can maximum discharge without violating the limits

## Slide 6
STUDY OBJECTIVE
To determine and visually display the amount and distribution of phosphorus within the Lagoons according to season

## Slide 7: METHODOLOGY
ASSUMPTIONS
Each cell was CSTR with constant volume
No non point P sources and recycle
P removal by discharge, ppt & attachment to sediment
1st order settling rate & settling velocity of 10 m/yr (Chapra, 2007)
Process model

## Slide 8: METHODOLOGY
Numerical method:
Created a cell_ID field as an identifier and date field for the temporal aspect of the data
TP Units: kg P/season
Model output in excel

## Slide 9: DATA USED in arcGis
Bear River watershed
NHDPlus data
Created a layer from already existing shape file
Edited cell shapes using editor tool
Analysis tool to extract & clip the LBR flow line

## Slide 10: DATA USED in ArcGIS
PROCEDURE
Tables joined using a query
Connected the tables using identifier Cell_ID
NOTE: Join/relates command wouldn’t work because of the one-many relationship
Shape file table
Xls. Imported table

## Slide 11: VISUALIZATION USING TRACKING ANALYST TOOL
Enable tool using customize extensions
Make sure all data is in the same GDB
Query table was exported as a layer in GDB
Add temporal data

## Slide 12: VISUALIZATION USING TIMESLIDER
Export query table into GDB as table
Enable time from the properties layer
Specify the time extent, change symbology and start timer

## Slide 13: RESULTS AND DISCUSSION
  DEMO in CLASS (tracking analyst)

## Slide 14: RESULTS AND DISCUSSION
  DEMO in CLASS (time slider)

## Slide 15: Challenges FACED
Sparse data for P
Learning the tracking analyst tool
One – many relationship table join

## Slide 16: conclusions and recommendations
GIS tools can be used to enhance visualization of data from process models
Tracking analyst tools recommended for temporal data from scientific research or real time data

## Slide 17: ACKNOWLEGDEMENTS
Instructors :Dr. Davis Tarboton, Dr. David Maidment, Dr. Ayse Irmark
Peer reviewers: Andrew Barney and Andrew Ritchey

## Slide 18: Thanks